IEEE P802.11
Wireless LANs

| TGk D8.0 SB Resolution for Admission Capacity |
| --- |
| Date: 2007-JUL-16 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Joe Kwak | InterDigital Communications | 482 Degas Bolingbrook, IL 60440 | 630-739-4159 | Joekwak @sbcglobal.net |

P54L31:  Modify paragraph in 7.3.2.43 as shown:

The Available Admission Capacity field is 2 octets long and contains an unsigned integer that specifies the  amount of medium time available using explicit admission control for the corresponding UP or AC traffic, in units of 32 microsecond periods per 1 second. See 11.10.9 for further details.

Insert new clause as shown:

### 11.10.9 BSS Available Admission Capacity

BSS Available Admission Capacity provides a means for an AP to advertise current admission policy used for explicit admission control of any UP or AC category.  This information may assist STAs in making BSS transition decisions.

A STA shall use the formula in K.2.2 to calculate medium time for TSPECs and for Available Admission Capacity values transmitted in the BSS Load and BSS Available Admission Capacity elements. Available Admission Capacity values are dynamic in a BSS. An AP shall update and recalculate Available Admission Capacity values as needed.  An AP shall only transmit current Available Admission Capacity values.  If an AP transmits the BSS Load element, the values for any transmitted BSS Available Admission Capacity values shall be less than or equal to the current BSS Load value.

An Available Admission Capacity value of 0 transmitted in the BSS Load element indicates that no explicit admissions will be granted by the AP.  An Available Admission Capacity value of 0 transmitted in the BSS Available Admission Capacity element indicates that no explicit admissions will be granted by the AP for that UP or AC category.  A STA shall not request admission for any TSPEC which requires more medium time than is currently advertised in the available admission capacity for the requested UP or AC of that TSPEC.  An AP which receives a TSPEC admission request for medium time which exceeds the current available admission capacity for the requested UP or AC category shall not admit the requested TSPEC. .  An AP which receives a TSPEC admission request for medium time which is less than the current available admission capacity for the requested UP or AC category shall admit the requested TSPEC and shall recalculate the available admission capacities according to local admission policy.

# Text boxes

Abstract

This document presents the proposed changed text needed to satisfy Sponsor Ballot Resolution CID#246 assigned to Joe Kwak. The included text is based on D8.0.  WORD track changes is used to show draft changes needed to resolve the above listed comments.