IEEE P802.11
Wireless LANs

| 802.11.2/D1.0 LB 101 Proposed Comment Resolution for Annex D Theoretical Throughput Limits |
| --- |
| Date: 2007-09-18 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Marc Emmelmann | Technical University Berlin | Einsteinufer 25 10587 Berlin, Germany | +49-30-314-24580 | emmelmann@ieee.org |
| Larry Green | Ixia | 402 E. Gutierrez Street Santa Barbara, CA 93101 | +1-818-444-2901 | lgreen@ixiacom.com |

# Revision History

| Revision | Changes |
| --- | --- |
| R0 | Original contribution as discussed during the TGT telephone conference calls on August 30 and September 7, 2007. |
| R1 | Included revision history Removed proposed resolution for those comments, TGT could not agree on during the telephone conference calls, i.e.: CIDs 987 and 467 (proposed resolution now in 11-07/2504) CID 240 Use the term “average collision free backoff” instead of “best case backoff” as agreed on during the September 7 telephone conference (this relates to CIDs 1389, 1390, 1391 and the same comments made to the subsequent sections of the draft). Removed proposed resultions for the following CIDs relating to tables 29 – 32 as they are resoved by the editor: CID 1600, 1601, 227, 1602, and 1603 |

Editorial Note: Sections (1) and (2) were removed in revision 1 of this document.

# (3) Section D.2.12 – D3.2 Comments

| 1356 | Malarkey, Alastair | N | D.2 | 153,36 | T | The term FR is not defined | Define the term FR as Frame Rate |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1357 | Malarkey, Alastair | N | D.2.12 | 154,07 | T | In the subsequent clauses the term Backoff slot is used. The term Slot time is not used. | Change to Backoff Slot |
| 237 | Sharma, Neeraj | N | D.3.1 | 154,36 | MT | The text states that the number of backoff slots is selected from the range of 1 to CWmin, but this should be between 0 and CWmin. | Change 1 to 0. |
| 932 | Wentink, Menzo | Y | D.3.1 | 154,36 | T | The text states that the number of backoff slots is selected from the range of 1 to CWmin, but this should be between 0 and CWmin. | Change 1 to 0. |
| 1599 | Cypher, David | Y | D.3.2 | 154,52 | T | With the publishing of 802.11-2007 | Replace 1999 with 2007 and make all other ammendment references directly to 802.11-2007 and update subclause headers according, as well. |

## Proposed resolution:

Accept CIDs: 1356, 237, 932

Counter CID 1357: (Accept the comment in general). The term is replaced by “average collision free backoff” which is more appropriate.

Accept CID 1599. (Note, this also applies to p153, l 33 where references to 802.11-REVma are given).

# (4) Section D.4.1 Comments

| 1358 | Malarkey, Alastair | Y | D.4.1 | 155,13 | T | Backoff is not the correct term in FS-to-FS interval. | replace "..Backoff" with "..Best-case Backoff" |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1359 | Malarkey, Alastair | Y | D.4.1 | 155,13 | T | Slots is not the correct term in DIFS | replace "..Slots..f" with "..Backoff slots..." |
| 1360 | Malarkey, Alastair | Y | D.4.1 | 155,13 | T | There is a value error in the DIFS equation. Backoff slot has value 50 not 28. | Use correct value of Backoff slot in calculation |
| 1361 | Malarkey, Alastair | Y | D.4.1 | 155,13 | T | Best-case Backoff should be in microseconds to use in FS-to_FS interval formulation | Replace with "Best-case backoff = CWmin / 2 * Backoff slot =…" |
| 1362 | Malarkey, Alastair | Y | D.4.1 | 155,13 | T | The term computed in D.4.1 c) is FR. | Either replace FR in clause c above with Frame Rate or replace Frame Rate in this formula with FR. |

## Proposed Resolutions

Accept CIDs: 1360, 1362

Counter CID 1358, 1359: (Accept the comment in general). The term is replaced by “average collision free backoff” which is more appropriate.

Counter CID 1361: (accept comment in general) accept the comment but use the term “average collision free backoff” on the left side of the equation instead.

# (5) Section D.4.2 Comments

| 1363 | Malarkey, Alastair | Y | D.4.2 | 155,35 | T | Backoff is not the correct term in FS-to-FS interval | replace "..Backoff" with "..Best-case Backoff" |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1364 | Malarkey, Alastair | Y | D.4.2 | 155,35 | T | Slots is not the correct term in DIFS | replace "..Slots..f" with "..Backoff slots..." |
| 1365 | Malarkey, Alastair | Y | D.4.2 | 155,35 | T | Best-case Backoff should be in microseconds to use in FS-to_FS interval formulation | Replace with "Best-case backoff = CWmin / 2 * Backoff slot =…" |
| 1366 | Malarkey, Alastair | Y | D.4.2 | 155,35 | T | The term computed in D.4.2 c) is FR. | Either replace FR in clause c above with Frame Rate or replace Frame Rate in this formula with FR. |

## Proposed Resolutions

Accept CIDs:  1366

Counter CID 1365: (accept comment in general) accept the comment but use the term “average collision free backoff” on the left side of the equation instead.

Counter CID 1363 and 1364: (Accept the comment in general). The term is replaced by “average collision free backoff” which is more appropriate.

# (6) Section D.4.3 Comments

| 1367 | Malarkey, Alastair | Y | D.4.3 | 156,01 | T | Backoff is not the correct term in FS-to-FS interval | replace "..Backoff" with "..Best-case Backoff" |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1368 | Malarkey, Alastair | Y | D.4.3 | 156,01 | T | Slots is not the correct term in DIFS | replace "..Slots..f" with "..Backoff slots..." |
| 1369 | Malarkey, Alastair | Y | D.4.3 | 156,01 | T | Best-case Backoff should be in microseconds to use in FS-to_FS interval formulation | Replace with "Best-case backoff = CWmin / 2 * Backoff slot =…" |
| 1370 | Malarkey, Alastair | Y | D.4.3 | 156,01 | T | The term computed in D.4.3 c) is FR. | Either replace FR in clause c above with Frame Rate or replace Frame Rate in this formula with FR. |

## Proposed Resolutions

Accept CIDs: 1370

Counter CID 1369: (accept comment in general) accept the comment but use the term “average collision free backoff” on the left side of the equation instead.

Counter CID 1367 and 1368: (Accept the comment in general). The term is replaced by “average collision free backoff” which is more appropriate.

# (7) Section D4.4 Comments

| 1371 | Malarkey, Alastair | Y | D.4.4 | 156,21 | T | Backoff is not the correct term in FS-to-FS interval | replace "..Backoff" with "..Best-case Backoff" |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1372 | Malarkey, Alastair | Y | D.4.4 | 156,21 | T | Slots is not the correct term in DIFS | replace "..Slots..f" with "..Backoff slots..." |
| 1373 | Malarkey, Alastair | Y | D.4.4 | 156,21 | T | Best-case Backoff should be in microseconds to use in FS-to_FS interval formulation | Replace with "Best-case backoff = CWmin / 2 * Backoff slot =…" |
| 1374 | Malarkey, Alastair | Y | D.4.4 | 156,21 | T | The term computed in D.4.4 c) is FR. | Either replace FR in clause c above with Frame Rate or replace Frame Rate in this formula with FR. |
| 1375 | Malarkey, Alastair | Y | D.4.4 | 156,21 | T | The term Tack is not clearly listed in table 30 | Change table title and 3rd column to use word Tack |
| 56 | Stephens, Adrian | N | D.4.4 | 156,21 | MT | Calculation is specific to 20MHz channel width. | Either state this, or state this and also add calculation for 10MHz and 5MHz channel widths. |

## Proposed Resolutions

Accept CIDs: 1374

Counter CID 1373: (accept comment in general) accept the comment but use the term “average collision free backoff” on the left side of the equation instead.

Counter CID 1371 and 1372: (Accept the comment in general). The term is replaced by “average collision free backoff” which is more appropriate.

Accept CID 1375 --- Attention, this is NOT reflected in the text provided in 11-07/2345 but should be adopted by the editor accordingly. Instructions to the editor were added to 07/2345 to reflect this situation.

Accept CIDs: 56

# (8) Section D4.5 Comments

| 1376 | Malarkey, Alastair | Y | D.4.5 | 157,23 | T | The definitions of FR previously do not require the sue of the floor function. Also the brackets are incomplete. | Delete "Floor(" |
| --- | --- | --- | --- | --- | --- | --- | --- |

## Proposed Resolutions

Accept CIDs: 1376

# (9) Section D4.6 Comments

| 1377 | Malarkey, Alastair | Y | D.4.6 | 157,42 | T | The TxTime formulation uses "'..Length + PBCC.." but the terms below are PBCC Indicator and PBCC Mode | change to "TxTime = Tpream + PLCPtime + ceiling(((Length + PBCC Indicator) * 8) / PHYrate) + Clock Switch Time" and change PBCC Mode line to "Clock Switch Time = 1 μs @ PBCC Mode of 33 Mb/s, otherwise 0." |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1378 | Malarkey, Alastair | Y | D.4.6 | 157,42 | T | Backoff is not the correct term in FS-to-FS interval | replace "..Backoff" with "..Best-case Backoff" |
| 1379 | Malarkey, Alastair | Y | D.4.6 | 157,42 | T | Slots is not the correct term in DIFS | replace "..Slots..f" with "..Backoff slots..." |
| 1380 | Malarkey, Alastair | Y | D.4.6 | 157,42 | T | Best-case Backoff should be in microseconds to use in FS-to_FS interval formulation | Replace with "Best-case backoff = CWmin / 2 * Backoff slot =…" |
| 1381 | Malarkey, Alastair | Y | D.4.6 | 157,42 | T | The term computed in D.4.6 c) is FR. | Either replace FR in clause c above with Frame Rate or replace Frame Rate in this formula with FR. |

## Proposed Resolutions:

Accept CIDs: 1377

Accept CIDs. 1381

Counter CID 1380: (accept comment in general) accept the comment but use the term “average collision free backoff” on the left side of the equation instead.

Counter CID 1378 and 1379: (Accept the comment in general). The term is replaced by “average collision free backoff” which is more appropriate.

# (10) Section D4.7 Comments

| 1382 | Malarkey, Alastair | Y | D.4.7 | 158,11 | T | Backoff is not the correct term in FS-to-FS interval | replace "..Backoff" with "..Best-case Backoff" |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1383 | Malarkey, Alastair | Y | D.4.7 | 158,11 | T | Best-case Backoff should be in microseconds to use in FS-to_FS interval formulation | Replace with "Best-case backoff = CWmin / 2 * Backoff slot =…" |
| 1384 | Malarkey, Alastair | Y | D.4.7 | 158,11 | T | The term computed in D.4.7 c) is FR. | Either replace FR in clause c above with Frame Rate or replace Frame Rate in this formula with FR. |

## Proposed Resolutions:

Accept CIDs: 1384

Counter CID 1383: (accept comment in general) accept the comment but use the term “average collision free backoff” on the left side of the equation instead.

Counter CID 1382: (Accept the comment in general). The term is replaced by “average collision free backoff” which is more appropriate.

# (11) Section D4.8 Comments

| 1385 | Malarkey, Alastair | Y | D.4.8 | 158,34 | T | Shouldn't this be Best-case Backoff to be consistent | Replace "Backoff" with "Best-case backoff" |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1386 | Malarkey, Alastair | Y | D.4.8 | 158,34 | T | Best-case Backoff should be in microseconds to use in FS-to_FS interval formulation | Replace with "Best-case backoff = CWmin / 2 * Backoff slot =…" |
| 1387 | Malarkey, Alastair | Y | D.4.8 | 158,34 | T | The term computed in D.4.8 c) is FR. | Either replace FR in clause c above with Frame Rate or replace Frame Rate in this formula with FR. |

## Proposed Resolutions:

Counter CID 1386: (accept comment in general) accept the comment but use the term “average collision free backoff” on the left side of the equation instead.

Note to the Editor: p159 l7 of 802.11.2-D1.0 should also read “Best-case Backoff”. This change is reflected in 11-07/2345

Accept CIDs: 1387

Counter CID 1385: (Accept the comment in general). The term is replaced by “average collision free backoff” which is more appropriate.

# (12) Section D4.9 Comments

| 1388 | Malarkey, Alastair | Y | D.4.9 | 159,13 | T | the term PBCC is used to define itself ! | Change "PBCC" to "PBCC Indicator" in TxTime formulation lines and change "PBCC:.." to "PBCC indicator:…" |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1389 | Malarkey, Alastair | Y | D.4.9 | 159,13 | T | Backoff is not the correct term in FS-to-FS interval | replace "..Backoff" with "..Best-case Backoff" |
| 1390 | Malarkey, Alastair | Y | D.4.9 | 159,13 | T | Slots is not the correct term in DIFS | replace "..Slots..f" with "..Backoff slots..." |
| 1391 | Malarkey, Alastair | Y | D.4.9 | 159,13 | T | Best-case Backoff should be in microseconds to use in FS-to_FS interval formulation | Replace with "Best-case backoff = CWmin / 2 * Backoff slot =…" |
| 1392 | Malarkey, Alastair | Y | D.4.9 | 159,13 | T | The term computed in D.4.9 c) is FR. | Either replace FR in clause c above with Frame Rate or replace Frame Rate in this formula with FR. |

## Proposed Resolutions:

Accept CIDs: 1388,

Accept CIDs: 1392

Counter CID 1391: (accept comment in general) accept the comment but use the term “average collision free backoff” on the left side of the equation instead.

Counter CID 1389 and 1390: (Accept the comment in general). The term is replaced by “average collision free backoff” which is more appropriate.

# (13) Section 4.10 Comments

| 1393 | Malarkey, Alastair | Y | D.4.10 | 159,38 | T | There are a number of inconsistencies in this formulation. The headers are not inlcuded in the base formulation. TpreamDSSS is not defined. Pad is not defined … | Please correct formulation |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1394 | Malarkey, Alastair | Y | D.4.10 | 159,38 | T | Backoff is not the correct term in FS-to-FS interval | replace "..Backoff" with "..Best-case Backoff" |
| 1395 | Malarkey, Alastair | Y | D.4.10 | 159,38 | T | Best-case Backoff should be in microseconds to use in FS-to_FS interval formulation | Replace with "Best-case backoff = CWmin / 2 * Backoff slot =…" |
| 1396 | Malarkey, Alastair | Y | D.4.10 | 159,38 | T | The term computed in D.4.10 c) is FR. | Either replace FR in clause c above with Frame Rate or replace Frame Rate in this formula with FR. |

## Proposed Resolutions:

Accept CID: 1393

Formulation of TXTIME corrected. Naming of components in alignment

with Cls. 19.8.3.3 of 802.11-2007.

Accept CID:  1396

Counter CID 1395: (accept comment in general) accept the comment but use the term “average collision free backoff” on the left side of the equation instead.

Counter CID 1394: (Accept the comment in general). The term is replaced by “average collision free backoff” which is more appropriate.

# Text boxes

Abstract

This document contains proposed comment resolutions for those CIDs of LB 101 addressing Annex D – Theoretical Throughput Limits.

This document contains the comments and proposed resolutions. It is accompanied by document 11-07/2345 which contains the draft text of 802.11.2-D1.0 Annex D and highlights the changes introduced by adopting the comment resolutions as proposed hereafter.

This submission addressed the following comment CIDs of LB 101:

1356, 237, 932, 1357, 1599, 1358, 1359,

1360, 1361, 1362, 1363, 1364, 1365, 1366, 1367, 1368, 1369,

1370, 1371, 1372, 1373, 1374, 1375, 56,

1376, 1377, 1378, 1379, 1380, 1381, 1382, 1383, 1384, 1385,

1386, 1387, 1388, 1389, 1390, 1391, 1392, 1393, 1394,

1396