IEEE P802.11
Wireless LANs

| FT Resource Request Protocol Removal |
| --- |
| Date: 2007-10-23 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Kapil Sood | Intel Corp. | 2111 NE 25th Ave JF3-206, Hillsboro OR 97124 | +1 503 264 3759 | kapil.sood@intel.com |
| Bernard Aboba | Microsoft |  |  | Bernard_aboba@hotmail.com |

Clause 7.2.3.6, Page 8, line 23

Change: is true, the frame is being

Clause 7.2.3.10, Page 9, line 43-50

Change:  Remove rows with Order 8 and 9 from Table 7-16

Clause 7.2.3.10, Page 10, line 22-42

Change:  Remove rows with Authentication Transaction Sequence number 3 and 4 from Table 7-17

Clause 7.3.2.25.4, Page 12, line 40

Change:  Request frame to an AP. The PMKID

Clause 7.3.2.45, Page 14, line 4

Change:  Remove bit B1 (Resource Request Protocol Capability) fromFig 7-95q

Clause 7.3.2.45, Page 14, line 23

Change:  Delete lines 23-24.

Clause 7.4.7, Page 18, line 50-53

Change:  Remove in Table 7-57b the 2 rows with Action Field values 3 and 4.  Change “3-255     Reserved”

Delete Clause 7.4.7.3, Page 20-21

Change:  Delete the entire clause 7.4.7.3

Delete Clause 7.4.7.4, Page 21

Change:  Delete the entire clause 7.4.7.4

Clause 8.4.1.1.2, Page 23, line 27

Change:  The PTKSA is a result of the 4-Way Handshake, an FT 4-Way Handshake, or an FT protocol..

Delete Clause 10.3.34, Page 41-45

Change:  Delete the entire Clause 10.3.34

Clause 11.4.1, Page 50, line 11

Change:  In addition, a Traffic Stream could be created if a non-AP STA sends a resource request to an AP in reassociation request during a transition to that AP.

Clause 11.4.3, Page 50-51, line 1

Change: Delete all changes to Clause 11.4.3, including Figure 11-7 on page 51, and lines 61-65.

Clause 11.4.4a, Page 52, line 3

Change:  A non-AP QoS STA may transmit a TSPEC as part of a RIC-Request in the reassociation request message. The SME in the HC decides whether to accept the TSPEC as specified, or refuse the TSPEC, or not accept but suggest an alternative TSPEC, and generates a RIC-Response, according to the procedures given in 11A.11.

The TS is moved to the Active state if the AP accepts the reassociation from the non-AP STA.

Clause 11A.1, Page 52, line 51

Change: Delete lines 51-59 on page 52.

Clause 11A.1, Page 53, line 8

Change: APs advertise capabilities and policies for supporting the FT methods.

Clause 11A.1, Page 53, line 13-15

Change: NOTE-- Throughout this clause, the notation Authentication-Request refers to an Authentication frame with the Authen-tication Transaction Sequence number set to 1; Authentication-Response refers to an Authentication frame with the Authentication Transaction Sequence number set to 2; The first parameter to the above two messages is the Authentication Algorithm, such as "Open System Authentication Algorithm" (or short-ened to "Open"), or "Fast BSS Transition Authentication Algorithm" (or shortened to "FT").

Clause 11A.3, Page 55, line 49

Change: policy bits in the MDIE and Fast BSS Transition over DS field shall be set according to the value of the MIB variables dot11FTOverDSEnabled..

Clause Annex D, Page 110, line 18-28

Change: Delete the entire definition of the MIB variable dot11FTResourceRequestSupported.  Change “ ”

Clause Annex D, page 109, line 8

Change: Delete line dot11FTResourceRequestSupported.  Change “”

Clause Annex D, Page 111, line 22

Change: entity shall retain a PTKSA for a non-AP STA

Clause 11A.5.1, Page 60, line 17

Change:  The FT protocol supports resource requests as part of the reassociation.

Clause 11A.6, Page 67, line 1

Change: Delete entire Clause 11A.6, 11A.6.1, 11A.6.2, 11A.6.3

Clause 11A.7.1, Page 74, line 32-39

Change:  Delete lines 32-39.  “.”

Clause 11A.7.1, Page 74, line 41

Change:  The STA may make a request for resources

Clause 11A.7.2, Page 75, line 41-44

Change:  Delete lines 25-28. “ .”

Clause 11A.7.2, Page 75, line 46

Change:  The non-AP STA may make a request for resources by

Clause 11A.8.1, Page 76, line 8

Change:  These messages are included in the FT protocol frames to initiate a Fast BSS Transition.

Clause 11A.8.1, Page 76, line 18

Change:  onstrate liveness of the peer and authenticate the information elements. .

Clause 11A.8.1, Page 76, line 28-32

Change:  Delete lines 28-32.  Change: “ .”

Clause 11A.8.1, Page 76, line 50

Change:  Delete the entire row in Table 11A-1 pertaining to Timeout Interval.  Change “ ”

Clause 11A.8.1, Page 77, line 18

Change:  This also includes a Status Code.

Clause 11A.8.4, Page 78, line 53

Change:  Transaction sequence number (1 octet) which shall be set to the value 3.

Clause 11A.8.5, Page 79, line 30

Change:  The Optional parameters in the FTIE may include a GTK sub-element.

Clause 11A.8.5, Page 79, line 48

Change:  Transaction sequence number (1 octet) which shall be set to the value 4.

Clause 11A.8.5, Page 79, line 59-65; and, Clause 11A.8.5 Page 80 line 1

Change:  Delete all lines 59-65 on page 79 and line 1 on page 80.  Change “ .”

Clause 11A.9.1, Page 80, line 27

Change:  Delete line 4.  Change “ ”

Clause 11A.9.3, Page 82, line 56

Change:  establishment, FT protocol (including resource requests), and cleanup

Clause 11A.9.3, Page 82, line 60

Change:  to get the PMK-R1 Security Association (PMK-R1 PMKSA) for the FT protocol.

Clause 11A.9.3, Page 84, line 31 in Fig 11A-15

Change:  Delete arrow “MLME-RESOURCE_REQUEST.indication (ANonce, SNonce, MD-ID, RSNIE, PMKR1Name, RIC-Req) && MIC-Verified” going out of state FT-PMK-R1-SA-RECD.  Delete entire state and contents of FT-RV-HANDSHAKE-NEGOTIATING.  Delete arrow “MLME-REASSOCIATE.indication(ANonce, SNonce, MD-ID, R0KH-ID, R1KH-ID, PMK-R1Name) && MIC-Verified” going into FT-HANDSHAKE-DONE.  Delete from state FT-HANDSHAKE-DONE the following line “(If Resv-Flow, then do not include RIC-Resp in this msg)”

Clause 11A.9.3.1, Page 85, line 41

Change:  Delete lines 31-33.  Change: “ .”

Clause 11A.9.3.2, Page 86, line 11

Change:  Delete line 1.  Change “ .”

Clause 11A.9.5, Page 90, line 31 Fig 11A-18

Change:  Delete arrow “Resource-Request && over-the-Air” going out of state FT-PTK-CALC.  Delete arrow “Resource-Request && over-the-DS” going out of FT-PTK-CALC”.  Delete arrow “Timeoutctr > N” going out of FT-RV-AIR-CONFIRM”.  Delete arrow “Timeoutctr > N” going out of FT-RV-DS-CONFIRM”.  Delete arrow “TimeoutEvt” going out of states FT-RV-AIR-CONFIRM and out of FT-RV-DS-CONFIRM.  Delete arrow “MLME-RESOURCE_REQUEST.confirm (ANonce, SNonce, MDIE, RSNIE, PMK-R1Name, RIC-Resp) && MIC-Verified” going out of state FT-RV-AIR-CONFIRM.  Delete arrow “MLME-REMOTE_REQUEST.indication (ANonce, SNonce, MDIE, RSNIE, PMK-R1Name, RIC-Resp) && MIC-Verified” going out of state FT-RV-DS-CONFIRM.  Delete arrows “Timeoutctr > N”, “TimeoutEvt”, and “MLME-REASSOCIATE.confirm(ANonce, SNonce, MDID, R0KH-ID, R1KH-ID, PMK-R1Name) && MIC-Verified” going out of state FT-RESERVE-2.  Delete “To Disconnect” arrow going out of states FT-RESERVE-2 and FT-RV-DS-CONFIRM.  Delete entire states FT-RV-AIR-CONFIRM, FT-RV-DS-CONFIRM, FT-RESERVE, and FT-RESERVE-2.  Change “UCT” going out of FT-PTK-CALC.

Clause 11A.9.5.1, Page 91, line 62-65 and Clause 11A.9.5.1 Page 92 line 1-9

Change:  Delete lines 62-65 on page 91 and lines 1-9 on page 92.  Change “ .   .”

Clause 11A.9.5.2, Page 92, line 57

Change:  Delete line 48.  Change “ ”

Clause 11A.10.1, Page 93, line 18

Change:  Change “The current AP encapsulates the FT Action Frame (Request) inside a Remote Request, and transmits it to the target AP over the DS. The target AP processes the remote request and responds to the non-AP STA by sending an FT Action Frame (Response) through the current AP.”

Clause 11A.10.2, Page 94, line 38 Figure 11A-19

Change:  Change Figure 11A-19 as follows :  Delete the following arrows “FT Action Confirm (Confirm IEs)”, “RemoteRequest (current AP address, FT Action Confirm)”, “RemoteResponse (current AP address, FT Action Acknowledge)”, “FT Action Acknowledge (Acknowledgement IEs)”

Clause 11A.10.2, Page 94, line 47

Change:  Change title of Fig 11A-19 “Figure 11A-18—Sample message flow for over-the-DS”

Clause 11A.10.2, Page 94, line 42 Figure 11A-19

Change:  Delete the text “Target AP processes confirmation.”  Change “ .”

Clause 11A.11.1, Page 95, line 46-50

Change:  To request resources the non-AP STA creates a Resource Information Container (RIC) and inserts the RIC in the Reassociation Request message to the target AP.

Clause 11A.11.1, Page 95, line 52-57

Change:   .

Clause 11A.11.1, Page 95, line 64-65 and Page 96 lines 1-2

Change:

Clause 11A.11.3.1, Page 99, line 8-12

Change:

Clause 11A.11.3.2, Page 101, line 28-36

Change:  If the resource request included QoS resources and is successful, then the procedures for handling of TSPEC, TCLAS and TCLAS Processing elements shall be as specified in 11.4, and the AP shall place the Traffic Streams into the "Active" state. The response RIC shall contain the updated admitted TSPEC. Each RDIE may also include a Schedule information element (as defined in 7.3.2.34) after the admitted TSPEC.

Clause Annex A A.4.4.1, page 104, line 14-22

Change: Detele rows on lines 14-22.  Change “”

# Text boxes

Abstract

This submission proposes a resolution to multiple comments from Sponsor Ballot that asks for the removal of the Fast BSS Resource Request protocol from TGr.  These updates apply to TGr D8.0.