IEEE P802.11
Wireless LANs

| Resolution of Some APSD-related Comments |
| --- |
| Date: 2006-09-19 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Michelle Gong | Intel Corporation | 2200 Mission College Blvd. Santa Clara, CA 95054, USA | +1-408-765-7994 | michelle.x.gong@intel.com |
| Dee Denteneer | Philips | HTC 37 5656 AE Eindhoven The Netherlands | + 33 40 27 46937 | Dee.denteneer@philips.com |
| Steve Emeott | Motorola | 1301 E. Algonquin Rd., Schaumburg, IL 60196 | +1 847-576-8268 | Steve.Emeott@Motorola.com |
| Kevin Hayes | Atheros | 5480 Great America Parkway, Santa Clara, CA 95054 |  | kevin@atheros.com |
| Guido Hiertz | Philips | ComNets, RWTH Aachen University, Kopernikusstr. 16, 52074 Aachen, Germany | +49-241-802-5829 | hiertz@ieee.org |
| Jarkko Kneckt | Nokia | Itämerenkatu 11-13 00180 Helsinki Finland | +358504821550 | Jarkko.kneckt@nokia.com |
| Kazuyuki Sakoda | Sony Corporation | 5-1-12 Kita-Shinagawa Shinagawa-ku, Tokyo, 141-0001 Japan | +81-3-5448-4017 | sako@wcs.sony.co.jp |
| Zhen Xie | Atheros | 5480 Great America Parkway, Santa Clara, CA 95054 |  | zhen@atheros.com |

The resolved comments are: CID 1100, 3951, 563, 564, and 565.

| 1100 | 11A.9: PowerSave | Since its unclear how TS are suspended, the section on TS reinstatement is unnecessary | Delete 11A.9.10 | Accept | The section has been removed in draft D1.06. |
| --- | --- | --- | --- | --- | --- |
| 3951 | 11A.9: PowerSave | while APSD is expected to be utilized, description on TS operation is completely missing. The subclause 11A.9.10 should not be a part of power management sublause but should be a part of TS operation. | Remove subclause 11A.9.10, create a new clause for TS operation, and describe the details. | Accept | The section has been removed in draft D1.06. |

| 563 | 11A.9: PowerSave | 11A.9.4 Basic approach: states: "1) Send traffic to these mesh points only on agreed schedules as negotiated as part of APSD (Automatic Power Save Delivery) TSPEC setup" This type of APSD, which in addition to a periodic TSPEC also involves EDCA channel access, is called Scheduled APSD in Clause 11.2.1.4 of the IEEE 802.11e standard. | Refer to "APSD with [periodic] TSPEC [and EDCA access]" as "Scheduled APSD as specified in 802.11e. | Reject | The periodic APSD operation as defined in the draft is different from the scheduled APSD as defined in 802.11e |
| --- | --- | --- | --- | --- | --- |
| 564 | 11A.9: PowerSave | 11A.9.4 Basic approach: Scheduled APSD (specifically, use of a periodic TSPECs in conjunction with EDCA channel access) couples ideally with MDA. MDA is a multilaterally negotiated periodic TSPEC (with time restriction to simplify scheduling). It should be possible to couple the two mechanisms together to give something very attractive. | Include text to explain how MDA and Scheduled APSD will be used together. | Reject | It's out of the scope of the standard |
| 565 | 11A.9: PowerSave | 11A.9.6 Mesh point power state transitions: States: "In addition a mesh point will enter awake state prior to every agreed schedule as negotiated as part of a periodic APSD TSPEC exchange with other mesh points". The same comment as before. | Replace the language "as part of a periodic APSD TSPEC exchange" with "as part of a Scheduled APSD TSPEC exchange" | Reject | The periodic APSD operation as defined in the draft is different from the scheduled APSD as defined in 802.11e |
| 566 | 11A.9: PowerSave | 11A.9.8 Power management operation with APSD: The appropriate signaling already exists in Scheduled APSD, as this form of APSD works on a schedule negotiated between the two parties [AP and STA]. No modification of the ADDTS request is necessary. The ADDTS request contains a TSPEC element which proposes a schedule. The Schedule element returned in the response to the ADDTS requesting Scheduled APSD service confirms the schedule. No modification Is needed to add a Schedule element to the ADDTS request, as proposed in this text. | The section should be entitled "Power Management with Scheduled APSD". Unscheduled APSD is not that useful for mesh [as is also indicated in the draft] and therefore it should not be mentioned in the draft. As written the section is inaccurate and confusing. Correct section and make it more direct and to the point. | Reject | The current TSPEC element is defined for hierarchical networks. A mesh network doesn't have a hierarchy. Thus, the concept of TSPEC doesn't suit mesh networks. |

References:

doc.: IEEE 802.11-07/0023r47 IEEE P802.11s™/D1.06

# Text boxes

Abstract

This document resolves comments related to Power Save-APSD.