IEEE P802.11
Wireless LANs

| TGp LB 110 Comment Resolution Clauses 1, 2, and 3 |
| --- |
| Date: 2007-09-20 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Francois Simon | ARINC, Inc. | 2551 Riva Road, Annapolis, MD 21401 | 410-266-4958 | fsimon@arinc.com |
| Wayne Fisher | ARINC, Inc. | 2551 Riva Road, Annapolis, MD 21401 | 410-266-4958 | wfisher@arinc.com |

|  | LB110 Comment Resolution |
| --- | --- |

- COMMENT:  [From Spreadsheet]  INSERT Original Comment Here:

| CID | Name | Subclause | Page | Line | Type | Comment | SuggestedRemedy | Response |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2 | Adachi, Tomoko | General | 1 | 1 | TR | Which present 802.11 services, frames, fields and elements are disallowed in WAVE? | List | Services, frames, fields and elements not used in WAVE mode are discarded by a WAVE STA |
| 7 | Seok, Yongho | General | 1 | 1 | TR | It is not clear to me how a STA is determined to be either a WAVE provider or a WAVE user. There should be something somewhere in the document that formalizes these terms, linking them to MIB values and subsequently, to behaviors. | Clairfy which STA become WAVE providers and which become WAVE users versus neither of these and what causes these distinctions. | Both STAs will have the dot11WAVEServicesEnabled = true. Only WAVE providers issue the Advertisment frame across the air link. |
| 26 | Adachi, Tomoko | 2 | 2 | 12 | ER | There is no Section 2 for Normative references. | Insert a Normative Reference section that lists in particular the IEEE 1609.x standards that 802.11p depends on. | The IEEE 1609.x standards does not depends on 802.11p. The uppers layers (IEEE 1609.x) depends on the service of 802.11p like any other appications using the 802.11 services. |
| 46 | Cypher, David | 3.168a | 2 | 19 | ER | The definition of WBSS states that it includes “none or more” WBSS users. | Change “none” to “zero” | The following text is suggested: "A set of cooperating stations (STA) operating in WAVE mode consisting of a single WAVE service provider and a single, multiple, or in the absence of WAVE service users." |
| 57 | Ecclesine, Peter | 3.168b | 2 | 24 | TR | The text states that a WSIE "may be included as a field in a WAVE Advertisement frame using the On-demand management frame" However, this statement has a number of problems: * Grammatically it is incorrect because it implies one has to use an "On-demand management frame" to include a WSIE into a WAVE Advertisement frame, which makes no sense * "On-demand management frame" is not defined, although it appears it is just a Beacon sent at a time other than a TBTT * "WAVE Advertisement frame" is undefined, although it appears it is just a Beacon with a WSIE | Clean up definitions and terminology to: * Avoid grammatical weirdness * Avoid undefined terms * Avoid two terms for same thing | WAVE Advertissment frame is a frame advertising a WBSS. It uses the On-demand beacon which is NOT 802.11p exclusive. The on-demand beacon is a 802.11 defined beacon which is sent at the request of the upper layers (above 802.11 MAC). See sub-clause 7.1.3.1.2; last sentence |

- Background, Explanation, Discussion, etc.:

Discussion.

- Recommended Resolution of the Comment:

See Comment Responses in table.

- Motion (if technical and/or significant):

(And instructions to the editor.)

Move to xxxxxxxxxxxxxxxxxx     …  .

Motion by: ____________________Date: _________________

Second:  ______________________

| Approve: | Disapprove: | Abstain: |
| --- | --- | --- |

References:

# Text boxes

Abstract

This document persents comments for General and Clauses 1, 2, and 3 for discussion and potential resolution.