IEEE P802.11
Wireless LANs

| TGp LB 110 Comment Resolution Clause 7.1.3 |
| --- |
| Date: 2007-09-20 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Francois Simon | ARINC, Inc. | 2551 Riva Road, Annapolis, MD 21401 | 410-266-4958 | fsimon@arinc.com |
| Wayne Fisher | ARINC, Inc. | 2551 Riva Road, Annapolis, MD 21401 | 410-266-4958 | wfisher@arinc.com |

|  | LB110 Comment Resolution |
| --- | --- |

- COMMENT:  [From Spreadsheet]  INSERT Original Comment Here:

| CID | Name | Subclause | Page | Line | Type | Comment | SuggestedRemedy | Response |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 150 | Malinen, Jouni | 7.1.3.1.2 | 4 | 14 | TR | Sentence does not stress clearly enough that the mentioned frame types are the only ones permitted in WAVE mode. | Change first sentence to: "In WAVE mode, only the following frames may be used: management frame of subtype 1000 (Beacon frame), .........." | Frames not used in WAVE mode are discarded. |
| 153 | Malinen, Jouni | 7.1.3.1.2 | 4 | 14 | TR | The restrictions on frame types should be moved from this clause to clause 11.3. | Move the text. | The insertion of the text in P802.11p/D3.0; sub-clause belongs in IEEE 802.11 Std-2007, Sub-clause 7.1.3.1.2. If the comment relates to move 7.1.3.1.2 to 11.3, then this be better addressed by 802.11 working group responsible for the maintenance of 802.11. |
| 155 | Malinen, Jouni | 7.1.3.1.2 | 4 | 15 | T | It seems that in WAVE mode QoS DATA frame is a mandotary.If WAVE mode only support QoS mode, exchange WAVE BSS into WAVE QBSS in the draft. Othewise, include the data frame of subtype of 0000. | Include the data frame of subtype of 0000. | QoS data frame is not mandatory in WAVE mode. |
| 159 | Malinen, Jouni | 7.1.3.1.2 | 4 | 16 | TR | "WAVE Advertisement frame" "On-demand beacon" These seems to be unsubstantial and reusing a beacon frame. But the manner is different. | Use the ordinary beacon and its behaviour. | TheWAVE advertissment frame uses the on-demand beacon. The on-demand beacon uses the beacon frame format defined in IEEE 802.11 Std-2007. Except that the transmission is initiated by the higher layers above the MAC. |
| 160 | Malinen, Jouni | 7.1.3.1.2 | 4 | 16 | TR | I can not believe that it is being proposed that unassociated and unauthenticated STAs access a DS. You can not skip fundamental parts of the MAC and still call yourself 802.11. Why are proposers of this amendment trying to break 802.11? | require association and authentication before access to the DS is granted | This comment is being addressed in sub-clause 5.2.3.3. |
| 161 | Myles, Andrew | 7.1.3.1.2 | 4 | 16 | TR | If WBSS providers use a "traditional IEEE 802.11 beacon" as WAVE Advertisement frames, there is no way to tell that this is not actually a ("traditional") AP, and non-WAVE STAs will try to authenticate/associate to it. The inclusion of a WSIE seems to be the only distinction, but this is optional and would be ignored by legacy STAs that don't recognize it anyway. | Use a new frame type for WAVE Advertisement frames. | Using a new frame type for WAVE advertisement frames bring us back to pre- Montreal meeting. It was pointed out that we should use the traditional beacon format. |
| 166 | Myles, Andrew | 7.1.3.1.2 | 4 | 17 | TR | "uses" or "is"? The advertisement does not use a beacon - it IS a beacon. | Reword to correctly reflect reality. | The WAVE advertissment happen to use the on-demand beacon. The on-demand beacon is not exclusive to WAVE mode. |

- Background, Explanation, Discussion, etc.:

Discussion.

- Recommended Resolution of the Comment:

See Comment Responses in table.

- Motion (if technical and/or significant):

(And instructions to the editor.)

Move to xxxxxxxxxxxxxxxxxx     …  .

Motion by: ____________________Date: _________________

Second:  ______________________

| Approve: | Disapprove: | Abstain: |
| --- | --- | --- |

References:

# Text boxes

Abstract

This document persents comments for Clauses 7.1.3 for discussion and potential resolution.