IEEE P802.11
Wireless LANs

| TGp LB 110 Comment Resolution Clause 7.3 |
| --- |
| Date: 2007-09-20 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Francois Simon | ARINC, Inc. | 2551 Riva Road, Annapolis, MD 21401 | 410-266-4958 | fsimon@arinc.com |
| Wayne Fisher | ARINC, Inc. | 2551 Riva Road, Annapolis, MD 21401 | 410-266-4958 | wfisher@arinc.com |

|  | LB110 Comment Resolution |
| --- | --- |

- COMMENT:  [From Spreadsheet]  INSERT Original Comment Here:

| CID | Name | Subclause | Page | Line | Type | Comment | SuggestedRemedy | Response |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 264 | Kolze, Thomas | 7.3.2.36 | 6 | 38 | TR | Wow! What an element! This is a standard? Unless there is some explicit indication of what is contained in this element, it is worthless. We already have a vendor specific IE which serves this purpose, only better, because it has OUI field. | Delete this element. | The content of the WSIE is not processed my the PHY and MAC layers of IEEE 802.11 Std-2007. The WSIE(s) element(s) are higher layer peer-to-peer WAVE mode STAs |
| 268 | Kolze, Thomas | 7.3.2.36 | 6 | 40 | TR | "The WISE .... is prenent only in the On-demand-beacon frame." It is unclear if the WISE is a mandatory component of the on-demand beacon. I would suggest making it optional as it might be useful to transmit on-demand beacons without WSIE. | Change 1st sentence to: "The WSIE, when used in management frames, may only be present in the On-demand beacon frame." | In sub-clause 3.168b states that the WSIE MAY be included in a Wave Advertisement frame using the on-demand beacon. The on-demand beacon is NOT WAVE exclusive. |
| 270 | Kolze, Thomas | 7.3.2.36 | 6 | 40 | T | The term Wave Advertisement should clearly be associated with WSIE here. | Recommend adding after 1st sentence "A On-demand Beacon frame containing a WSIE is also referred to as a WAVE Advertisement frame. | One may have a WAVE advertissment without a WSIE included in the Wave Advertissment. The WAVE advertissment uses the on-demand beacon. However, the on-demand beacon is not exclusive to WAVE mode |
| 275 | Lauer, Joseph | 7.3.2.36 | 6 | 42 | ER | The Content field of the WSIE is presumably defined by IEEE 1609.4 but there is no reference to this. | Add a reference to the standard that defines the content of the WSIE. | The reference to other standards above the MAC layer of 802.11Std is out of scope. There is no such precedence in IEEE 802.11 Std-2007. |
| 276 | Lauer, Joseph | 7.3.2.36 | 6 | 42 | TR | To attempt to future proof the WSIE the Content field should contain a sub-element. Sub-element of type 0 would be for the current 1609 standards. Sub-elements of other types could then be defined to allow other protocol stacks to sit on top of 802.11p. | Redefine the WSIE Content field with a sub-element structure, e.g. Protocol Stack sub-element. Define Protocol Stack sub-element 0 to carry the 1609 protocol stack. | The content of the WSIE is outside the scope of 802.11 as metioned in the comment's referenced sub-clause. |
| 283 | Montemurro, Michael | 7.3.2.36 | 6 | 51 | ER | clarify the type of "management information" contained in the WSIE | change "management information" to "WAVE management information" | The content of the WSIE is outside the scope of this standard as mentioned in sub-clause 7.3.2.36; last paragraph. |

- Background, Explanation, Discussion, etc.:

Discussion.

- Recommended Resolution of the Comment:

See Comment Responses in table.

- Motion (if technical and/or significant):

(And instructions to the editor.)

Move to xxxxxxxxxxxxxxxxxx     …  .

Motion by: ____________________Date: _________________

Second:  ______________________

| Approve: | Disapprove: | Abstain: |
| --- | --- | --- |

References:

# Text boxes

Abstract

This document persents comments for Clauses 7.3 for discussion and potential resolution.