IEEE P802.11
Wireless LANs

| Proposed Texts for TGs Frame Forwarding at Intermediate and Destination MPs |
| --- |
| Date: 2006-09-20 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Liwen Chu | STMicroelectronics, Inc. | 1060 East Brokaw Road, MS 212, San Jose, CA 95131 | +1-408-467-8436 | Liwen.chu@st.com |
| George Vlantis | STMicroelectronics, Inc. | 1060 East Brokaw Rd. San Jose, CA 95131 | +1 408 451-8109 | George.vlantis@st.com |
| Guenael Strutt | Motorola | 1064 Greenwood Blvd – Lake Mary, FL 32771 -- USA | +1-407-562-4050 | Guenael.Strutt@motorola.com |
| Michael Bahr | Siemens AG, Corporate Technology | Otto-Hahn-Ring 6, 81730 München, Germany | +49-89-636-49926 | bahr@siemens.com |

Background

This contribution provides updated texts for frame forwarding at intermediate and destination MPs.

The following is normative text proposed as an amendment to P802.11s/D0.06.

Update Clause 11A.5.5.2.2 as follows:

- At Intermediate and destination MPs

On receipt of a unicast mesh frame, an MP shall decipher it and check it for authenticity. If it is not from a peer MP, the frame shall be silently discarded.

The MP shall then check to see whether the Mesh DA in Address 3 field is known; if it is an unknown address, the MP may either silently discard the frame or trigger a path discovery procedure depending on the path selection protocol that is currently active in the mesh.

By the pair of source MP Address (identified by Address 4 field) and Mesh Sequence Number, the MP may detect duplicate frames. Duplicate frames may be discarded.

If Address 3 does not match the MP’s own address, but is a known MAC addresses in the forwarding information, the MP shall decrement the TTL field in the Mesh Header. If zero has been reached, the frame shall be discarded. Otherwise, the MP shall forward the frame by setting the Address 1 field to the MAC address of the next hop MP as determined from the forwarding information and the TA field to its own MAC address and queueing the frame for transmission.

If Address 3 matches the MP’s own MAC address, and the frame is a Mesh data frame,  then the MP shall check the Address Extension Mode field in the Mesh Header field and take the following actions based on its value:

- If the Address Extension Mode is set to 00 or 01, indicating this MP is the final destination of the frame, the MP shall process and send it to an upper layer.  By the pair of source MP Address (identified by Address 4 field) and Mesh Sequence Number, the destination MP may detect duplicate frames.  Duplicate frames may be discarded.

- If the Address Extension Mode is set to 10 or 11:

- If the current MP is the final destination of the frame (mesh DA = DA), the MP shall process and send it to an upper layer

- If the current MP is a proxy MP for non-mesh, proxied entities, the MP shall first check whether or not the destination address (DA) in Address 5 field is one of the addresses of its proxied entities. If the destination address is the address of one of its proxied entities, the MP shall translate the frame to the corresponding format and queue it for transmission to the final destination.

- If the current MP is a root MP (in HWMP proactive tree building mode), the MP shall check whether the DA in Address 5 field is one of its known addresses or not:

- If the DA in Address 5 corresponds to an MP for which there is valid forwarding information and Address 4 is the same as Address 6, the MP shall reformat the frame as a 4-address frame with Address 3 field set to the DA, Address 4 set to the source end-point addressMesh SA, Address 1 set to the next-hop MP in the forwarding information on the mesh path to the destination MP, and Address 2 set to the root MP’s address.  The MP shall then queue the frame for transmission. The address extension mode becomes 00 or 01 if the received frame is a Data Frame or a Multihop Action Frame (respectively). The MP shall then queue the frame for transmission.

- If the DA in Address 5 corresponds to an MP for which there is valid forwarding information and Address 4 is not the same as Address 6, the MP shall set the Address 3 field to the DA, Address 1 set to the next-hop MP in the forwarding information to the destination MP, and Address 2 set to the root MP’s address. The MP shall then queue the frame for transmission.

- If the DA in Address 5 corresponds to a non-mesh entity proxied by an MP for which there is valid forwarding informationone of its known MPs, the MP shall update the Address 3 field to the address of the proxy MP, the Address 1 field to the next-hop MP in the forwarding information on the mesh path to the proxy MP, and Address 2 to the root MP’s address.  The MP shall then queue the frame for transmission.

Note that in some cases, an MP could be both a proxy MP and a root MP. In such a case, the MP should follow both the steps described for the case that Address Extension Mode is set to 10 or 11.

Also, note that during the forwarding process at intermediate MPs, the contents of the frame body are not changed.

References:

- L. Chu et al., “Forwarding at Intermediate and Destination Mesh Points (MP) using 6-Address Scheme,” IEEE 802.11-07/2439r0.

# Text boxes

Abstract

This submission provides updated texts for Clauses 11A.5.5.2.2.

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart.kerry@philips.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.