IEEE P802.11
Wireless LANs

| Normative Text Changes for LB108 CID#97 |
| --- |
| Date: 2007-11-02 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Emily Qi | Intel Corp. | 2111 NE 25th Ave Hillsboro OR 97229 | 503-264-7799 | Emily.H.Qi@intel.com |

- TGv Editor: Change clause 10.3.50 and 10.3.51 as follows:

- Location request

This set of primitives supports the exchange of location parameter information between peer SMEs. Location Request and Response Protocol Exchange depicts the location request process. The figure illustrates the basic protocol and is only an example and therefore is not meant to be exhaustive of all possible protocol uses.

- Location Request and Response Protocol Exchange

- MLME-LOCATION.request

- Function

This primitive requests the transmission of a location request action frame to a peer entity.

- Semantics of the service primitive

The primitive parameters are as follows:

MLME-LOCATION.request	(
Peer MAC Address,
Dialog Token,
Response Requested,
Location Parameters
)

| Name | Type | Valid Range | Description |
| --- | --- | --- | --- |
| Peer MAC Address | MACAddress | Any valid individual MAC Address, or the Broadcast MAC address | The address of the peer MAC entity to which the location request shall be sent. |
| Dialog Token | Integer | 0 – 255 | The dialog token to identify the location transaction. |
| Response Requested | Integer | 0 – 255 | The response requested value indicates if a Location Response frame is requested. |
| Location Parameters | Set of location elements | Set of location elements | A set of location elements describing the STA location information. See 7.3.2.66. |

- When generated

This primitive is generated by the SME to request that a Location Request frame be sent to a peer entity to convey location information.

- Effect of receipt

On receipt of this primitive, the MLME constructs a Location Request frame containing the set of location elements specified. This frame is then scheduled for transmission.

- MLME-LOCATION.confirm

- Function

This primitive reports the result of a location request.

- Semantics of the service primitive

The primitive parameters are as follows:

MLME-LOCATION.confirm	(
ResultCode,

Peer MAC Address,
Dialog Token,
Management Action Pending,
Location Parameters
)

| Name | Type | Valid Range | Description |
| --- | --- | --- | --- |
| ResultCode | Enumeration | SUCCESS, INVALID PARAMETERS, or UNSPECIFIED FAILURE | Indicates the result of the corresponding MLME-LOCATION.request. |
| Peer MAC Address | MACAddress | Any valid individual MAC Address | The address of the peer MAC entity to which the location response shall be sent. |
| Dialog Token | Integer | 0 – 255 | The dialog token to identify the location transaction. |
| Management Action Pending | Integer | 0 – 255 | The management action pending value indicates if a management action is pending for the STA. |
| Location Parameters | Set of location elements | Set of location elements | A set of location elements describing the location information. See 7.3.2.66. |

- When generated

This primitive is generated by the MLME as a result of the receipt of a Location Response action management frame. This primitive is also generated when the MLME-LOCATION.request contains invalid parameters and when a timeout or failure occurs.

- Effect of receipt

On receipt of this primitive, the SME evaluates the result code.

- MLME-LOCATION.indication

- Function

This primitive indicates that a Location Request frame has been received requesting a location transaction.

- Semantics of the service primitive

The primitive parameters are as follows:

MLME-LOCATION.indication	(
Peer MAC Address,
Dialog Token,
Response Requested,
Location Parameters
)

| Name | Type | Valid Range | Description |
| --- | --- | --- | --- |
| Peer MAC Address | MACAddress | Any valid individual MAC Address or the broadcast MAC address | The address of the peer MAC entity to which the location request shall be sent. |
| Dialog Token | Integer | 0 – 255 | The dialog token to identify the location transaction. |
| Response Requested | Integer | 0 – 255 | The response requested value indicates if a location response message is requested. |
| Location Parameters | Set of location elements | Set of location elements | A set of location elements describing the requested location information. See 7.3.2.66. |

- When generated

This primitive is generated by the MLME when a valid Location Request frame is received.

- Effect of receipt

On receipt of this primitive, the SME either rejects the request or commences the location transaction.

10.3. 50.4 MLME-LOCATION.response

10.3. 50.4.1 Function

This primitive requests the transmission of location information to a peer entity, in response to a received Location Request frame.

10.3. 50.4.2 Semantics of the service primitive

The primitive parameters are as follows:

MLME-LOCATION.response	(
Peer MAC Address,
Dialog Token,
Management Action Pending,
Location Parameters
)

| Name | Type | Valid Range | Description |
| --- | --- | --- | --- |
| Peer MAC Address | MACAddress | Any valid individual MAC Address | The address of the peer MAC entity to which the location request shall be sent. |
| Dialog Token | Integer | 0 – 255 | The dialog token to identify the location transaction. |
| Management Action Pending | Integer | 0 – 255 | The management action pending value indicates if a management action is pending for the STA. |
| Location Parameters | Set of location elements | Set of location elements | A set of location elements describing the STA location information. See 7.3.2.66. |

10.3. 50.4.3 When generated

This primitive is generated by the SME to request that a Location Response frame be sent to a peer entity to convey location information.

10.3. 50.4.4 Effect of receipt

On receipt of this primitive, the MLME constructs a Location Response frame containing the set of location elements specified. This frame is then scheduled for transmission.

.

TGv Editor: Change clause 10.3.52 and 10.3.53 as follows:

- Location Configuration request

This set of primitives supports the exchange of location configuration parameter information between peer SMEs. Location Configuration Request and Response Protocol Exchange depicts the location configuration request process. The figure illustrates the basic protocol and is only an example and therefore is not meant to be exhaustive of all possible protocol uses.

- Location Configuration Request and Response Protocol Exchange

- MLME-LOCATIONCFG.request

- Function

This primitive requests the transmission of location configuration request action frame to a peer entity.

- Semantics of the service primitive

The primitive parameters are as follows:

MLME-LOCATIONCFG.request	(
Peer MAC Address,
Dialog Token,
Location Parameters
)

| Name | Type | Valid Range | Description |
| --- | --- | --- | --- |
| Peer MAC Address | MACAddress | Any valid individual MAC Address | The address of the peer MAC entity to which the location configuration request shall be sent. |
| Dialog Token | Integer | 0 – 255 | The dialog token to identify the location transaction. |
| Location Parameters | Set of location elements | Set of location elements | A set of location elements describing the STA location information. See 7.3.2.66. |

- When generated

This primitive is generated by the SME to request that a Location Configuration Request frame be sent to a peer entity to convey location information.

- Effect of receipt

On receipt of this primitive, the MLME constructs a Location Configuration Request frame containing the set of location elements specified. This frame is then scheduled for transmission.

- MLME-LOCATIONCFG.confirm

- Function

This primitive reports the result of a location configuration request.

- Semantics of the service primitive

The primitive parameters are as follows:

MLME-LOCATIONCFG.confirm	(
Dialog Token,
ResultCode,

Peer MAC Address,
PresenceLocation Parameters
)

| Name | Type | Valid Range | Description |
| --- | --- | --- | --- |
| Dialog Token | Integer | 0 – 255 | The dialog token to identify the location transaction. |
| ResultCode | Enumeration | SUCCESS, INVALID PARAMETERS, or UNSPECIFIED FAILURE | Reports the outcome of a request to send a Location Configuration Request frame. |
| Peer MAC Address | MACAddress | Any valid individual MAC Address | The address of the peer MAC entity to which the location configuration response shall be sent. |
| Location Parameters | Set of location elements | Set of location elements | A set of location elements describing the location information. See 7.3.2.66. |

- When generated

This primitive is generated by the MLME as a result of the receipt of a Location Configuration Response action management frame. This primitive is also generated when the MLME-LOCATIONCFG.request contains invalid parameters and when a timeout or failure occurs.

- Effect of receipt

On receipt of this primitive, the SME evaluates the result code.

- MLME-LOCATIONCFG.indication

- Function

This primitive indicates that a Location Configuration Request frame has been received requesting a location transaction.

- Semantics of the service primitive

The primitive parameters are as follows:

MLME-LOCATIONCFG.indication	(
Peer MAC Address,
Dialog Token,
Location Parameters
)

| Name | Type | Valid Range | Description |
| --- | --- | --- | --- |
| Peer MAC Address | MACAddress | Any valid individual MAC Address | The address of the peer MAC entity to which the location configuration request shall be sent. |
| Dialog Token | Integer | 0 – 255 | The dialog token to identify the location transaction. |
| Location Parameters | Set of location elements | Set of location elements | A set of location elements describing the requested location information. See 7.3.2.66. |

- When generated

This primitive is generated by the MLME when a valid Location Configuration Request frame is received.

- Effect of receipt

On receipt of this primitive, the SME either rejects the request or commences the location transaction.

10.3.52.4 MLME-LOCATIONCFG.response

10.3.52.4.1 Function

This primitive requests the transmission of location information to a peer entity, in response to a received Location Configuration Request frame.

10.3.52.4.2 Semantics of the service primitive

The primitive parameters are as follows:

MLME-LOCATIONCFG.response	(
Peer MAC Address,
Dialog Token,
Location Parameters
)

| Name | Type | Valid Range | Description |
| --- | --- | --- | --- |
| Peer MAC Address | MACAddress | Any valid individual MAC Address | The address of the peer MAC entity to which the location request shall be sent. |
| Dialog Token | Integer | 0 – 255 | The dialog token to identify the location transaction. |
| Location Parameters | Set of location elements | Set of location elements | A set of location elements describing the STA location information. See 7.3.2.66. |

10.3.52.4.3 When generated

This primitive is generated by the SME to request that a Location Configuration Response frame be sent to a peer entity to convey location information.

10.3.52.4.4 Effect of receipt

On receipt of this primitive, the MLME constructs a Location Configuration Response frame containing the set of location elements specified. This frame is then scheduled for transmission.

# Text boxes

Abstract

This document is a normative text proposal to provide comment resolutions for TGv LB108 CID #97. Changes are shown with respect to TGv draft D1.02.

The intent of the document is to use Microsoft Word’s “track changes” from the tools menu to convey the changes to be made.

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart.kerry@philips.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.