IEEE P802.11
Wireless LANs

| MLME-JOIN.xxxx in WAVE mode |
| --- |
| Date: 2007-11-09 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Francois Simon | ARINC / USDOT | ARINC, Inc. 2551 Riva Road Annapolis MD | 410-266-4531 | fsimon@arinc.com |

Background

In April / May 2007 time frame – P802.11p/D2.0 there was an amendement specifying specific JOIN primitives for WAVE: MLME-WAJOIN.request and MLME-WAJOIN.confirm.  At the Montreal meeting, when a decision was made to replace the Action frame by a Beacon to annonce the WBSS (see Doc.: IEEE 802.11 11-07-0781-02-000P), the motion included the removal of the MLME-WAJOIN.xxxx primitives and use the 802.11 base standard MLME-JOIN.xxx primitives: “Remove MLME-WAJOIN.xxx and modify MLME-JOIN.xxx (if required)”. Doing so, we ended up with the logic described below:

Current logical specification in P802.11p D3.0

/* 10.3.3.1.2	 MLME-JOIN.request*/

if dot11WAVEServicesEnabled = false then  /* 802.11 Std-2007 procedure*/

The primitive parameters are as follow:

MLME-JOIN.request (

SelectedBSS,

JoinFailureTimeout,

ProbeDelay,

OperationalRateSet,

VendorSpecificInfo

)

else  /*P802.11p/D3.0*/

The primitive parameters are as follow:

MLME-JOIN.request (

BSSID,

SSID,

OperationalRateSet,

LocalTime,

EDCA parameter set

)

endif

/*10.3.3.2.2	MLME-JOIN.confirm*/

if dot11WAVEServicesEnabled = false then /* 802.11 Std-2007 procedure*/

The primitive paraneters are as follow:

MLME-JOIN.confirm (

ResultCode,

VendorSpecificInfo,

)

else /*P802.11p/D3.0*/

The primitive parameter is as follow:

MLME-JOIN.comfirm (

ResultCode

)

endif

Issue

The way P802.11p/D3.0 is specified, from the standard viewpoint, any 802.11 STA has to test the dot11WAVEServicesEnabled MIB attribute to find out which of the two alternative paths to take for MLME-JOIN.request  and MLME-JOIN.confirm primitive.  This behaviour prompted the following LB110 CIDs: 278, 279, 282, and 285.

References:

# Text boxes

Abstract

FOR DISCUSSION PURPOSES ONLY

The purpose of this discussion is to find an alternative to the MLME-JOIN.xxxx primitives in WAVE mode.  It addresses in particular LB 110, CID# 278, 279, 282, and 285.  Other CIDs are indirectly affected by the current specification.