IEEE P802.11
Wireless LANs

| On-demand beacon without a WSIE |
| --- |
| Date: 2007-11-09 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Francois Simon | ARINC / USDOT | ARINC, Inc. 2551 Riva Road Annapolis MD | 410-266-4531 | fsimon@arinc.com |

Issue

As P802.11p/D3.0 is today, the original issue first came to mind when one asks the question: “How does a WAVE STA receiving an On-demand beacon without a WSIE recognizes it is a WAVE On-demand beacon?  The answer is: it does not.  The remainder of the discussion tries to answer the question: “does it care?”.  As we look further in to this question, one starts to ask questions about legacy* receivers, non-WAVE receivers with On-demand beacon capability, and WAVE receivers.  How remote the possibilities are, we cannot discard the interoperability occurrences within the standard.

Note: (*) For the purpose of this discussion, a ‘Legacy’ STA is an STA that does not have knowledge of the Extended Capabilities IE (ECIE).

| ID | Name | Cls. | Pg. | Ln. | Ye | Comment | Suggested Remedy |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 357 | Hamilton, Mark | 10.3.37.3.3 | 17 | 3 | TR | MLME-ONDEMANDBEACON.indication is generated when a WAVE Advertisement frame is received. But (as noted in earlier comment), there is no way to tell a WAVE Advertisement frame from a "traditional" Beacon frame. | Either use a new frame type for WAVE Advertisement frames, or remove this primitive and use the traditional Beacon primitive (with support for WSIE added). |

| ID | Transmiter | Receiver | Comments |
| --- | --- | --- | --- |
| 1 | Legacy | Legacy | Non WAVE mode Issue - 802.11 Std procedure applies (regular beacon) |
| 2 | Legacy | Non-WAVE STA | Non WAVE mode Issue - Receiver does not see the ECIE. It may use the timing and Country information within the beacon |
| 3 | Legacy | WAVE STA | WAVE mode Issue - Receiver does not see the ECIE. It may use the timing and Country information within the beacon |
| 4 | Non-WAVE with On-demand bit =1 | Legacy | Non WAVE mode Issue - Receiver does not see the ECIE., it may receive the beacon unexpectedly (timing). It may use the timing and Country information within the beacon. |
| 5 | Non-WAVE with On-demand bit = 0 | legacy | Non WAVE mode Issue - Transmitter may be capable of allowing regular beacon. 802.11 Std procedure applies |
| 6 | Non-WAVE with On-demand bit = 1 | Non-WAVE | Non WAVE mode Issue Appropriate procedures apply for the two non-WAVE STAs. |
| 7 | Non-WAVE with On-demand bit = 0 | Non-WAVE | Non WAVE mode Issue - Appropriate procedures apply for the two non-WAVE STA when On-demand bit = 0; It may use the timing and Country information within the beacon. |
| 8 | Non-WAVE with On-demand bit = 0 | WAVE | WAVE mode Issue - For the WAVE receiver, it is not an On-demand beacon. It may use the timing and Country information within the beacon. |
| 9 | Non-WAVE with On-demand bit = 1 | WAVE | WAVE mode Issue - For the WAVE receiver it is an On-demand beacon. It may use the timing and Country information within the beacon. |
| 10 | WAVE with On-demand bit = 0 | Legacy | WAVE mode Issue - Should not happen for a WAVE transmitter. However, the receiver does not see the ECIE. It may receive the beacon unexpectedly (timing).It may use the timing and Country information within the beacon |
| 11 | WAVE with On-demand bit = 1 | Legacy | WAVE mode Issue - Receiver does not see the ECIE. it may receive the beacon unexpectedly (timing). It may use the timing and Country information within the beacon |
| 12 | WAVE with On-demand bit = 0 | Non-WAVE | WAVE mode Issue - Should not happen for a WAVE transmitter. It may use the timing and Country information within the beacon |
| 13 | WAVE with On-demand bit = 1 | Non-Wave | WAVE mode Issue - Receiver interprets as an on-demand beacon. It assumes it would use the timing and Country information within the beacon |
| 14 | WAVE with On-demand bit = 0 | WAVE | WAVE mode Issue - Should not happen for a WAVE transmitter. It may use the timing and Country information within the beacon anyway. |
| 15 | WAVE with On-demand bit = 1 | WAVE | WAVE mode Issue - Receiver interprets as an on-demand beacon. It assumes it would use the timing and Country information within the beacon |

Proposed Solution:

One may make a risky proposition by stating that any beacon without a WSIE received by a WAVE STA fulfills the requirement to provide timing and country information to the WAVE STA receiver, if it needs it.  If this is the case, the answer to: “How does a WAVE STA receiving an On-demand beacon without a WSIE recognizes it as a WAVE On-demand beacon?”  The answer is still “It does not”.  Answering the second question: Does a WAVE STA receiver care how it gets the information it needs when a WSIE is not required? The answer is “it does not care.”

If this proposition is true, there is no change in P802.11p/D3.0 required concerning this issue.

.

Decision: ?

# Text boxes

Abstract

FOR DISCUSSION PURPOSES ONLY

The purpose of this discussion is to analyze the effect on a WAVE & non-WAVE 802.11 STA receiving an On-demand beacon without a WSIE information element.  Note because of its nature, an On-demand beacon transmitted with or without a WSIE is the subject of a separate discussion.  The discussion here addresses, in particular, LB110 CID# 357 and has been raised by several members of TGp and dicussed in the 10/08/07 ad-hoc meeting.