IEEE P802.11
Wireless LANs

| TGp LB 110 Annex J Comment Resolution |
| --- |
| Date: 2007-11-10 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Alastair Malarky | Mark IV | 6030 Ambler Drive, Mississauga, Ontarion, Canada L4W 2P1 | 905-624-3020 | amaalrky@ivhs.com |

|  | LB110 Comment Resolution |
| --- | --- |

- COMMENTS:

| ID | Commenter | Clause | Pg | Ln | E or T | Yes or No | Comment | Suggested Remedy |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 526 | Roy, Richard | Annexes I and J | 28 | 30 | TR | The European frequency and channel allocations specified in previous submissions are still missing. | Add the European channelization and freq1uency allocations to the annexes as proposed in previous submission 11-07-2228-00-000p-regulatory-language-change.doc. |
| 538 | Rai, Vinuth | Annex J | 33 | 45 | TR | 11p document should support the use of 5MHz Channels. This would allow WAVE radios to allow for communication within this 5MHz channel within the DSRC spectrum.For eg: The presence of 5 MHz channels will allow for a longer channel time span therefore facilitating longer intersymbol times. This is help reduce intersymbol interference and improve SNR | Insert row in table J.1. With the following entries Regulatory Channel: <ANA>, Channel Starting Frequency: 5Ghz, Channel Spacing 5Mhz, and channel set: 171-185. The remainder of the row can be filled as appropriate. Also add a footnote corresponding to this entry indicating that the FCC currently does not allow for 5Mhz |
| 539 | Kavner, Doug | Table J.1 | 33 | 46 | T | Regulatory classes 12 & 13 have the same EIRP. Per note 2, class 12 should have a lower EIRP. | Change class 12 to 100 mW |

- Background, Explanation, Discussion, etc.:

With respect to 526, a European regulation (ETS 300-328) was added to the ISM band by 11-06-1825.  This was inadvertently omitted in the instructions in the last 11p proposal.  The instructions should have included the fact that Europe entry was also changed.

The frequency allocation changes proposed in 11-07-0228 are inconsistent with the current regulations and are declined, see response to 538

With respect to comment 538 and 526, and the frequency allocation changes proposed in 11-07-022, there is no regulation currently permitting 5 MHz channels or 40 MHz channel.  Annex J is a regulatory section and should only include items for which regulations apply.  Regulatory sections are those to which all devices must comply in the regulatory domain within which they operate, not a section to introduce wishes.

Comment 539 correctly identifies that there is an error in the table.

- Recommended Resolution of the Comment:

| ID | Resolution |
| --- | --- |
| 526 | Counter - see resolution proposed in 11-07-2653-01-000p-tgp-lb-110-comment-resolution-for-annex-i.doc |
| 538 | Declined. Annex J is by definition a documentation of approved regulations, not a place to introduce a wish list. |
| 539 | Declined. The table does not list EIRP but rather output power (at the antenna input). The same output power is permitted in both cases but the EIRPs limits are different. |

- Motion (if technical and/or significant):

(And instructions to the editor.)

Move to decline comments 538 and 539 accept suggested remedies for comment 526.

Motion by: ____________________Date: _________________

Second:  ______________________

| Approve: | Disapprove: | Abstain: |
| --- | --- | --- |

References:

# Text boxes

Abstract

This document proposes resolutions for letter ballot 110 comments 526, 538 and 539 which pertain to Annex J of the Draft P802.11p_D3.0 submission.  The document also proposes a motion to accept the resolutions.