IEEE P802.11
Wireless LANs

| TGp LB 110 Annex J Comment Resolution |
| --- |
| Date: 2007-11-10 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Alastair Malarky | Mark IV | 6030 Ambler Drive, Mississauga, Ontario, Canada L4W 2P1 | 905-624-3020 | amalarky@ivhs.com |

|  | LB110 Comment Resolution |
| --- | --- |

- COMMENTS:

| ID | Commenter | Clause | Pg | Ln | E or T | Yes or No | Comment | Suggested Remedy |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 526 | Roy, Richard | Annexes I and J | 28 | 30 | TR | The European frequency and channel allocations specified in previous submissions are still missing. | Add the European channelization and frequency allocations to the annexes as proposed in previous submission 11-07-2228-00-000p-regulatory-language-change.doc. |
| 538 | Rai, Vinuth | Annex J | 33 | 45 | TR | 11p document should support the use of 5MHz Channels. This would allow WAVE radios to allow for communication within this 5MHz channel within the DSRC spectrum.For eg: The presence of 5 MHz channels will allow for a longer channel time span therefore facilitating longer intersymbol times. This is help reduce intersymbol interference and improve SNR | Insert row in table J.1. With the following entries Regulatory Channel: <ANA>, Channel Starting Frequency: 5Ghz, Channel Spacing 5Mhz, and channel set: 171-185. The remainder of the row can be filled as appropriate. Also add a footnote corresponding to this entry indicating that the FCC currently does not allow for 5Mhz |
| 539 | Kavner, Doug | Table J.1 | 33 | 46 | T | Regulatory classes 12 & 13 have the same EIRP. Per note 2, class 12 should have a lower EIRP. | Change class 12 to 100 mW |

- Background, Explanation, Discussion, etc.:

With respect to 526, a European regulation (ETS 300-328) was added to the ISM band by IEEE 802.11-06/1825.  This was inadvertently omitted in the instructions in the last 11p proposal.  The instructions should have included the fact that the Europe entry was also changed in tables I-1 and I-2.

The frequency allocation changes proposed in IEEE 802.11-07/0228 are inconsistent with the current regulations and are declined; see response to 538.

With respect to comment 538 and 526, and the frequency allocation changes proposed in IEEE 802.11-07/0228, there is no regulation currently permitting 5 MHz channels or 40 MHz channels for these bands.  Annex J is a regulatory section and should only include items for which regulations apply.  Regulatory sections are those to which all devices must comply in the regulatory domain within which they operate, not a section to introduce wishes.

Comment 539 misatakes EIRP with output power.  The FCC permits a fixed maximum output power of 28.8 dBm (760 mW) at the antenna port, however the antenna gain can be higher for Class 13 for the same transmit power.

- Recommended Resolution of the Comment:

| ID | Resolution |
| --- | --- |
| 526 | Counter - see resolution proposed in 11-07-2653-01-000p-tgp-lb-110-comment-resolution-for-annex-i.doc |
| 538 | Declined. Annex J is by definition a documentation of approved regulations, not a place to introduce a wish list. |
| 539 | Declined. The table does not list EIRP but rather output power (at the antenna input). The same output power is permitted in both cases but the EIRPs limits are different. |

- Motion (if technical and/or significant):

(And instructions to the editor.)

Move to decline comments 538 and 539 and to accept counter to 526 to only modify instructions to include the Europe entry in Tables I-1 and I-2, and instruct the editor to make these changes to P802.11p D3.0.

Motion by: ____________________Date: _________________

Second:  ______________________

| Approve: | Disapprove: | Abstain: |
| --- | --- | --- |

References:

# Text boxes

Abstract

This document proposes resolutions for letter ballot 110 comments 526, 538 and 539 which pertain to Annex J of the Draft P802.11p_D3.0 submission.  The document also proposes a motion to accept the resolutions.