IEEE P802.11
Wireless LANs

| Proposed resolutions to CID 799 and CID 1545 |
| --- |
| Date: 2007-07-14 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |

In section 11.20.1, modify the paragraph as indicated:

A non-AP STA that supports Multicast Diagnostic Reporting supporting Wireless Network Management Capability element shall set the Multicast Diagnostic capability bit in the Wireless Network Management Capabilities element to 1 if it supports multicast diagnostic reporting. A non-AP STA supporting Wireless Network Management Capability element shall set the Multicast Diagnostic capability bit in the Wireless Network Management Capabilities element to 0 if it does not support multicast diagnostic reporting..

Add to the end of section 11.20.1, add the following paragraph:

A station that declines a request for triggered multicast diagnostic reporting shall send a Measurement Report element (as described in 7.3.2.22) in a Measurement Report frame (as described in 7.4.1.2) with the Measurement Report Mode field set appropriately to indicate the reason for a failed or rejected request.

References:

# Text boxes

Abstract

This document contains a proposed resolution to CID 799 and 1545 from LB108.

Comment 1545: “Need to add a mechanism to allow the STA to refuse a multicast diagnostic measurement request at a particular time due to the lack of resource.”

Comment 799: "Replace the sentence ‘A non-AP STA that supports Multicast Diagnostic Reporting shall set the Multicast Diagnostic capability bit in the Wireless Network Management Capabilities element to 1.’ with ‘A non-AP STA supporting Wireless Network Management Capability element shall set the Multicast Diagnostic capability bit in the Wireless Network Management Capabilities element to 1.’."