IEEE P802.11
Wireless LANs

| 3-Address Mesh Broadcast Frames |
| --- |
| Date: 2008-11-10 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Javier Cardona | cozybit Inc. | 165 Jessie St., San Francisco, CA 94105 | +1-415-974-6770 | javier@cozybit.com |
| Raja Bannerjea Ronak Chokshi | Marvell Semiconductor | 5488 Marvell Lane, Santa Clara, CA 94087 | +1-408-222-3713 | rajab@marvell.com rchokshi@marvell.com |
| Sandesh Goel | Marvell India Pvt Ltd | 6th Floor, Muttha Towers, Off Airport Road, Pune, India - 411006 | +91-99605-96612 | sgoel@marvell.com |
| Bilel Jamoussi Bob Withrow | Nortel Networks | 600 Technology Park Billerica, MA 01821 | +1-978-288-4566 | jamoussi@nortel.com bwithrow@nortel.com |
| Osama Aboul-Magd | Nortel Networks | 3500 Carling Avenue Ottawa, ONT, Canada K2H-8E9 | +1-613-763-5827 | osama@nortel.com |
| Guido R. Hiertz | Philips | ComNets, Dept. of Communication Networks, RWTH Aachen University, Kopernikusstr. 5, 52074 Aachen, Germany | +49-241-802-5829 | hiertz@ieee.org |
| Thomas Kuehnel | Microsoft Corp. | One Microsoft Way, Redmond, WA 98052 | +1-425-7064351 | tkuehnel@microsoft.com |

Change second row of Table s2 as follows:

| 01 | Mesh Address Extension field contains Addr4 | 6 | Management (Multihop Action) Proxied Group Addressed Data |
| --- | --- | --- | --- |

Change Table s52 as follows:

| Supported Frames | FromDS ToDS bits | Address Extension Mode value (binary) | Address 1 | Address 2 | Address 3 | Address 4 | Address 5 | Address 6 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Mesh Individually Addressed Data | 11 | 00 | RA | TA | DA = Mesh DA | SA = Mesh SA | Not Present | Not Present |
| Mesh Group Addressed Data | 10 | 00 | DA | TA | SA=Mesh SA | Not Present | Not Present | Not Present |
| Multihop Action | 00 | 01 | RA | TA | DA = Mesh DA | SA = Mesh SA | Not Present | Not Present |
| Mesh Individually Addressed Data | 11 | 10 | RA | TA | Mesh DA | Mesh SA | DA | SA |
| Mesh Group Addressed Data | 101 | 01 | DA | TA | Mesh SA | SA | Not Present | Not Present |
| Multihop Action | 00 | 11 | RA | TA | Mesh DA | Mesh SA | DA | SA |

Change 11B.6.5.3 as follows:

11B.6.5.3 Addressing and Forwarding of Broadcast Frames

11B.6.5.3.1 At Source mesh STAs

A mesh STA that is the source of a group addressed frame shall use a 3 address group addressed frame or a 4 address individually addressed (fully acknowledged broadcast).

In the case of 3 address broadcast frames, the Source mesh STA shall set the Address 3 field to the group  address and the Address 2 and Address 3 fields to its own MAC address.  The Source mesh STA shall also set the ToDS bit to zero and the FromDS bit to one on the Frame Control field.

If the frame is originally received by a mesh STA from proxied entities with a group address in the Address 1 (RA/DA) field the Source mesh STA shall enable Mesh Address Extension by setting the Address Extension Mode to 01 and Address 4 to the address of the proxied entity.  It shall set the Address 1 field to the group address and the Address 2 and Address 3 fields to its own MAC address.

The Source mesh STA shall set the TTL field in the Mesh Header to dot11MeshTTL in order to control the hop count. For example, if the TTL field is set to 1, frames are delivered to immediate neighbors only. Otherwise, the frames are forwarded multiple hops, limited by the TTL value.

The Source mesh STA shall set the Mesh Sequence Number field in the Mesh Header to a value from a single modulo-65536 counter that is incrementing by 1 for each new frame.

Procedures which enhance the reliability or efficiency of group addressed transmissions are outside

the scope of this standard.

11B.6.5.3.2 At Intermediate and destination Mesh STAs

On receipt of a frame with Address 1 (RA) set to its MAC address or a group address and with Address 3 (DA/Mesh DA) set to a groupaddress, a mesh STA deciphers the frame and checks for authenticity. If it is not from a peer mesh STA, the frame shall be silently discarded. Otherwise, it shall be further processed as follows.

The tuple of Address 4 (SA/Mesh SA) and Mesh Sequence Number from the Mesh Header shall be used as a unique message signature for tracking group addressed frames. The Mesh SA corresponds to Address 3 in 3 address group addressed frames and to Address 4 in 4 address fully acknowledged group addressed frames.  The mesh STA checks whether the frame has previously been received. If this is the case, the frame shall be discarded. Otherwise, the mesh STA shall retain the signature and continues processing the frame.

The mesh STA then decrements the TTL field in the Mesh Header field. If the TTL value has reached zero, the message shall not be forwarded to other mesh STAs. If the TTL value has not reached zero and if the dot1MeshForwarding is set to 1, the mesh STA sets the TA field (Address 2) to its own MAC address and the frame is queued for transmission to neighbor peer mesh STAs in order to propagate this group addressed frame throughout the MBSS. The transmission procedure of the group addressed frame is as described in the previous subclause.

If the mesh STA is a proxy mesh STA, the mesh STA shall transmit the frame to all its proxied entities outside the boundary of the mesh after translating the frame to the appropriate frame formats for proxied entities.

Note that during the forwarding process at intermediate mesh STAs, the contents of the frame body are not changed.

Delete 11B.6.5.4

References:  IEEE 802.11-08/0278r5 “Avoiding Interactions with Lazy WDS equipment”

# Footnotes

NOTE— The reason for not using four-address MAC header format for group addressed traffic is to avoid interactions with existing implementations.  Earlier versions of this standard defined the four-address MAC header format (previously called WDS format) without defining procedures for its use.  As a result there is a large number of deployed devices that use the four-address frame format in ways that would affect and be affected by mesh traffic if four-address group addressed frames were to be used.

# Text boxes

Abstract

The use of 3 address frame format for mesh broadcast frames is proposed.  This avoids interactions with legacy equipment (Lazy-WDS) and makes a more efficient use of 802.11 header addresses.  The revision r2 of this document has been updated to draft 802.11s/D2.02 and any changes adopted during the September 2008 meeting.