IEEE P802.11
Wireless LANs

| TGz Draft 1.0 LB127 CID 229-372 (8.5.9.x) |
| --- |
| Date: May 8, 2008 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Menzo Wentink | Qualcomm | Straatweg 66, Breukelen, the Netherlands | +31-65-183-6231 | mwentink@qualcomm.com |

Abstract

This document addresses TGz LB127 CID 229-372, which relate to subclause 8.5.9.x.

Instruction to the editor: Accept changes and replace subclauses as shown.

Replace 8.5.9.x with the following:

8.5.9 TDLS Peer Key Handshake

The TDLS Peer Key Handshake occurs after any other direct link setup procedures and is used to create an STKSA providing data confidentiality between the two STAs. The AP must establish an RSNA with each STA prior to PeerKey setup. The initiator STA starts the PeerKey Handshake, providing the key to use for securing the connection.

The TDLS Peer Key EAPOL-Key exchange provides a mechanism for obtaining the keys to be used for direct STA-to-STA communication. The initiator STA shall start a timer when it sends the first EAPOL-Key message and the peer STA shall do the same on receipt of the first EAPOL-Key message. On expiration of this timer, the STA shall transition to the STKINIT state.

A STA should use the TDLS Peer Key Handshake prior to transferring any direct STA-to-STA data frames. The STKSA should be deleted when the STA to STA connection is terminated.

The following assumptions apply:

- FTIE denotes an Fast BSS Transition information element as specified in Clause 7.3.2.46 of 802.11r-D7.0.

- STA_I is the initiator STA

- STA_P is the peer STA

- AP is the access point with which both the STA_I and the STA_P are associated

- MAC_I is the MAC address of STA_I

- MAC_P is the MAC address of STA_I

- INonce is the nonce generated by STA_I

- PNonce is the nonce generated by STA_P

- DH_I is the public value of STA_I

- DH_P is the public value of STA_P

The TDLS Peer Key Handshake has two components:

- SMK Handshake: This handshake is initiated by the initiator STA and, as a result of this handshake, the SMKSA is installed in both the STAs. This message exchange goes through the AP and is protected using the PTK.

- 4-Way STK Handshake: Using the installed SMKSA, the initiator STA initiates the 4-Way Handshake (as per 8.5.3.4) and, as a result of this, the STKSA gets installed in both the STAs. The STKSA is used for securing data exchange between the initiator STA and the peer STA. This message exchange goes directly between the peer STAs.

8.5.9.1 SMK Handshake

The Initiator STA initiates the SMK Handshake by sending first message to the Peer STA through the AP path. This is done to establish a SMKSA between Imitator and Peer STA associated with the same AP. Unlike the 4-Way Handshake and Group Key Handshake, the SMK Handshake is initiated by the initiator STA.

For SMK Handshake, the modulus p shall be 1536 bits (as per RFC 3526) in length and the generating element g shall be 2.

The prime is: 2^1536 - 2^1472 - 1 + 2^64 * { [2^1406 pi] + 741804 }. Its hexadecimal value is:

FFFFFFFF FFFFFFFF C90FDAA2 2168C234 C4C6628B 80DC1CD1

29024E08 8A67CC74 020BBEA6 3B139B22 514A0879 8E3404DD

EF9519B3 CD3A431B 302B0A6D F25F1437 4FE1356D 6D51C245

E485B576 625E7EC6 F44C42E9 A637ED6B 0BFF5CB6 F406B7ED

EE386BFB 5A899FA5 AE9F2411 7C4B1FE6 49286651 ECE45B3D

C2007CB8 A163BF05 98DA4836 1C55D39A 69163FA8 FD24CF5F

83655D23 DCA3AD96 1C62F356 208552BB 9ED52907 7096966D

670C354E 4ABC9804 F1746C08 CA237327 FFFFFFFF FFFFFFFF

The information flow of the SMK handshake is as follows:

SMK Message 1:	Initiator STA → Peer STA

RSNIE_I, FTIE(0, 0, 0, INonce, MAC_I, BSSID, Lifetime, DH_I)

SMK Message 2:	Peer STA → Initiator STA

RSNIE_P, FTIE(7, MIC, PNonce, INonce, MAC_I, MAC_P, BSSID, Lifetime, DH_P)

SMK Message 3:	Initiator STA → Peer STA

RSNIE_I, FTIE(4, MIC, PNonce, INonce, MAC_I, MAC_P, BSSID, Lifetime, DH_I)

8.5.9.1.1 SMK Handshake Message 1

The Initiator STA performs following steps before generating Message 1:

- Create RSNIE by filling the element id (fixed hex 30), length, version (1), and pairwise cipher suite list field. Since group cipher suit field is before pairwise cipher suite list field (so STA needs to fill it), STA shall fill this field with any value and on the other side STA processing this field shall ignore it.

- Generate 256 bit random number which is sent in Key Nonce field.

- Decides on lifetime of SMKSA, which is sent as part of Lifetime.

- Initiator STA selects a random integer A < p and computes public DH_I = gA mod p.

The initiator STA sends Message 1 to the peer STA P through AP. After sending the message 1, the Initiator STA starts a timer (different from the Lifetime-Timer) and waits for response message from the Peer STA.

On receipt of Message 1, the peer STA performs following actions:

- Verify the initiator MAC address against existing direct link. If no direct link exists, it silently discards the message.

- If all checks succeed,

  - Generate 256 bit random number which is sent in Key Nonce field.

  - Check the suggested lifetime value proposed by initiator STA. If needed select a smaller lifetime value or use the same lifetime value to create the Lifetime to be used in message 2.

  - Peer STA selects a random integer B < p and computes public DH_P = gB mod p.

  - Peer STA computes the SMK as

SMK-Key-Data = KDF-384(SHA-256(DH_IB mod p), "SMK Key Derivation", BSSID || MAC_I || MAC_P || INonce || PNonce)

SMK-KCK = L(SMK-Key-Data, 0, 128)

SMK = L(SMK-Key-Data, 128, 256)

where

—   KDF-384 is the KDF function as defined in 8.5.1.5.2 used to generate a key of length 384 bits.

—   L(-) is defined in 8.5.1.

—   "SMK Key Derivation" is 0x534d4b204b65792044657269766174696f6e.

—   BSSID is the basic service set identification as defined in 7.1.3.3.3.

  - Peer STA selects one of the ciphersuites from the ciphersuite list in the initiator RSNIE and creates peer RSNIE.

- Using all the information, peer STA creates Message 2 and sends it to initiator STA through AP.

8.5.9.1.2 SMK Handshake Message 2

The peer STA sends Message 2 to the initiator STA through the AP path. After sending Message 2, the Peer STA starts a timer (different from the Lifetime-Timer) and waits for response message from the Initiating STA.

On receipt of Message 2, the Initiator STA performs the following actions:

- Verify the Peer MAC address against existing direct link. If no direct link exists, it silently discards the message.

- Verify the Initiator MAC address and INonce from the FTIE and if it does not match, the Initiator STA silently discards the message.

- If all checks succeed,

  - The Initiator STA computes the SMK as

SMK-Key-Data = KDF-384(SHA-256(DH_PA mod p), "SMK Key Derivation", BSSID || MAC_I || MAC_P || INonce || PNonce)

SMK-KCK = L(SMK-Key-Data, 0, 128)

SMK = L(SMK-Key-Data, 128, 256)

- Verify the MIC on Message 2.  If the MIC verification fails, the Initiator STA silently discards the message. The MIC shall be calculated using the SMK-KCK and the AES-128-CMAC algorithm. The output of the AES-128-CMAC shall be 128 bits. The MIC shall be calculated on the concatenation, in the following order, of:

- MAC_I

- MAC_P

- BSSID

- RSNIE_P

- PNonce

- INonce

- Lifetime

- DH_P

- If the MIC verification succeeds,  the Initiator STA creates Message 3 and sends it to the Peer STA through the AP path.

8.5.9.1.3 SMK Handshake Message 3

The Initiator STA sends Message 3 to the Peer STA through the AP path. After sending Message 3, the SMK handshake is complete from initiator STA side.

On reception of Message 3, the peer STA performs following actions:

- Verify the Initiator MAC address against existing direct link. If no direct link exists, silently discard the message.

- Verify the Peer MAC address and PNonce from the FTIE and if either does not match, silently discard the message.

- Verify the MIC on Message 3.  If the MIC verification fails, the Peer STA silently discards the message. . The MIC shall be calculated using the SMK-KCK and the AES-128-CMAC algorithm. The output of the AES-128-CMAC shall be 128 bits. The MIC shall be calculated on the concatenation, in the following order, of:

- MAC_I

- MAC_P

- BSSID

- RSNIE_I

- PNonce

- INonce

- Lifetime

- DH_I

- If all checks succeed, the SMK handshake is complete from the Peer STA side.

8.5.9.2 SMK handshake error conditions

If the STA_P does not receive a valid SMK Message 3 or a 4-Way STK Message 1 after sending the EAPOL request message to initiate the TDLS Peer Key rekey within a 2000 millisecond timeout, the STA_P shall invoke a direct link teardown procedure.

If the STA_I does not receive an SMK Message 2 from the STA_P, the STA_I shall attempt dot11RSNAConfigSMKUpdateCount transmits of the SMK Handshake Message 1 plus a final timeout. If the STA_I still has not received a response after these retries, it shall invoke a direct link teardown procedure. The retransmit timeout value shall be 2000 milliseconds for the first timeout, the listen interval for the second timeout, and twice the listen interval for subsequent timeouts. If there is no listen interval, then 200 milliseconds shall be used for all timeout values.

Upon receipt of the SMK Message 3, the STA_I will transmit Message 1 of the 4-Way STK Handshake to the STA_P. If the STA_I does not receive Message 2 of the 4-Way STK Handshake from the STA_P, it shall attempt dot11RSNAConfigSMKUpdateCount transmits of 4-Way STK Handshake Message 1, plus a final timeout. If STA_I still has not received a response after these retries, it shall invoke a direct link teardown procedure. The retransmit timeout value shall be 1000 milliseconds for the first timeout, half the listen interval for the second timeout, and the listen interval for subsequent timeouts. If there is no listen interval, then 1000 milliseconds shall be used for all timeout values.

8.5.9.3 STKSA rekeying

Rekeying is always initiated by the STA_I. When needed, the STA_P sends an EAPOL request message to the STA_I to request rekeying. The STA_P shall wait a minimum of one half the IEEE 802.1X timeout after the STSL setup before initiating a TDLS Peer Key rekey procedure. To perform rekeying, there are two cases:

1) If the SMK timer has not expired, the STAs will initiate a 4-Way Handshake to create a new STK. The 4-Way Handshake is always initiated by STA_I. In this case, STA_P should not delete any existing STKSA prior to verifying Message 3 of the 4-Way Handshake with STA_I for this session.

2) If the SMK has expired, STA_I shall not use an existing STKSA and shall start the SMK Handshake followed by a 4-Way Handshake to create new keys.

The format of the EAPOL-Key request message in case 1 from STA_P to STA_I is as follows:

Request Message:	STA_P → STA_I

EAPOL-Key(1,1,0,0,1,0,0,0, MIC, PMKID KDE)

The request message uses the following values for each of the EAPOL-Key frame fields:

Descriptor Type = N - see 8.5.2

Key Information:

Key Descriptor Version = 1 (RC4 encryption with HMAC-MD5) or 2 (NIST AES key wrap with HMAC-SHA1-128)

Key Type = 1 (PTK)

SMK Message = 0

Install = 0

Key Ack = 0

Key MIC = 1

Secure = 1

Error = 0

Request = 1

Encrypted Key Data = 0

Reserved = 0

Key Length = 0

Key Replay Counter = request replay counter of peer STA

Key Nonce = 0

EAPOL-Key IV = 0

Key RSC = 0

Key MIC = MIC computed over the body of this EAPOL-Key frame

Key Data Length = Length of Key Data field in octets

Key Data = SMKID in SMKID KDE

8.5.9.4 Error Reporting

Error reporting messages are defined in this sub-clause and used to report errors whenever STAs detect an error during the SMK Handshake.

The STA, upon receipt of the error messages defined in this sub-clause, shall tear down the direct link with the other STA and clear all the TDLS Peer Key states.

The format of EAPOL-Key request message for reporting an error message is as follows:

Error Message: EAPOL-Key(1,1,0,0,0,1,0, 0, MIC, Error KDE, MAC Address KDE).

The request message uses the following values for each of the EAPOL-Key frame fields:

Descriptor Type = N - see 8.5.2

Key Information:

Key Descriptor Version = 1 (RC4 encryption with HMAC-MD5) or 2 (NIST AES key wrap with HMAC-SHA1-128)

Key Type = 0 (Group/SMK)

SMK Message = 1 (SMK)

Install = 0

Key Ack = 0

Key MIC = 1

Secure = 1

Error = 1

Request = 1

Encrypted Key Data = 0

Reserved = 0

Key Length = 0

Key Replay Counter = request EAPOL replay counter

Key Nonce = 0

EAPOL-Key IV = 0

Key RSC = 0

Key MIC = MIC computed over the body of this EAPOL-Key frame

Key Data Length = Length of Key Data field in octets

Key Data = Error KDE (different types defined in Table 64), MAC Address KDE

8.5.9.4.1 Error ERR_CPHR_NS

This error message is sent whenever a STA finds that it does not support any of the ciphersuites proposed by the other STA. In response to this error, the STA creates an Error KDE with error type ERR_CPHR_NS and sends the message back to the other STA. The MAC address KDE contains the MAC address of the other

STA.

8.5.8.4.4 Error ERR_NO_STSL

This error message is sent whenever a STA finds that it does not have an existing direct link with the other STA. In response of this error, the STA creates an Error KDE with error type ERR_NO_STSL and sends the message back to the other STA. The MAC address KDE contains the MAC address of the other STA.

| 229 | Liwen | Chu | 8 | 21 | 6 | T |  | When two TDLS peer STAs set up security association and enter power saving mode using the AP path, one way to keep security is that they use normal data frames to encapsulate the encrypted frames by TDLS key. The AP does not need to decrypt and encrypt the data frames. | Modify the draft to allow this TDLS peer security. |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 230 | Jesse | Walker | 8.5.8.1.3 | 24 | 28 | T | Y | The Peer also needs to verify INonce, KeyId, and Lifetime fields | In the comment |  |
| 231 | Adrian | Stephens | 8.5.9 |  |  | T | Y | "The TDLS Peer Key EAPOL-Key exchange provides a mechanism for obtaining the keys to be used for direct STA-to-STA communication. The initiator STA shall start a timer when it sends the first EAPOL-Key message and the peer STA shall do the same on receipt of the first EAPOL-Key message. On expiration of this timer, the STA shall transition to the STKINIT state." 1. Where is the value of this timer specified? 2. What is the STKINIT state, and which state machine enters this state? | Define the value of this time - perhaps by reference to a MIB variable. Reference the state machine description which includes this state. |  |
| 232 | Adrian | Stephens | 8.5.9 |  |  | T | Y | "A STA should use the TDLS Peer Key Handshake prior to transferring any direct STA-to-STA data frames. The STKSA should be deleted when the STA to STA connection is terminated." This is over general. | 1. Exclude the normal DLS case. 2. Exclude the case when one or more of the AP and both STAs do not support RSN. |  |
| 233 | Bill | Marshall | 8.5.9 | 21 | 14 | T | y | initiator is not starting a PeerKey handshake, its starting a TDLS PeerKey handshake | change "starts the PeerKey Handshake" to "starts the TDLS PeerKey Handshake" |  |
| 234 | Bill | Marshall | 8.5.9 | 21 | 25 | T | y | these are not assumptions, they are just notation | change line to "The following notation is used in the TDLS PeerKey description:" |  |
| 235 | Bill | Marshall | 8.5.9 | 21 | 27 | T | y | as the time of the approval of this amendment, 802.11r won't exist -- all of its changes will be incorporated into the base document that TGz is amending | delete "of 802.11r-D7.0" |  |
| 236 | Clint | Chaplin | 8.5.9 |  |  | T | Y | I'm uncomfortable with the term "public value" as used in this draft. It's such a generic term, and has absolutely no descriptive element in it. And why is the variable usually called "DH"? What does "DH" stand for? | "public key value"? |  |
| 237 | Ganesh | Venkatesan | 8.5.9 | 21 | 32 | T | Y | [KS] Both lines 32 and 33 have same STA-I | Change line 32 to Initiator STA an line 33 to Peer STA |  |
| 238 | Ganesh | Venkatesan | 8.5.9 | 21 | 46 | T | Y | [KS] Clause 8.5.3 defines the 4-way handshake as between a supplicant and an Authenticator. There are certain security properties of the roles of these 2 end-points. In the TDLS peer key handshake, it is not clear which end point is playing which of the 2 roles. | Clarify the roles and assumptions of the 2 security endpoints. |  |
| 239 | Henry | Ptasinski | 8.5.9 | 21 | 13 | T | Y | “The AP must ...setup” implies that the AP is actively participating in the TDLS setup. | Change to “Prior to PeerKey setup, each STA shall establish an RSNA with the AP” |  |
| 240 | Henry | Ptasinski | 8.5.9 | 21 | 16 | T | Y | BSSID is sent in the exchange, but never verified. | Add a requirement that the BSSID be validated (same in all messages and matches the current association). |  |
| 241 | Henry | Ptasinski | 8.5.9 | 21 | 18 | T | Y | “shall start a timer” doesn't provide any details about the timer. | Provide details here or a reference to clause 8.5.9.2 (assuming that's the timer referenced here). |  |
| 242 | Henry | Ptasinski | 8.5.9 | 21 | 22 | T | Y | “A STA should use the TDLS Peer Key Handshake prior to transferring ...” is insufficiently strict. | Change to “When using TDLS with an AP with which the STA has an RSNA, the STA shall use the TDLS Peer Key Handshake prior to transferring ...” |  |
| 243 | Hideyuki | Suzuki | 8.5.9 | 21 | 10 | T | Y | Although TDLS Peer Key Handshake has been combined with 3-way TDLS setup handshake, so this description is inaccurate. | Rewrite this description appropriately. |  |
| 244 | Hideyuki | Suzuki | 8.5.9 | 21 | 10 | T | Y | Either STA should initiate the handshake first or both can initiate at the same time. | TDLS Peer Key Handshake needs to be fixed from the viewpoint of peer to peer model in order to support simultaneity. |  |
| 245 | Hideyuki | Suzuki | 8.5.9 | 21 | 17 | T | Y | TDLS Peer Key Handshake does not use EAPOL-Key exchange. | Rewrite the description of TDLS Peer Key Handshake appropriately. |  |
| 246 | Hideyuki | Suzuki | 8.5.9 | 21 | 20 | T | Y | STKINIT is the state of the PeerKey Handshake Supplicant key management state machine. | Define TDLS Peer Key Handshake state machine and use it. |  |
| 247 | Hideyuki | Suzuki | 8.5.9 | 21 | 45 | T | Y | To my understanding, all of the information which is necessary to build a STK are already exchanged through SMK Handshake, so the initiator STA might not explicitly need to initiate the 4-Way STK Handshake. | Rethink whether 4-Way handshake should be combined into 3-Way TDLS Setup Handshake then rewrite this description of the 4-Way STK Handshake appropriately. |  |
| 248 | Hideyuki | Suzuki | 8.5.9 | 22 | 6 | T | Y | TDLS Peer Key Handshake has been combined with 3-way TDLS setup handshake, so the word "first message" should be modified appropriately. | "first message" should be changed to "TDLS Setup Request" or SMK Message 1. |  |
| 249 | Jesse | Walker | 8.5.9 | 21 | 10 | T | Y | The TDSL Peer Key Handshake seems to me to be needlessly heavyweight and non-extensible. It seems to me that a much lighter-weight protocol can be devised within the security model adopted by 802.11z. In particular, 802.11z assumes that the AP is trusted to not compromise the TDSL messages or utilize any of this communications to compromise the resulting DL key. | Under the trust assumptions 802.11z is already making about the AP, a design that (a) requires the AP to enforce RSN-protected links (already explicitly required on p.21 line 13-14) and (b) the Initiator and the Peer exchange random nonces used to derive a session key using the 802.11i KDF suffices. See 11-08--0476 as an example protocol meeting this description. Replacing 8.5.9 with 11-08-0476 or some like proposal would address my concerns with the existing 8.5.9. This will reduce the network and CPU bandwidth by orders of magnitude without degrading security one bit. |  |
| 250 | Jesse | Walker | 8.5.9 | 21 | 10 | T | Y | Since the intent is to reuse the 4-Way Handshake, which is controlled by the SME and 802.1X, the relation between the TDLS Peer Key Handshake on one hand and the SME and 802.1X has to be worked through in a way that will be interoperable. No text regarding these relationship exists currently | Add a model explaining how the SME invokes the TDLS Peer Key Setup protocol, how the necessary interactions with 802.1X happen, such as relaying the keys created by the protocol, occur |  |
| 251 | Jesse | Walker | 8.5.9 | 21 | 13 | T | N | "…data confidentiality…" 802.11 does not support any data confidentiality-only cipher suites. | "…data confidentiality and integrity…" |  |
| 252 | Jesse | Walker | 8.5.9 | 21 | 13 | T | Y | "The AP must establish…prior to PeerKey setup." While I entirely condone the sentiment behind this, err, uh, requirement, there are two problems with describing the functionality this way. The first 802.11z is not suppoed to change APs, and they currently don't implement this check. The second is that the check needs to be at the STA, not the AP, to be effective from a security perspective. | Replace the offending sentence with something like "A STA shall establish an RSNA-protection association with the AP prior to initiating Peer Key setup. The STA shall not initiate or respond to the PeerKey setup messages unless the AP's RSN information element omits WEP-40 and WEP-104 as enabled pairwise and group cipher suites, and the 'No Pairwise' subfield of the RSN capabilities field is 0." |  |
| 253 | Kevin | Hayes | 8.5.9 | 21 | 37 | T | Y | Add the following to the assumption list: The AP is trusted by both STA peers. | See comment. |  |
| 254 | Kevin | Hayes | 8.5.9 | 21 | 42 | T | Y | "This message exchange goes through the AP and is …" This is supposed to be a specification, not a loose colloquial description. | Please precisely describe how the message exhange is transported, describing the identity of all parties. Or delete the text. |  |
| 255 | Matthew | Fischer | 8.5.9 | 21 | 12 | T | Y | Does the phrase "direct link setup" now include TDLS? That relationship is implied in this sentence, but does it hold everywhere in this draft as well as in the baseline? | At a minimum, redefine DLS to include TDLS if that is appropriate, otherwise, make certain that references to direct links are explicit about which type of direct links are applicable (e.g. TDLS DLS vs non-TDLS DLS) |  |
| 256 | Matthew | Fischer | 8.5.9 | 21 | 12 | T | Y | The comment is intended to apply to all of the subclauses of 8.5.9. General grammar issues and ambiguous references to "STA" | Throughout 8.5.9 and all of its subclauses, find and fix missing articles, add adjectives to "STA" as appropriate, make verb conjugates match and make them correct for the context. |  |
| 257 | Meiyuan | Zhao | 8.5.9 | 21 | 14 | T | Y | It is assumed that the initiator STA starts the TDLS Peer Key Handshake. However, it is not clear from TDLS execution that there's only one initiator STA. It could be the two STAs initiate their own instance of TDLS simultaneously. If it is allowed to have both initiators to start peer key handshake, the two STAs end up with two sets of keys. Even with a mechanism to drop a set of key, the simultaneous execution of two Peer Key Handshake protocol instances can enable inter-leaving attacks. | Current design of peer key handshake is a hack of a client/server protocol for peer to peer communication. The design philosophy is incorrect. To make it work, at least carefully analyze TDLS protocol to clearly define roles to enable only one peer key handshake instance. A better approach is to re-design the peer key handshake protocol that is directly suitable for peer to peer setting. |  |
| 258 | Nancy | Cam-Winget | 8.5.9 | 21 | 27 | T | Y | This first item does not need to be an assumption as TGz succeeds TGr so it should be implied that FT and FTIE are already defined in the base 802.11 specification. | Remove this line. |  |
| 259 | Nancy | Cam-Winget | 8.5.9 | 21 | 43 | T | Y | What PTK? If each Peer STA is communicating via the AP, then their messages are protected by different PTK's; e.g. the STA_I's PTK shared with the AP and the STA_P's PTK shared with the PTK. | Either remove or clarify this sentence. |  |
| 260 | Stephen | Emeott | 8.5.9 | 21 | 12 | T | Y | According to clause 11.z1, the peer key handshake seems to begin with the first message in the tunneled direct link setup | Change sentence to read "The TDLS Peer Key Handshake begins with the first message in the directl link setup procedure (11.z1). |  |
| 261 | Stephen | Emeott | 8.5.9 | 21 | 17 | T | Y | The second paragraph refers to a TDLS Peer Key EAPOL-Key exchange, when the exchange seems to occur using ethertype 89-0d frames. | Remove references to the EAPOL-key frame and refer instead to the ethertype 89-0d frames |  |
| 262 | Stephen | Emeott | 8.5.9 | 21 | 43 | T | Y | The message exchange is protected "using either the PTK of the initiator STA or the PTK of the peer STA, depending upon whether the message is being transmitted to/from the AP" | Make the suggested change |  |
| 263 | Tomoko | Adachi | 8.5.9 | 21 | 10 | T | Y | Is public key used? Can't common key cryptosystem be used to ease the implementation (reduce the amount of calculation)? | Use common key cryptosystem. |  |
| 264 | Adrian | Stephens | 8.5.9.1 |  |  | T | N | "1406 pi" The operation and the value of pi are undefined. | Either replace pi with the Greek symbol of that name, or add a multiplication symbol and define "pi". |  |
| 265 | Adrian | Stephens | 8.5.9.1 |  |  | T | Y | In documenting the value of the prime, is the most significant byte first or last. Is the most significant nibble first or last. Is it read left to right first, or top to bottom first? | Define how to interpret this block of characters as a number. |  |
| 266 | Bill | Marshall | 8.5.9.1 | 22 | 28 | T | y | it is unclear what is meant by the first parameter shown in the FTIE. Values 0, 7, and 4 are used in the three messages of the sequence | add an explanation of this value. |  |
| 267 | Bill | Marshall | 8.5.9.1 | 22 | 31 | T | y | Lifetime and DH_P are not contained in the FTIE | move the right paren (ending the FTIE contents) to follow the BSSID |  |
| 268 | Bill | Marshall | 8.5.9.1 | 22 | 34 | T | y | Lifetime and DH_I are not contained in the FTIE | move the right paren (ending the FTIE contents) to follow the BSSID |  |
| 269 | Brian | Hart | 8.5.9.1 | 22 | 7 | T | Y | "Imitator"? Or initiator? | Check & fix if needed |  |
| 270 | Ganesh | Venkatesan | 8.5.9.1 | 22 | 4 | T | Y | [KS] The use of a public-key exchange adds a new component to 802.11 security which has been avoided, largely due to the computational time and latency needed on low-power 802.11 devices. In addition, this requires a significant non-incremental component in traditional device supplicants. The security of DH approach is still susceptible to MITM attacks. These MITM attacks can be limited to those that can be launched on the AP (assuming 802.11i mechanisms exists on 2 links). So, DH approach is insufficient, and largely an overkill. | Define the security goals for the Peer-key handshake. Adopt the resolution presented in 11-08-0476-00 (version number may change). |  |
| 271 | Ganesh | Venkatesan | 8.5.9.1 | 22 | 11 | T | Y | [KS] The use of a 1536-bit based group is insufficient for matching the strength of a 128-bit AES crypto. RFC 3526 states "For the 128-bit AES we need about a 3200-bit group [Orman01]". If DH is to be used, then use a higher-bit group. | If TGz decides to continue using DH scheme, then use a higher-bit group (4096-bit or higher) to match cryptographic strength of 128-bit AES. |  |
| 272 | Hideyuki | Suzuki | 8.5.9.1 | 22 | 28 | T | Y | FTIE does not have PNonce field or INonce field. Although FTIE has ANonce and SNonce field, each fields are dedicated for the value chosen by R1KH or S1KH. | Define new IE for SMK Handshake or modify the definition of FTIE appropriately. |  |
| 273 | Jesse | Walker | 8.5.9.1 | 22 | 11 | T | Y | Why do we believe that a 1536 bit prime will meet the security needs of the application beyond 2015? When we have to increase the size of the Diffie-Hellman group to 3K bits = 384 octets (to meet FIPS 140-2 in 2010), the parameters will no longer fit in a single IE. Why do we believe that we can meet the power consumption requirements of battery powered devices with a prime this large (roughly 34 million cycles per operation)? Why is there no extensibility mechanism to replace this Diffie-Hellman group with other ones as need demands. While Diffie-Hellman is a lovely algorithm, no attempt has been made to justify its use for this application. | As far as I can tell, a non-Diffie-Hellman algorithms, such as the one suggested in 11-08-0476, will provide the same level of security at a computational cost that is ***4 ORDERS OF MAGNITUDE*** lower per key establishment. Replace the current Diffie-Hellman approach with a cheaper algorithm, such as that in 11-08-0476. |  |
| 274 | Jesse | Walker | 8.5.9.1 | 22 | 31 | T | Y | FTIE Mic Control field is 2 octets; MIC is 16 octets; PNonce is 32 octets; INonce is 32 octets; MAC_I is 6 octets + 2 octets overhead, MAC_P is 6 octets + 2 octets overhead; BSSID is 6 octets + 2 octets overhead; Lifetime is ?? octets + 2 octets overhead; DH_P is 192 octets + 2 octets overhead. 2+16+32+32+6+2+6+2+6+2+??+2+192+2 = 302+?? > 255 = maximum number of octets in an 802.11 IE. It is unclear why the FTIE needs to carry the DH_P, since 7.3.2.z3 defines a separate IE for this purpose. Should the Lifetime be given by the Timeout Interval IE (7.3.2.49 in 802.11r)? | Some surgery is required, even if TGz decides to stick with the current scheme instead of replacing it with something cheaper. |  |
| 275 | Jesse | Walker | 8.5.9.1 | 22 | 31 | T | N | While I understand that the document assumes that the AP will not launch man-in-the-middle attacks against the SMK protocol, it really bothers me a great deal that message 2 does not include both DH_I and DH_P. It seems as though this makes man-in-the-middle attacks even more attractive by failing to bind all of the parameters properly. It also gives the crypto community an even more attractive target for ridiculing our collective efforts publicly. Isn't avoidance of further public relations disasters over inept our continuing inept use of cryptography a consideration? | In the comment |  |
| 276 | Jesse | Walker | 8.5.9.1 | 22 | 34 | T | N | It probably doesn't matter that the initiator repeat the DH_I in message 3--the two parties can discover they have agreed on this parameter from the MIC. | No change is required, but the 802.11 bit police are usually looking for ways to reduce message overheads... |  |
| 277 | Jesse | Walker | 8.5.9.1 | 22 | 28 | T | Y | I am confused again. The updates P802.11z D1.0 makes to 7.3.2.46 does not include additions for the Lifetime and DH_I fields, yet the message format on line 28 indicates these are indeed subfields of FTIE. Why is DH_I needed here, as it has its own subfield defined in 7.3.2.z2? What is the Lifetime subfield, and how large is it? Note that 7.3.2.46 does NOT give you the option to elide the PNonce subfield to save space, as this message has done. | Please utilize data structures consistently |  |
| 278 | Jesse | Walker | 8.5.9.1 | 22 | 28 | T | Y | I am even more confused. Since SMK messages have their own Ethertype, they really need their own extensible format. I don't object to utilizing 802.11 IEs to convey information, but the formats for this new application protocol are entirely implicit. (The formats in 7.2 are NOT extensible, because a legacy system isn't given a clue about how to deal with extensions developed after deployment) | Please create a new clause defining SMK messages as first class objects. Include a version distinguisher, and define the MANDATORY semantics around handling the version distinguisher, to make the protocol extensible in the future. |  |
| 279 | Joseph | Epstein | 8.5.9.1 | 22 | 14 | T | N | The formula should be given in proper mathematical symbols, rather than the pseudoformulation from the RFC. | Replace "pi" with the greek letter, show the exponentiations through superscripting, and replace the curly braces. The use of ^ can be considered unclear without an explanation. |  |
| 280 | Jouni | Malinen | 8.5.9.1 | 22 | 25 | T | Y | The SMK Handshake for TDLS seems to be using an unauthenticated Diffie-Hellman exchange to generate SMK. This is potentially open to man-in-the-middle attacks. Even though it is not mentioned in the draft, I would assume that the pre-existing encrypted connection between the AP and STAs is used as an implicit “authentication” for the SMK Handshake and DH. However, this may result in decreased security guarantees and potential misconception on how secure the direct link is. Would it be possible to end up using TKIP to protect the AP-STA links and negotiate CCMP for the direct link? In such a case, the SMK and STK derived for CCMP would depend on security of TKIP (i.e., if TKIP is broken, man-in-the-middle attack against the DH in SMK Handshake could be possible). I don't consider this to be major issue since the STAs have already agreed to use the AP for the data connection. However, I think it would be useful to explicitly spell out the assumptions about the AP security and risks involved if the STA-AP-STA link is using less secure encryption than the direct link. | Consider adding a paragraph that lists the assumptions on the AP behavior for the security of the tunneled SMK Handshake (including the use of the AP connection as an implicit authentication for DH and affect of TKIP as the STA-AP encryption on the security of key generation for possible CCMP protected direct link). |  |
| 281 | Matthew | Fischer | 8.5.9.1 | 22 | 7 | T | Y | Wrong word | Imitator should be initiator (not sure about case) |  |
| 282 | Meiyuan | Zhao | 8.5.9.1 | 22 | 28 | T | Y | Message 1 should include the MAC_P as well to specify the recepient of the message. Otherwise, there's increase vulnerability to denial of service attack | Add MAC_P in message 1 of SMK handshake |  |
| 283 | Meiyuan | Zhao | 8.5.9.1 | 22 | 4 | T | Y | The design of SMK Handshake uses a variant of Diffie-Hellman key exchange protocol. However, this design fails to provide authenticity of the two parties. MIC protection using the key derived from the secret key is not sufficient to provide authenticity. | Modify the design to provide authenticity. The design could be similar to STS protocol which provide party authenticity. |  |
| 284 | Meiyuan | Zhao | 8.5.9.1 | 22 | 31 | T | Y | To help authenticity and session binding, message 2 should include both DH_P and DH_I | Add DH_I in message 2 |  |
| 285 | Meiyuan | Zhao | 8.5.9.1 | 22 | 34 | T | Y | To help authenticity and session binding, message 3 should include both DH_P and DH_I | Add DH_P in message 3 |  |
| 286 | Nancy | Cam-Winget | 8.5.9.1 | 22 | 14 | T | Y | By the indication of a modulo prime indicated in this sentence, an individual who is knowledgeable in crypto could discern that some public key operation is to take place (and judging by the use of DH and RFC 3526, that it is possibly a Diffie Hellman exchange)….but nowhere, are these constructs introduced, nor is there any explanation for how this parameter applies and what it is trying to achieve. While we could extract this from further reading the message descriptions, an introductory paragraph of how the SMKSA is validated? uses this to derive keys? is required to make sense of this. | In the comment. |  |
| 287 | Stephen | Emeott | 8.5.9.1 | 22 | 27 | T | Y | The FTIE does not take Lifetime nor DH_I as arguments | Modify the message definition to put a ")" after BSSID. Same goes for the FTIE() arguments in message 2 and message 3 |  |
| 288 | Bill | Marshall | 8.5.9.1.1 | 22 | 38 | T | y | lack of normative language in this clause | change "STA performs" to "STA shall perform" |  |
| 289 | Bill | Marshall | 8.5.9.1.1 | 22 | 40 | T | y | RSNIE is not in this message | change to RSNIE_I |  |
| 290 | Bill | Marshall | 8.5.9.1.1 | 22 | 41 | T | y | Very awkward statement regarding the group cipher suit field | change to "The Group cipher suite shall be set to zeroes." |  |
| 291 | Bill | Marshall | 8.5.9.1.1 | 22 | 45 | T | y | Key Nonce field is undefined | change "sent in Key Nonce field" to "sent in the Inonce field" |  |
| 292 | Bill | Marshall | 8.5.9.1.1 | 21 | 34 | T | y | Sice the FTIE definition uses the terms ANonce and SNonce, there is potential confusion here since TGz is ugins INonce and PNonce. | make this association clear; suggest changing lines 34 and 35 to "INonce is the nonce generated by STA_I and stored in the SNonce field of the FTIE", and similar change to line 35 |  |
| 293 | Bill | Marshall | 8.5.9.1.1 | 22 | 47 | T | y | "as part of Lifetime" doesn't specify where/how to include this information | clarify |  |
| 294 | Bill | Marshall | 8.5.9.1.1 | 22 | 49 | T | y | extraneous word "public" on this line | delete "public" |  |
| 295 | Bill | Marshall | 8.5.9.1.1 | 22 | 51 | T | y | lack of normative language in this clause | change "STA sends" to "STA shall send" |  |
| 296 | Bill | Marshall | 8.5.9.1.1 | 22 | 51 | T | y | peer STA_P is confusing | change to "to the peer STA through the AP" |  |
| 297 | Bill | Marshall | 8.5.9.1.1 | 22 | 52 | T | y | lack of normative language in this clause | change "STA starts" to "STA shall start" |  |
| 298 | Bill | Marshall | 8.5.9.1.1 | 22 | 3 | T | y | there may be several existing direct links. | change "against existing direct link" to "against existing direct links" |  |
| 299 | Bill | Marshall | 8.5.9.1.1 | 22 | 3 | T | y | there may be several existing direct links. | change "If no direct link exists" to "If no matching direct link exists" |  |
| 300 | Bill | Marshall | 8.5.9.1.1 | 22 | 3 | T | y | unclear pronoun "it" - which STA?? | change "it" to "the peer STA" |  |
| 301 | Bill | Marshall | 8.5.9.1.1 | 22 | 3 | T | y | lack of normative language in this clause | change "silently discards" to "shall silently discard" |  |
| 302 | Bill | Marshall | 8.5.9.1.1 | 22 | 6 | T | y | lack of normative language in this clause | change "If all check succeed" to "If all checks succeed, the peer STA shall" |  |
| 303 | Bill | Marshall | 8.5.9.1.1 | 22 | 8 | T | y | the random number isn't sent yet | change "sent" to "placed" |  |
| 304 | Bill | Marshall | 8.5.9.1.1 | 22 | 8 | T | y | Key Nonce field is undefined | change "in Key Nonce field" to "in the PNonce field" |  |
| 305 | Bill | Marshall | 8.5.9.1.1 | 22 | 10 | T | y | "used" is unclear | change "used" to "placed" |  |
| 306 | Bill | Marshall | 8.5.9.1.1 | 22 | 11 | T | y | extraneous word "public" on this line | delete "public" |  |
| 307 | Bill | Marshall | 8.5.9.1.1 | 22 | 21 | T | y | this is not a single large integer value, but rather an octet string. | change to 0x53 0x4d 0x4b 0x20 etc |  |
| 308 | Bill | Marshall | 8.5.9.1.1 | 22 | 23 | T | y | "the initiator RSNIE" is unclear | change to RSNIE_I |  |
| 309 | Bill | Marshall | 8.5.9.1.1 | 22 | 25 | T | y | lack of normative language in this clause | change "sends" to "shall send" |  |
| 310 | Bill | Marshall | 8.5.9.1.1 | 22 | 25 | T | y | handling of message 2 in 8.5.9.1.2 is checking a MIC, but the MIC is not being calculated | add the normative procedures to calculate the MIC |  |
| 311 | Clint | Chaplin | 8.5.9.1.1 | 23 | 21 | T | Y | Defining a string as "0x534d4b204b65792044657269766174696f6e" is ambiguous and can lead to incompatibilities | define as "0x53 0x4d 0x4b 0x20 0x4b 0x65 0x79 0x20 0x44 0x65 0x72 0x69 0x76 0x61 0x74 0x69 0x6f 0x6e" |  |
| 312 | Ganesh | Venkatesan | 8.5.9.1.1 | 22 | 49 | T | Y | [KS] The DH is computed using exponentiation operation, as opossed to the multiplication operation suggested on this line | If group decides to use DH, then change DH_I = g^A mod p |  |
| 313 | George | Vlantis | 8.5.9.1.1 | 23 | 3 | T | Y | In the case of TDLS, the check of the MAC address in step (a) does not make a lot of sense. | Please clarify the method with TDLS. |  |
| 314 | Henry | Ptasinski | 8.5.9.1.1 | 22 | 42 | T | Y | The group cipher suite identifier use in the exchange should be well defined. | Define a new cipher suite to represent “no group-addressed data allowed on this link”, add it to table 7-32 in the base standard, and use it in the TDLS handshake. |  |
| 315 | Henry | Ptasinski | 8.5.9.1.1 | 22 | 52 | T | Y | “starts a timer” doesn't provide sufficient details about the timer. | Provide details here or a reference to clause 8.5.9.2 (assuming that's the timer referenced here). |  |
| 316 | Henry | Ptasinski | 8.5.9.1.1 | 23 | 5 | T | Y | The BSSID should be verified. | After step (a), add a check that the BSSID matches the current association. |  |
| 317 | Hideyuki | Suzuki | 8.5.9.1.1 | 23 | 3 | T | Y | TDLS Peer Key Handshake has been combined with 3-way TDLS setup handshake. So basically there is no TDLS direct link at this stage. | Remove this sentence or separate SMK Handshake from 3-Way TDLS Setup Handshake. |  |
| 318 | Jesse | Walker | 8.5.9.1.1 | 22 | 42 | T | Y | "…with any value…" I will continue to vote "Do Not Approve" as long as this is any value but the group cipher suite for the BSS; it will confuse other members of the BSS too much otherwise. I will also continue to vote "Do Not Approve" if the draft allows this to assume the values WEP-40 or WEP-104. Hasn't the industry suffered enough over WEP to not forbid its use for new functions? | Require the initiator to set the group cipher suite to the value equal to that used by the BSS. Also require that the initiator SHALL NOT initiate the SMK Handshake and the receiver SHALL reject SMK Handshake messages if the Group Cipher Suite is WEP-40 or WEP-104 |  |
| 319 | Jesse | Walker | 8.5.9.1.1 | 22 | 45 | T | Y | "…the Key Nonce field…" Clause 7.3.2.46 fails to define a KeyNonce field for the FTIE. | Please utilize data structures consistently |  |
| 320 | Jesse | Walker | 8.5.9.1.1 | 22 | 47 | T | Y | "…of Lifetime." Clause 7.3.2.46 fails to define a Lifetime field for the FTIE | Please utilize data structures consistently |  |
| 321 | Jesse | Walker | 8.5.9.1.1 | 22 | 47 | T | Y | As a rule, we should make every effort so that our designs do not make denial-of-service any worse. The Lifetime fails to give an guidance avoiding this. | Define a minimum time for the Lifetime paramater. 5 minutes (300 seconds) seems like a reasonable lower bound--if anyone needs to establish keys any faster than this, something is wrong!!! |  |
| 322 | Jesse | Walker | 8.5.9.1.1 | 22 | 49 | T | Y | "…a random integer A < p" | Require A to be at least 224 bits in length (at least one non-zero bit for bits >= 223, where the bits are numbered 0,1,2,...,n). The custom today is to make A 160 bits in length. This size will be too small to provide assurance against attacks based on the Special Number Seive by 2010. 224 bits will give us a safety margin until about 2020, although it will make performance suck even more than it would otherwise. |  |
| 323 | Jesse | Walker | 8.5.9.1.1 | 23 | 3 | T | Y | Two other checks should be required: verify that the lifetime is not too short and verify that DH_I is actually a member of the group instead of a value generated randomly by an attacker; if you really, really want to do Diffie-Hellman, do it right, or else you're wasting everyone's time. This check can be done using the elementary identity DH_I^p mode p = 1. | In the comment |  |
| 324 | Jesse | Walker | 8.5.9.1.1 | 23 | 6 | T | Y | What happens if one of the checks fails? | Specify mandatory failure processing |  |
| 325 | Jesse | Walker | 8.5.9.1.1 | 23 | 22 | T | Y | You'll find it is useful in real life to generate a key identifier and include this in the protocol--indeed, the 4-Way Handshake REQUIRES that you do this. | A perfectly good key identifier is Truncate-128(SHA-256(BSSID ¦¦ MAC_I ¦¦ MAC_P ¦¦ INonce ¦¦ PNonce)), on the assumption that at least one of <INonce, PNonce> has been generated randomly as per the spec. Messages 2 and 3 should convey this key identifier, so that the two parties know that they agree on the key to use. |  |
| 326 | Jouni | Malinen | 8.5.9.1.1 | 22 | 49 | T | Y | Diffie-Hellman uses exponentiation, not multiplication, modulo p. | Replace “DH_I = gA mod p” with “DH_I = gA mod p” (i.e., use subscript for 'A'). |  |
| 327 | Kevin | Hayes | 8.5.9.1.1 | 22 | 47 | T | Y | "sent as part of Lifetime" How is it sent? Is it sent in my Lifetime? In your Lifetime? | Please precisely describe how the lifetime of the SMKSA is communicated. Or delete the sentence. |  |
| 328 | Kevin | Hayes | 8.5.9.1.1 | 22 | 49 | T | Y | gA mod p | gA mod p |  |
| 329 | Kevin | Hayes | 8.5.9.1.1 | 23 | 3 | T | Y | "Verify…against existing direct link." What is meant by this? | Please precisely describe what to verify. |  |
| 330 | Kevin | Hayes | 8.5.9.1.1 | 23 | 6 | T | Y | "If all checks succeed" What checks? The one that is not precisely described in line 3 above? Please list any other checks and if no others, then lose the plural on 'checks'. | See comment. |  |
| 331 | Kevin | Hayes | 8.5.9.1.1 | 23 | 26 | T | Y | The calculation of the MIC is not explained or even mentioned here. Yet the next step says to check that is is correct. What gives? | Add precise description of MIC calculation. |  |
| 332 | Liwen | Chu | 8.5.9.1.1 | 23 | 3 | T | Y | On receipt of SMK Handshake Message 1, the peer STA verifies the initiator MAC address against existing direct link. But actually SMK messages can be carried in TDLS setup messages. This should be fixed. | Use the method proposed in 11-08/290 to fix the problem. |  |
| 333 | Matthew | Fischer | 8.5.9.1.1 | 22 | 38 | T | Y | grammar issues with these sentences - missing articles in quite a few places and the STA nouns could use a few adjectives to clarify which STA -also, the verbs at each subbullet are inconsistent in conjugation | Find and fix missing articles, add adjectives to "STA" as appropriate, make verb conjugates match and make them correct for the context. Note that subbullet d) includes both a noun and verb in its predicate, while the previous subbullets use the common noun of the preceding sentence - make all subbullets consistent for improved readability. |  |
| 334 | Stephen | Emeott | 8.5.9.1.1 | 22 | 47 | T | Y | The Lifetime should be packed in some type of IE | Make the suggested change |  |
| 335 | Stephen | Emeott | 8.5.9.1.1 | 22 | 36 | T | Y | The construction of message 1-3 should be more concisely described, similar to how the construction of the STKSA rekeying EAPOL-Key message is described in 8.5.9.3 to avoid any confusion about the fields in the frame. | Make the suggested change |  |
| 336 | Jesse | Walker | 8.5.9.1.1 | 23 | 9 | T | Y | "…a smaller lifetime…" | Again, there needs to be some normative prohibition against picking a lifetime that is too small, e.g., below 300 seconds. |  |
| 337 | George | Vlantis | 8.5.9.1.2 | 23 | 35 | T | Y | In the case of TDLS, the checks of the MAC addresses in steps (a) and (b) do not make a lot of sense. | Please clarify the method with TDLS. |  |
| 338 | Henry | Ptasinski | 8.5.9.1.2 | 23 | 30 | T | Y | “starts a timer” doesn't provide sufficient details about the timer. | Provide details here or a reference to clause 8.5.9.2 (assuming that's the timer referenced here). |  |
| 339 | Henry | Ptasinski | 8.5.9.1.2 | 23 | 37 | T | Y | The BSSID should be verified. | After step (a), add a check that the BSSID matches the current association and the BSSID provided in Message 1. |  |
| 340 | Hideyuki | Suzuki | 8.5.9.1.2 | 23 | 35 | T | Y | TDLS Peer Key Handshake has been combined with 3-way TDLS setup handshake. So basically there is no TDLS direct link at this stage. | Remove this sentence or separate SMK Handshake from 3-Way TDLS Setup Handshake. |  |
| 341 | Jesse | Walker | 8.5.9.1.2 | 23 | 39 | T | Y | There are again checks missing. | Require the initiator to check that (a) the Lifetime is not too small, (b) that the receiver has not increased the lifetime originally proposed, and (c) that DH_P is actually a group element by verifying DH_P^p mod p = 1. It wouldn't hurt to check the key identifier, too, although presently this has not been defined and included in the message. |  |
| 342 | Jesse | Walker | 8.5.9.1.2 | 23 | 41 | T | Y | What happens if one of the checks fails? | Specify mandatory failure processing |  |
| 343 | Jesse | Walker | 8.5.9.1.2 | 24 | 13 | T | N | I would include the (presently undefined) KeyID in the MIC calculation as well--it will make debugging easier for implementers and doesn't hurt security one bit | In the comment |  |
| 344 | Jesse | Walker | 8.5.9.1.2 | 24 | 15 | T | Y | What happens if the MIC check fails? | Specify mandatory failure processing |  |
| 345 | Keith | Amann | 8.5.9.1.2 | 23 | 35 | T | Y | The text states that on receipt of message 2 the initiator STA performs a check verifying whether a direct link exists, and if not then it silently discards the message. This is a chicken and egg problem since the direct link doesn't exist until the negotiation of the security message is completed. | Clarify the text to indicate that "no direct link exists" means that the station is also not in the process of attempting to construct a direct link with the peer. |  |
| 346 | Keith | Amann | 8.5.9.1.2 | 23 | 35 | T | Y | The text indicates that in the event of an error the messages should be silently discarded, but clause 8.5.8.4.4 states that when a station detects that it does not have a direct link established it should respond with an appropriate error message. | Clarify these paragraphs, and any others that are related, to clearly indicate what a stations normative behavior should be in the case of an error (i.e. it should or should not send an error response), particularly as it relates to situations where no direct link exists. |  |
| 347 | Kevin | Hayes | 8.5.9.1.2 | 24 | 2 | T | Y | Firstly, should probably use the '¦¦' notation rather than a bulleted list. Secondly, why not do the MIC on the while EAPOL-Key frame, as is done for other protocols in this standard? | Please precisely describe the calculation of the MIC which shall include the entire frame. |  |
| 348 | Liwen | Chu | 8.5.9.1.2 | 23 | 35 | T | Y | On receipt of SMK Handshake Message 2, the initiator STA verifies the initiator MAC address against existing direct link. But actually SMK messages can be carried in TDLS setup messages. This should be fixed. | Use the method proposed in 11-08/290 to fix the problem. |  |
| 349 | Meiyuan | Zhao | 8.5.9.1.2 | 24 | 5 | T | Y | The ordering of information for MIC calculation should be different for messages sent by STA_I and STA_P. The current design uses the same ordering, which enables reflection attack. | Change the ordering of MIC calculation in message 2 to: "MAC_P MAC_I BSSID RSNE_P PNonce INonce Lifetime DH_P DH_I". And change the ordering of MIC calculation in message 3 to: "MAC_I MAC_P BSSID RSNE_I INonce PNonce Lifetime DH_I DH_P". |  |
| 350 | George | Vlantis | 8.5.9.1.3 | 24 | 25 | T | Y | In the case of TDLS, the checks of the MAC addresses in steps (a) and (b) do not make a lot of sense. | Please clarify the method with TDLS. |  |
| 351 | Henry | Ptasinski | 8.5.9.1.3 | 24 | 27 | T | Y | The BSSID should be verified. | After step (a), add a check that the BSSID matches the current association and the BSSID provided in Message 2. |  |
| 352 | Jesse | Walker | 8.5.9.1.3 | 24 | 28 | T | Y | What happens if any of these checks fail? | Specify mandatory failure processing |  |
| 353 | Liwen | Chu | 8.5.9.1.3 | 24 | 25 | T | Y | On receipt of SMK Handshake Message 3, the peer STA verifies the initiator MAC address against existing direct link. But actually SMK messages can be carried in TDLS setup messages. This should be fixed. | Use the method proposed in 11-08/290 to fix the problem. |  |
| 354 | Adrian | Stephens | 8.5.9.2 |  |  | T | Y | This subclause contains a number of "magic numbers" - i.e. values probably chosen as a best guess of this group on the value of timeouts. However, these values may turn out to be poorly chosen for whatever reason, and should be manageable in future. | Replace each magic number (e.g., 2000, 1000, 200) with a mib variable reference. Add mib variables for each of these magic numbers. |  |
| 355 | Clint | Chaplin | 8.5.9.2 | 25 | 2 | T | Y | "The retransmit timeout value shall be 2000 milliseconds for the first timeout, the listen interval 3 for the second timeout, and twice the listen interval for subsequent timeouts. If there is no listen interval, 4 then 200 milliseconds shall be used for all timeout values." | "The retransmit timeout value shall be 2000 milliseconds for the first timeout, the listen interval for the second timeout, and twice the listen interval for subsequent timeouts. If there is no listen interval, then 200 milliseconds shall be used for all timeout values other than the first." or "The retransmit timeout value shall be 2000 milliseconds for the first timeout, the listen interval for the second timeout, and twice the listen interval for subsequent timeouts. If there is no listen interval, then 2000 milliseconds shall be used for all timeout values." |  |
| 356 | Henry | Ptasinski | 8.5.9.2 | 25 | 2 | T | Y | The listen interval is provided by a STA to the AP. Peers in TDLS do not have any knowledge of each other's listen interval. | Define the time in absolute terms, or relative to some value already known by both sides (e.g. DTIM). |  |
| 357 | Hideyuki | Suzuki | 8.5.9.2 | 24 | 48 | T | Y | To my understanding, all of the information which are necessary to build a STK are already shared through the SMK Handshake(SMK, PNonce, INonce, MAC_P and MAC_I). So the initiator STA might not explicitly need to initiate the 4-Way STK Handshake. | Need careful consideration on whether TDLS PeerKey Handshake and/or 4-Way handshake should be combined into 3-Way TDLS Setup Handshake or not, then modify the description of TDLS PeerKey Handshake appropriately. |  |
| 358 | Hideyuki | Suzuki | 8.5.9.2 | 24 | 50 | T | Y | "direct link teardown procedure" is not defined in this draft. | Define the "direct link teardown procedure" for TDLS. |  |
| 359 | Hideyuki | Suzuki | 8.5.9.2 | 25 | 1 | T | Y | "direct link teardown procedure" is not defined in this draft. | Define the "direct link teardown procedure" for TDLS. |  |
| 360 | Jouni | Malinen | 8.5.9.2 | 25 | 2 | T | Y | “The listen interval” is used as a timeout for SMK handshake. However, 802.11z does not specify which listen interval (or well, whose.. peer or initiator?) is used here. I would assume this text was just copied from the RSN 4-way handshake timeouts that the Authenticator uses. However, in case of TDLS PeerKey handshake, the initiator or peer STA do not really know the listen interval of the other STA and there is not much point in using STA's own listen interval as a timeout for retry in this case. Unless the STA can somehow figure out the other STA's listen interval, it would be better to just define a fixed timeout for TDLS PeerKey handshake. Furthermore, it does not look correct to replace the 2000 millisecond timeout with a 200 millisecond timeout if “there is no listen interval” (whatever that would mean in TDSL..) | Replace “The retransmit timeout value shall be 2000 milliseconds for the first timeout, the listen interval for the second timeout, and twice the listen interval for subsequent timeouts. If there is no listen interval, then 200 milliseconds shall be used for all timeout values.” with “The retransmit timeout value shall be 2000 milliseconds.” Similarly, on line 10, replace “The retranmit timeout value shall be 1000 millisecond sfor the first timeout, half the listen interval for the second timeout, and the listen interval for subsequent timeouts. If there is no listen interval, then 1000 milliseconds shall be used for all timeout values.” with “The retransmit timeout value shall be 1000 milliseconds.” |  |
| 361 | Meiyuan | Zhao | 8.5.9.2 | 25 | 9 | T | Y | The behavior of setting different values at different circumstances is confusing. It says "If the STA_I still has not received a response after these retries, it shall invoke a direct link teardown procedure. The retransmission timeout value shall be 1000 milliseconds...." Does this refer to the retransmission of STK handshake message or TDLS tear down message? If it's former, it's not consistent with base standard where the timeout value is 100 milliseconds. If it's latter, it's not consistent with the previous paragraph where the value is 2000 millisecond. Further the values of subsequent retires are different in the two paragraphs as well. | Clarify the setting of timeout values. |  |
| 362 | Meiyuan | Zhao | 8.5.9.2 | 25 | 6 | T | Y | STA_I sends message 3, not receives message 3. In this paragraph, the roles of STA_I and STA_P are contradictory from the specification. | Change the paragraph to: "Upon receipt of the SMK Message 3, the STA_P shall transmit Message 1 of the STK Handshake to the STA_I. If the STA_P does not receive Message 2 of the 4-Way STK…from the STA_I, it shall attempt …. If STA_P still has not received..." |  |
| 363 | Stephen | Emeott | 8.5.9.2 | 24 | 48 | T | Y | Its unclear why error handling for the rekey is described before the rekey proceduring in 8.5.9.3 is defined. | Relocate the material to the end of 8.5.9.3 |  |
| 364 | Bill | Marshall | 8.5.9.3 | 25 | 35 | T | y | where is the value of "N" defined | please clarify |  |
| 365 | Clint | Chaplin | 8.5.9.3 | 25 | 25 | T | Y | "If the SMK has expired" | "If the SMK timer has expired" |  |
| 366 | Jesse | Walker | 8.5.9.3 | 25 | 17 | T | Y | What is "the 802.1X Timeout"? 802.1X, an external standard, defines numerous timeouts. How does the 802.11 MAC or SME access this value? Hint: from a specsmanship perspective, you only get to use interfaces defined in the 802.1X spec if you want to follow this tact, and they don't define one. | I think we will have to reference an 802.11i timer instead. These are maintained in the SME, which coordinates between the MAC and 802.1X. The 802.11i key management state machines in 8.5.5 and 8.5.6 are probably the right place to begin looking for the "right" timer. |  |
| 367 | Jesse | Walker | 8.5.9.3 | 25 | 21 | T | Y | 802.1X is a module external to 802.11. The base standard defines SME state machines in 8.5.5 and 8.5.6 to mediate between the MAC and 802.1X. IF 802.11z continues to use the 4-Way handshake, you will need to update at least the Supplicant (non-AP STA) state machine to express the new functionality defined herein. | In the comment |  |
| 368 | Jesse | Walker | 8.5.9.3 | 25 | 30 | T | Y | I am confused again. Line 25 says STA_I initiates the rekey, but line 30 seems to say that STA_P initiates. | Please make the text internally consistent |  |
| 369 | Jouni | Malinen | 8.5.9.3 | 25 | 18 | T | Y | This paragraph seems to be in conflict with itself.. The first sentence states that rekeying is always initiated by the STA_i and the third sentence talks about STA_P initiating a TDLS Peer Key rekey procedure. STA_P is only requesting STA_I to initiate the rekeying procedure.. | Replace “before initiating” with “before requesting”. |  |
| 370 | Jouni | Malinen | 8.5.9.3 | 25 | 39 | T | Y | 802.11r and 802.11w introduce stronger MIC for EAPOL-Key frames to allow MD5 and SHA-1 -based mechanisms to be avoided. 802.11z should do the same for its use of EAPOL-Key. | Insert “or 3 (NIST AES key wrap with AES-128-CMAC)” into the end of Key Description Version description. This applies to all EAPOL-Key messages in the draft, not just the one on page 25 line 39. |  |
| 371 | Jesse | Walker | 8.5.9.4 | 26 | 34 | T | Y | The use of the EAPOL-Key message implies an interaction with 802.1X via the SME. | Update the SME state machines in 8.5.5. and 8.5.6 to add any new DL specific details on how to accomplish this. |  |
| 372 | Jesse | Walker | 8.5.9.4.1 | 27 | 27 | T | Y | Why is this needed? The devices can already discover this from the inclusion of RSNIEs in their setup messages. The error code appears to be nothing more than an opportunity to create new types of denial of service | Think about removing this error code. |  |