IEEE P802.11
Wireless LANs

| TGz Draft 1.0 CID 373-416 (10.3.z1).doc |
| --- |
| Date: May 8, 2008 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Menzo Wentink | Qualcomm | Straatweg 66, Breukelen, the Netherlands | +31-65-183-6231 | mwentink@qualcomm.com |

Abstract

This document addresses TGz LB127 CID 373-416, which relate to subclause 10.3.z1.

Instruction to the editor: Accept changes and replace subclauses as shown.

Replace 10.3.z1 with the following:

10.3.z1 Management of tunneled direct link setup

The following MLME primitives support the signaling of tunneled direct link setup. Figure z8 depicts the TDSL setup process. The figure illustrates the basic protocol, which is only an example and is not meant to be exhaustive of all possible protocol uses.

Figure z8—Tunneled Direct Link Setup Protocol Exchange

EDITORIAL NOTE—Add TDLS Setup Confirm.

10.3.z1.1 MLME-TDLSSETUPREQUEST.request

10.3.z1.1.1 Function

This primitive requests that a TDLS Setup Request frame be sent to the candidate peer STA.

10.3.z1.1.2 Semantics of the Service Primitive

The primitive parameters are as follows:

MLME-TDLSSETUP.request(

PeerSTAAddress,

TDLSSetupRequest

TDLSRequestTimeout

)

| Name | Type | Valid Range | Description |
| --- | --- | --- | --- |
| PeerSTAAddress | MAC Address | Any valid individual MAC Address | Specifies the address of the peer MAC entity with which to perform the TDLS Setup process. |
| TDLSSetupRequest | As defined in TDLS Setup Request element | As defined in TDLS Setup Request element | Specifies the proposed service parameters for the TDLS Setup. |
| TDLSRequestTimeout | Integer | ≥ 0 | Specifies a time limit (in TU) after which the TDLS Setup procedure is terminated. |

10.3.z1.1.3 When Generated

This primitive is generated by the SME to request that a TDLS Setup Request frame be sent to the candidate peer STA.

10.3.z1.1.4 Effect of Receipt

On receipt of this primitive, the MLME constructs a TDLS Setup Request action management frame. The STA then attempts to transmit this to the candidate peer STA.

10.3.z1.2 MLME-TDLSSETUPREQUEST.confirm

10.3.z1.2.1 Function

This primitive reports the result of a TDLS Setup procedure.

10.3.z1.2.2 Semantics of the Service Primitive

The primitive parameters are as follows:

MLME-TDLSSETUP.confirm(

TDLSSetupResponse

)

| Name | Type | Valid Range | Description |
| --- | --- | --- | --- |
| TDLSSetup- Response | As defined in TDLS Setup Response element | As defined in TDLS Setup Response element | Specifies service parameters for the TDLS Setup. |

10.3.z1.2.3 When Generated

This primitive is generated by the MLME as a result of an MLME-TDLSSETUP.request and indicates the results of the request.

This primitive is generated when the MLME-TDLSSETUP.request contains invalid parameters, when a timeout or failure occurs, or when the STA receives a TDLS Setup Response frame from the AP.

10.3.z1.2.4 Effect of Receipt

On receipt of this primitive, the SME evaluates the Element Status and may use the reported data.

10.3.z1.3 MLME-TDLSSETUPREQUEST.indication

10.3.z1.3.1 Function

This primitive indicates that a TDLS Setup Request frame was received from a candidate peer STA.

10.3.z1.3.2 Semantics of the Service Primitive

The primitive parameters are as follows:

MLME-TDLSSETUP.indication(

PeerSTAAddress,

TDLSSetupRequest

)

| Name | Type | Valid Range | Description |
| --- | --- | --- | --- |
| PeerSTAAddress | MACAddress | Any valid individual MAC Address | The address of the non-AP STA MAC entity from which a TDLS Setup Request frame was received. |
| TDLSSetup- Request | As defined in TDLS Setup Request element | As defined in TDLS Setup Request element | Specifies the proposed service parameters for the TDLS Setup. |

10.3.z1.3.3 When Generated

This primitive is generated by the MLME when a valid TDLS Setup Request frame is received.

10.3.z1.3.4 Effect of Receipt

On receipt of this primitive the SME should operate according to the procedure in 11.z1.

10.3.z1.4 MLME-TDLSSETUPRESPONSE.request

10.3.z1.4.1 Function

This primitive requests that a TDLS Setup Request frame be sent to the initiating STA.

10.3.z1.4.2 Semantics of the Service Primitive

The primitive parameters are as follows:

MLME-TDLSSETUPRESPONSE.request(

PeerSTAAddress,

TDLSSetupRequest

ResultCode

)

| Name | Type | Valid Range | Description |
| --- | --- | --- | --- |
| PeerSTAAddress | MAC Address | Any valid individual MAC Address | Specifies the address of the peer MAC entity with which to perform the TDLS Setup process. |
| TDLSSetupRequest | As defined in TDLS Setup Request element | As defined in TDLS Setup Request element | Specifies the proposed service parameters for the TDLS Setup. |
| ResultCode | Enumeration | SUCCESS, REFUSED, INVALID_ PARAMETERS, TIMEOUT |  |

10.3.z1.4.3 When Generated

This primitive is generated by the SME to request that a TDLS Setup Response frame be sent to the initiating STA.

10.3.z1.4.4 Effect of Receipt

On receipt of this primitive, the MLME constructs a TDLS Setup Response action management frame. The STA then attempts to transmit this to the initiating STA.

10.3.z1.5 MLME-TDLSSETUPRESPONSE.confirm

10.3.z1.5.1 Function

This primitive reports the result of a TDLS Setup procedure.

10.3.z1.5.2 Semantics of the Service Primitive

The primitive parameters are as follows:

MLME-TDLSSETUPRESPONSE.confirm(

TDLSSetupResponse

)

| Name | Type | Valid Range | Description |
| --- | --- | --- | --- |
| TDLSSetup- Response | As defined in TDLS Setup Response element | As defined in TDLS Setup Response element | Specifies service parameters for the TDLS Setup. |

10.3.z1.5.3 When Generated

This primitive is generated by the MLME as a result of an MLME-TDLSSETUP.request and indicates the results of the request.

This primitive is generated when the MLME-TDLSSETUP.request contains invalid parameters, when a timeout or failure occurs, or when the STA receives a TDLS Setup Response frame from the AP.

10.3.z1.5.4 Effect of Receipt

On receipt of this primitive, the SME evaluates the Element Status and may use the reported data.

10.3.z1.6 MLME-TDLSSETUPRESPONSE.indication

10.3.z1.6.1 Function

This primitive indicates that a TDLS Setup Request frame was received from a candidate peer STA.

10.3.z1.6.2 Semantics of the Service Primitive

The primitive parameters are as follows:

MLME-TDLSSETUPRESPONSE.indication(

PeerSTAAddress,

TDLSSetupResponse

ResultCode

)

| Name | Type | Valid Range | Description |
| --- | --- | --- | --- |
| PeerSTAAddress | MACAddress | Any valid individual MAC Address | The address of the non-AP STA MAC entity from which a TDLS Setup Request frame was received. |
| TDLSSetup- Request | As defined in TDLS Setup Request element | As defined in TDLS Setup Response element | Specifies the proposed service parameters for the TDLS Setup. |
| ResultCode | Enumeration | SUCCESS, REFUSED, INVALID_ PARAMETERS, TIMEOUT |  |

10.3.z1.6.3 When Generated

This primitive is generated by the MLME when a valid TDLS Setup Response frame is received.

10.3.z1.6.4 Effect of Receipt

On receipt of this primitive the SME should operate according to the procedure in 11.z1.

Add TDLS Teardown

| 373 | Adrian | Stephens | 10 | 32 | 17 | T | Y | "Add TDLS Teardown". This draft is incomplete, witness this text. It should not have gone to letter ballot, as the rules for going to letter ballot require it to be complete and have no avoidable TBDs. This phrase is equivalent to an avoidable TBD. | Add the teardown interface. |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 374 | Clint | Chaplin | 10 | 32 | 17 | T | Y | Ahem. "Add TDLS Teardown" Busted. You're not supposed to send out a draft that isn't complete. | Don't do this again. |  |
| 375 | Ganesh | Venkatesan | 10 | 32 | 17 | T | Y | several primitives missing. | Add the following primitives: TDLS Setup Confirm.Request, .Confirm and .Indication TDLS TeardownRequest.Request, .Confirm, .Indication TDLS TeardownResponse.Request, .Confirm, .Indication Any other that may be required for Peer Power Save |  |
| 376 | Tomoya | Yamaura | 10.3 | 28 | 6 | T | Y | This note seems for me that we still need to wait the text on "DLS Setup Confirm". | Please add text as quick as possible (at the bottom line, include it in D2.0) |  |
| 377 | Tomoya | Yamaura | 10.3 | 27 | 41 | T | Y | There is no description about TDLS Teardown. | Please add text as quick as possible (at the bottom line, include it in D2.0) |  |
| 378 | Bill | Marshall | 10.3.z1 | 27 | 47 | T | y | since the TDLS Setup Request/Response/Confirm are ordinary data frames, they should be generated by the SME and sent using MA-UNITDATA; therefore there is no need for a MLME interface for the SME to tell the MAC to send these frames. | Delete the new sections added to 10.3 |  |
| 379 | Bill | Marshall | 10.3.z1 | 28 | 6 | T | y | the text on this line indicates a lack of technical completeness of the draft, which means it should not have been approved for letter ballot | Add TDLS Setup confirm, or delete all of the change in 10.3 as they are ordinary data packets and not MAC management frames |  |
| 380 | Darwin | Engwer | 10.3.z1 | 28 | 1 | T | Y | This clause defines two 3-primitive services, each one consisting of a set of .request/.confirm/.indication primitives, and together defining a request and response mechanism. This is highly unusual since the two services effectively define a single request/response mechanism. The preferred approach to such a service specification is to define a single service, consisting of a single set of .request/.indication/.response/.confirm primitives. Note that such a 4-primitive service specification does not preclude certain use case scenarios using only a subset of the four primitives. For example, if the .request action failed the result could be direct generation of a .confirm within the requestor, say with an "invalid parameters" or "request timed-out" result code. | Change to two 3-primitive service definitions to a single 4-primitive service definition, e.g., MLME-TDLSSETUP with corresponding .request/.indication/.response/.confirm primitives. |  |
| 381 | David | Hunter | 10.3.z1 | 32 | 17 | T | Y | Need MLME-TDLSTEARDOWN.request and .response primitives. | Add descriptions of MLME-TDLSTEARDOWN.request and .response primitives. |  |
| 382 | David | Hunter | 10.3.z1 | 32 | 17 | T | Y | Need MLME-TDLSDLPATHSWITCH.request and . response primitives. | Add descriptions of MLME-TDLSDLPATHSWITCH.request and .response primitives. |  |
| 383 | David | Hunter | 10.3.z1 | 32 | 17 | T | Y | Need MLME-TDLSAPPATHSWITCH.request and .response primitives. | Add descriptions of MLME-TDLSAPPATHSWITCH.request and .response primitives. |  |
| 384 | Ganesh | Venkatesan | 10.3.z1 | 28 | 6 | T | Y | TDLS Setup Confirm is missing from Figure-z8. The TDLS protocol is incomplete without the Setup Confirm. | Add TDLS Setup Confirm to Figure-z8 |  |
| 385 | Hideyuki | Suzuki | 10.3.z1 | 28 | 6 | T | Y | As editorial notes implies, TDLS Setup Confirm sequence needs to be added. | Add TDLS Setup Confirm sequence. |  |
| 386 | Hideyuki | Suzuki | 10.3.z1 | 32 | 17 | T | Y | As editorial notes implies, TDLS Teardown sequence needs to be added. | Add TDLS Teardown sequence. |  |
| 387 | Jouni | Malinen | 10.3.z1 | 28 | 6 | T | Y | “Add TDLS Setup Confirm” does not sound like an editorial change.. If the figure is missing the use of Confirm, it should be fixed (a technical change).. If not, the editorial note should be removed. | Add the TDLS Setup Confirm, if needed, or remove the editorial note. |  |
| 388 | Rajendra | Kumar | 10.3.z1 |  |  | T | N | Description of MLME primitive for TDLS Setup Confirm is not given | Please provide a description of MLME primitive for TDLS Setup Confirm |  |
| 389 | Rajendra | Kumar | 10.3.z1 |  |  | T | N | Description of MLME primitive for TDLS Teardown Request is not given | Please provide a description of MLME primitive for TDLS Teardown Request |  |
| 390 | Rajendra | Kumar | 10.3.z1 |  |  | T | N | Description of MLME primitive for TDLS Teardown Response is not given | Please provide a description of MLME primitive for TDLS Teardown Response |  |
| 391 | Rajendra | Kumar | 10.3.z1 |  |  | T | N | Description of MLME primitive for TDLS DL Path Switch Request is not given | Please provide a description of MLME primitive for TDLS DL Path Switch Request |  |
| 392 | Rajendra | Kumar | 10.3.z1 |  |  | T | N | Description of MLME primitive for TDLS DL Path Switch Response is not given | Please provide a description of MLME primitive for TDLS DL Path Switch Response |  |
| 393 | Rajendra | Kumar | 10.3.z1 |  |  | T | N | Description of MLME primitive for TDLS AP Path Switch Request is not given | Please provide a description of MLME primitive for TDLS AP Path Switch Request |  |
| 394 | Rajendra | Kumar | 10.3.z1 |  |  | T | N | Description of MLME primitive for TDLS AP Path Switch Response is not given | Please provide a description of MLME primitive for TDLS AP Path Switch Response |  |
| 395 | Rajendra | Kumar | 10.3.z1 |  |  | T | N | Description of MLME primitive for Peer Traffic Indication is not given | Please provide a description of MLME primitive for Peer Traffic Indication |  |
| 396 | Tomoko | Adachi | 10.3.z1 | 27 | 48 | T | Y | As the teardown primitives need to be added, the name of this subclause should be changed to "Management of tunneled direct link". | As in comment. |  |
| 397 | Tomoko | Adachi | 10.3.z1 | 27 | 49 | T | Y | "The following MLME primitives support the signaling of tunneled direct link setup." Not only for setup but teardown. | Change it to "The following MLME primitives support the signaling of tunneled direct links." |  |
| 398 | Tomoko | Adachi | 10.3.z1 | 27 | 49 | T | Y | "Figure z8 depicts the TDSL setup process." It should be noted that the MLME of the AP is not shown because it does take any role. | As in comment. |  |
| 399 | Tomoko | Adachi | 10.3.z1 | 27 | 50 | T | Y | "The figure illustrates the basic protocol, which is only an example and is not meant to be exhaustive of all possible protocol uses." What is this trying to say? Is this something special to the tunneled direct link setup? Or in the same level with other MLME? | Clarify or remove the sentence. |  |
| 400 | Tomoko | Adachi | 10.3.z1 | 28 | 1 | T | Y | When will the TDLS Setup Confirm frame (7.2.2.1.3) be transmitted? No related primitives for this frame? | Remove the TDLS Setup Confirm frame from the draft. |  |
| 401 | Tomoko | Adachi | 10.3.z1 | 32 | 17 | T | Y | "Add TDLS Teardown" | Please do so. |  |
| 402 | Ganesh | Venkatesan | 10.3.z1.1.2 | 28 | 22 | T | Y | Where does TDLSRequestTimeout value specified? Is this part of the TDLS Setup Request? | Clarify. Add TDLS Request Timeout field to the TDLS Setup Request frame (7.2.2.1.1) |  |
| 403 | Ganesh | Venkatesan | 10.3.z1.1.2 | 29 |  | T | Y | "Specifies a time limit (in TU) after which the TDLS Setup procedure is terminated"? Is this a limit for the complete TDLS protocol? i.e. by this time limit a DLS link must be established? Or a time limit before which the initator must see a response from the Peer? | Clarify by expanding on "after which the TDLS Setup procedure is terminated". |  |
| 404 | Ganesh | Venkatesan | 10.3.z1.2.1 | 29 |  | T | Y | MLME-TDLSSETUP.confirm is a result of parsing the request from the SME by MLME and responding back to the SME with a status code. The confirm cannot use the TDLS Setup Response element as defined in 7.2.2.1.2 as information for this frame is available only after the peer responds. Same comment applies to 10.3.z1.5.2 as well. | Replace the parameter TDLSSetupResponse with Status. |  |
| 405 | Darwin | Engwer | 10.3.z1.2.2 | 29 | 25 | T | Y | The TDLSSetupResponse parameter is cited as being "defined in TDLS Setup Response element" which I think would be Table z3 in cl. 7.2.2.1.2, but that would imply a response frame from the acceptor STA. But according to Figure z8 (previous page) this does not happen as part of a MLME-TDLSSETUPREQUEST service. This would therefore seem to be further proof that the two services ought to be specified as a single service using all four primitives. (see other comment by this commentor on the same topic) | Change to two 3-primitive service definitions to a single 4-primitive service definition, e.g., MLME-TDLSSETUP with corresponding .request/.indication/.response/.confirm primitives. |  |
| 406 | Srinivasa | duvvuri | 10.3.z1.2.2 | 29 | 22 | T | Y | refers to wrong type of MLME and also MLME needs more arguments | it should be MLME-TDLSSETUPREQUEST.confirm . the argument TDLSSetpResponse is also wrong. it should be TDLSSetupRequest. It should also contain the args peerSTAAddress, ResultCode indicating SUCCESS. ..etc. The table in the section needs to be updated accordingly. |  |
| 407 | Adrian | Stephens | 10.3.z1.2.3 |  |  | T | Y | "This primitive is generated when the MLME-TDLSSETUP.request contains invalid parameters, when a timeout or failure occurs, or when the STA receives a TDLS Setup Response frame from the AP." This is not consistent with figure z8, which shows the confirm being issued synchronously with the request. Same comment on 10.3.z1.5.3. | Make it consistent. Either replace the response.ind with the request.cfm, or modify this text to say "Generated in response to the request and indicates the status of the parameters in the request". |  |
| 408 | Srinivasa | duvvuri | 10.3.z1.2.3 | 29 | 33 | T | Y | Incorrect statement | the following statement is not correct. "or when the STA receives a TDLS Setup Respinse frame from the AP". this MLME-TDLSSETUPREQUEST.confirm is generated when the TDLS Setup Request frame is succesfully generated , not when the Setup Response Frame is received. there is a separate MLME called MLME-TDLSSETUPRESPONSE.indication is used when a STA receives TDLS Setup Response frame . |  |
| 409 | Ganesh | Venkatesan | 10.3.z1.2.4 | 29 | 37 | T | Y | "On receipt of this primitive, the SME evaluates the Element Status and may use the reported data". Where is the 'reported data' obtained from? | Replace with "On receipt of this primitive, the SME either terminates the TDLS setup, Status indicates failure or starts the TDLS Request Timout timer and awaits a response from the peer, Status indicates success". |  |
| 410 | Bill | Marshall | 10.3.z1.4.1 | 30 | 21 | T | y | MLME-TDLSSETUPRESPONSE.request should request a "Response" frame to be sent instead of another Request frame | change "Request" to "Response" on this line, and also on second row of table that follows line 32 (twice), |  |
| 411 | Bill | Marshall | 10.3.z1.4.4 | 31 | 9 | T | y | TDLS Setup Response is not an action management frame | change to "TDLS Setup Response frame" |  |
| 412 | Michael | Bahr | 10.3.z1.6.3 | 32 | 17 | T | Y | According to the note, TDLS Teardown is missing. | Add text for TDLS Teardown. |  |
| 413 | Bill | Marshall | 10.3.z1.6.4 | 32 | 17 | T | y | the text on this line indicates a lack of technical completeness of the draft, which means it should not have been approved for letter ballot | Add TDLS Teardown, or delete all of the change in 10.3 as they are ordinary data packets and not MAC management frames |  |
| 414 | Darwin | Engwer | 10.3.z1.6.4 | 32 | 17 | T | Y | Editing instructions indicate the need to add a TDLS teardown service definition. Since this definition has not been included in D1.0 it would seem to be lacking. | Add a definition for the TDLS Teardown service by specifying the necessary four primitives. |  |
| 415 | Jouni | Malinen | 10.3.z1.6.4 | 32 | 17 | T | Y | What does the “Add TDLS Teardown” mean here? Is the draft missing some MLME primitives? If yes, the draft is not really yet ready for WG LB.. If not, this note should be removed. | Add the missing MLME primitives or remove the “Add TDLS Teardown” note. |  |
| 416 | Stephen | McCann | 10.3.z1.6.4 | 32 | 17 | T | Y | Regarding the note "Add TDLS Teardown", there is no text. It appears that this draft is not complete. | Add suitable text for TDLS teardown or alternatively remove this editorial comment. |  |