IEEE P802.11
Wireless LANs

| Remove Characteristic Two Curves |
| --- |
| Date: 2008-05-13 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Dan Harkins | Aruba Networks | 1322 Crossman ave, Sunnyvale, CA 94089 United States of America | +1 408 227 4500 | dharkins@arubanetworks.com |

Editor—add the following paragraph to the end of section 7.3.1.1

7.3.1.1 Authentication algorithm number field

When elliptic curve finite cyclic groups are used, elliptic curves over a prime field, Fp, (whose defining equation is written y2 = x3 + ax + b) shall be used.

Editor—add the following paragraph to the beginning of 11B.2.3.1

11B.2.3.1 Elliptic Curve Finite Cyclic Groups

Only elliptic curves over a prime field, Fp, shall used with SAE in this standard. When generating the password element in section 11B.2.3.1.1, the defining equation y2 = x3 + ax + b is used to solve for a y-coordinate using a known x-coordinate.

References:

Federal Information Processing Standard (FIPS) 186-2

http://csrc.nist.gov/publications/PubsFIPS.html

# Text boxes

Abstract

It is required to remove support for characteristic two elliptic curves from the draft. Elliptic curves defined over a prime field continue to be supported and encouraged for use. Examples of such curves include those defined by the United States National Institute of Standards and Technology (NIST).