## Slide 1: VHT60 Tutorial
Date: 2008-07-14
Authors:

## Slide 2: Overview
IEEE 802.11 VHT SG is proposing a PAR for a TG to create an amendment to 802.11 in the 60 GHz band
PAR requires an increase in throughput to at least 1 Gbps, well beyond that of 802.11n
Expected PHY modifications
  New 802.11 clause for 60 GHz PHY
Expected MAC modifications
  Supporting necessary changes to the channel access mechanism specific to the PHY and operating band (directional antennas in 60 GHz)
  Multi-band capability
  Efficiency enhancements

## Slide 3: Market Drivers
Need for Higher TPT standard
Maintain Wired equivalence
GigE is widely deployed
10GigE is emerging
Faster CPUs
Larger and Faster Storage
HD content
SSD Growing 2x a year
>80 GB iPOD and camcorders
DVD Capacity growing 8x
Blue Ray– 50 GB dual layer
Competitive environment driving Proprietary 11n extensions
Proprietary modes fragment the market
Higher Capacity
Gigabit nano-cells free capacity for normal network use
from 11-08/130r1
Notes: doc.: IEEE 802.11-07/2090r0
July 2007
        Eldad Perahia (Intel)
Page <number>

## Slide 4: Applications
Applications discussed in the study group include (many are enhancements of 802.11n applications)
  From Wi-Fi Alliance liaison report:
    Wireless Display
    In Home Distribution of HDTV and other content
    Rapid Upload and Download of large files to/from server
    Backhaul Traffic (e.g. Mesh, Point-to-Point)
    Campus / Auditorium deployments
    Manufacturing Floor Automation
  Usage models from other submissions:
    Wireless local area networking
    High speed cable replacement
    Wireless docking
    Sync and go

## Slide 5: Technology (1/2)
Multi-band as opposed to multi-mode
  Higher frequencies for higher level MCSs
  Fast session transfer between PHYs
  <6 GHz assists 60 GHz
  Maintain the network architecture of the 802.11 system
  Reuse and maintain backward compatibility to 802.11 management plane
<6GHz transmission range
60GHz directional
transmission
from 11-08/349r1

## Slide 6: Technology (2/2)
60 GHz transceiver system with directional antennas can achieve 1 Gbps with ranges exceeding 10 m
from 11-07/2790r0
from 11-07/2790r0

## Slide 7: VHT 60 GHz PAR Scope
The 60 GHz ISM band provides the opportunity for much wider band channels than in <6 GHz enabling single link throughputs greater than 1 Gbps
Two aspects of the PAR ensure distinct identity from 802.15.3c
  Enable fast session transfer between PHYs
  Maintain the 802.11 user experience
Fast session transfer provides seamless rate fall back between VHT and 802.11n for multi-band devices
  Provides expected WLAN coverage from combo 60 + 2.4/5 GHz devices
  Does not mandate multi-band devices
As an amendment to 802.11, VHT maintains the 802.11 user experience
  maintaining the network architecture of the 802.11 system
    E.g. infrastructure basic service set, extended service set, access point, station
  Reuse and maintain backward compatibility to 802.11 management plane
    E.g. association, authentication, security, measurement, capability exchange, MIB
Coexistence
  Coexistence of various systems in the 60 GHz band is an important issue to VHT demonstrated by being explicitly called out in the PAR scope
  Furthermore, the task group will produce a coexistence assurance document

## Slide 8: Related Submissions
VHT Applications, 11-07/2587r0, Gal Basson, Wilocity
Per-User Data Rate, Band and Bandwidth Options for VHT, 11-07/2605r0, Jason Trachewsky, Broadcom
Multi-band Modulation, Coding, and Medium Access Control, 11-07/2780r1, Robert Daniels, The University of Texas at Austin
What Is Happening In 60 GHz, 11-07/2790r0, Sheung Li, SiBEAM
60 GHz vs. 5 GHz Propagation Discussion, 11-07/2793r0, Vinko Erceg, Broadcom
VHT PAR Direction, 11-08/0130r1, Gal Basson, Wilocity
Potential Benefits of Dual-radio VHT Systems, 11-08/0349r1, Harkirat Singh, Samsung
WLAN Overlay with 60 GHz Channels, 11-08/0364r1, John Barr, Motorola
Modifications to the 60GHz PAR & 5 C’s Proposal, 11-08/498r0, Eldad Perahia, Intel
VHT 60 GHz Channel Model Recommendation, 11-08/632r0, Vinko Erceg, Broadcom
Response to 802.15.3c Questions, 11-08/724r0, Eldad Perahia, Intel
Wi-Fi Alliance (WFA) VHT Study Group Usage Models, 11-07/2988r4, Rolf de Vegt, Qualcomm, Chair WFA VHT Study Group
Mapping WFA Usage Models to Operating Bands, 11-08/451r0, Eldad Perahia, Intel
60 GHz PAR & 5C’s, 11-08/806r0