## Slide 1: VHTL6 Tutorial (VHTL < 6 GHz)
Date: 2008-07-13
Authors:

## Slide 2: Overview
IEEE 802.11 VHT SG is proposing a PAR for a TG to create an amendment to 802.11 for below 6 GHz operation excluding 2.4 GHz band
PAR requires a maximum throughput of at least of 1Gbps in multi-STA configuration and 500 Mbps for single link: well beyond that of 802.11n
  500Mbps metric: at a given range to provide a significant higher throughput than IEEE802.11n for a single link communication
  1Gbps metric: at a given range and given throughput for a single link transmission to provide the ability to sustain multiple simultaneous transmissions of this kind resulting in a higher aggregated throughput
Expected MAC and PHY modifications
  Amendment of 802.11 for
    larger bandwidth support
    multi-user support
    backward compatibility and coexistence with IEEE802.11a/n devices

## Slide 3: Market Drivers
Need for Higher TPT standard
Maintain Wired equivalence
GigE is widely deployed
10GigE is emerging
Faster CPUs
Larger and Faster Storage
HD content
SSD Growing 2x a year
>80 GB iPOD and camcorders
DVD Capacity growing 8x
Blue Ray– 50 GB dual layer
Competitive environment driving Proprietary 11n extensions
Proprietary modes fragment the market
Higher Capacity
Gigabit nano-cells free capacity for normal network use
from 11-08/130r1
Evolution of storage/backhaul capabilities and success of Wi-Fi creates demand for higher wireless throughput capabilities combined with an effective management of multi-devices environments (hotspots/corporate/home)
Notes: doc.: IEEE 802.11-07/2090r0
July 2007
        Eldad Perahia (Intel)
Page <number>

## Slide 4: Applications
Applications discussed in the study group include (many are enhancements of 802.11n applications)
  From Wi-Fi Alliance liaison report 11-07/2988r3:
    Wireless Display
    In Home Distribution of HDTV and other content
    Rapid Upload and Download of large files to/from server
    Backhaul Traffic (e.g. Mesh, Point-to-Point)
    Campus / Auditorium deployments
    Manufacturing Floor Automation
  Usage models from other submissions:
    Multimedia, simultaneous transmission of multiple high rate video streams, audio, and on-line gaming, immersive environments and collaborative communications, will drive the need for higher throughput in the home, enterprise and outdoor environments (11-08/609r3)
    IMT-Advanced context: mobile cooperation using Wi-Fi to reinforce and complement cellular (11-08/081r2). Provision the possibility to access new licensed spectrum below 6GHz.
from 11-08/081r2

## Slide 5: Technology (1/2)
Flexible larger bandwidth support: up to 80MHz
  Multichannel CSMA (11-08/307r1)
  Dynamic multiuser OFDM (11-07/2860r0,2062r1)
Serve multiple users at the same time through frequency or space multiplexing: OFDMA/SDMA, network coding
  Access to another source of diversity: multi-user diversity (11-07/2187r1)
from 11-07/2860r0
from 11-07/2062r1
from 11-07/2187r1

## Slide 6: Technology (2/2)
Ensure backward compatibility and coexistence with IEEE802.11a/n in the 5GHz band
Potential access to new spectrum below 6GHz part of the IMT-Advanced 1Gbps nomadic charter (11-07/219r4)
from 11-08/081r2
from 11-08/307r1
MAC
MAC
MAC
PHY
MAC controller
STA
Frequency chunks

## Slide 7: VHTL6 PAR scope
The scope of this project is to define an amendment that shall define standardized modifications to both the 802.11 physical layers (PHY) and the 802.11 Medium Access Control Layer (MAC) so that modes of operation can be enabled that are capable of supporting:
  A maximum multi-STA throughput (measured at the MAC data service access point), of at least 1Gbps and a maximum single link throughput (measured at the MAC data service access point), of at least 500Mbps.
  Below 6GHz carrier frequency operation excluding 2.4GHz operation and ensuring backward compatibility and coexistence with legacy IEEE802.11a/n devices in the 5GHz unlicensed band.

## Slide 8: VHTL6 PAR Scope explanatory notes
The project may include the capability to handle multiple simultaneous communications.
The multi-STA throughput is defined as the sum of the MAC SAP throughputs across all active transmissions within a set of STAs.
The 1Gbps maximum multi-STA throughput may be achieved when considering multiple simultaneously actively-communicating STAs, e.g., a BSS with 1 AP and 3 STAs.
Though the primary metric used in the scope of the project deals with MAC SAP throughput, the intent is to provide enhancements over IEEE802.11n on the following inter-dependent performance indicators: throughput at the MAC data SAP, range of operation, aggregate network capacity (spectrum efficiency), power consumption (peak and average).
Captures infrastructure BSS, IBSS and mesh network topologies
Motivation for including single link throughput metric
  Easier feasibility references: quote 2 technical presentations documents 11-08/0307r1 and 11-08/0535r0
  Meet limited device capabilities expectations
  Give back focus on device and not on a test setup
  Provides 5x improvement in PAR throughput target compared to 11n (11a: 27Mbps MAC SAP -> 11n: 100Mbps i.e. 3.7x increase)
Feasibility of multiple STAs 1Gbps and single link 500Mbps MAC SAP throughput links has been assessed in simulations and presented in documents 11-08-0307-01-0vht (https://mentor.ieee.org/802.11/file/08/11-08-0307-01-0vht-on-the-feasibility-of-1gbps-for-various-mac-phy-architectures.ppt) and 11-08-0535-00-0vht (https://mentor.ieee.org/802.11/file/08/11-08-0535-00-0vht-phy-and-mac-throughput-analysis-with-80-mhz-for-vht-below-6-ghz.ppt) for 80MHz bandwidth operation.

## Slide 9: Related Submissions
VHT Considerations-- submission 11-07/0621r0 by Marc de Courville, Motorola
Draft PAR and 5 Criteria -- submission 11-077/0574r1 by Dengwen Zhu/Darwin Engwer, Nortel
Dynamic Multi-user OFDM for 802.11 systems -- submission 11-07/2062r1 by Marc Emmelmann, Technical University Berlin
Another resource to exploit: multi-user diversity -- submission 11-07/2187r0 by Marc de Courville, Motorola
WLAN Evolution (VHT) Targets and focus areas -- submission 11-07/2194r0 by Naveen K. Kakani, Nokia
IMT-Advanced Status Report -- submission 11-07/2140r3 by Bruce Kraemer, Marvell
Analysis on IEEE 802.11n MAC Efficiency -- submission 11-07/2431r0 by Minyoung Park, Intel Corporation
Probing the will of the SG -- submission 11-07/2472r0 by Marc de Courville, Motorola
Wi-Fi Alliance (WFA) VHT Study Group Usage Models, 11-07/2792, presented by Rolf De Vegt, Qualcomm
Efficiency of VoIP on 802.11n, 11-07/2704, presented by Darwin Engwer, Nortel Networks
60 GHz vs. 5 GHz Propagation Discussion, 11-07/2793, presented by Vinko Erceg, Broadcom
Performance Comparison of Dynamic OFDM with 802.11n, 11-07/2860, presented by James Gross, Technical University Berlin
VHT in Below 6 GHz Frequency Bands, 11-07/2861, presented by Vinko Erceg, Broadcom
Wi-Fi Alliance (WFA) VHT Study Group Usage Models, 11-07/2988r0, presented by Rolf De Vegt
Legacy Coexistence – A Better Way?, 11-07/3001r1, presented by Brian Hart
Mobile cooperation usage models, 11-08/0081r2, presented by Marc De Courville
IMT.Advanced aligned scope proposal, 11-08/0121, presented by Marc De Courville
On the feasibility of 1Gbps for various MAC/PHY architectures, 11-08/0307r1, Roberta Fracchia
Coexistence Mechanisms at 5 GHz, 11-08/0315r1, Brian Hart
PAR & 5C’s proposal discussion lead by Marc de Courville 11-08/0219r4
Wi-Fi Alliance (WFA) VHT Study Group Usage Models, 11-07-2988r4, presented by Rolf de Vegt