IEEE P802.11
Wireless LANs

| LB133 CID 101 Proposed Resolution Text |
| --- |
| Date: 2008-08-13 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Dorothy Stanley | Aruba Networks | 1322 Crossman Ave Sunnyvale, CA 94089 | +1-630-363-1389 | dstanley@arubanetworks.com |

Change bullet f in 11.2.1.5 as follows:

- When dot11MgmtOptionFBMSEnabled is set to false, iImmediately after every DTIM, the AP shall transmit all buffered group addressed MSDUs. 

When dot11MgmtOptionFBMSEnabled is set to true and the AP has set up an FBMS delivery interval for a multicast stream, the AP shall transmit all group addressed frames belonging to particular FBMS Element immediately after the DTIM with the Current Count field value of FBMS Counter field set to 0 for that particular FBMS stream. If any of the associated STAs are using FBMS then the EOSP field of each group addressed frame shall be set to 0 if and only if there are buffered group addressed MSDUs belonging to the group address of that particular frame. 

The More Data field of each group addressed frame shall be set to 1 to indicate the presence of further buffered group addressed MSDUs. If the AP is unable to transmit all of the buffered group addressed MSDUs before the primary or secondary TBTT following the DTIM, the AP shall indicate that it will continue to deliver the group addressed MSDUs by setting set the bit for AID 0 (zero) in the bit map control field of the TIM element of every Beacon frameTIM element to 1 for a single BSSID or the corresponding group address bit is set to 1 for multiple BSSIDs, as defined in 7.3.2.6 and when dot11MgmtOptionFBMSEnabled is set to true, by setting the FBMS Descriptor information element to indicate to which group addresses there are still buffered frames, until all buffered group addressed frames have been transmitted.

When the AP transmits an STBC DTIM or TIM Beacon frame, the AP shall retransmit all group addressed frames that were transmitted following the non-STBC DTIM or TIM Beacon frame except that they are transmitted using the basic STBC MCS. It may be the case that a complete set of buffered group addressed frames is sent over a period of time during which non-STBC and STBC transmissions are interleaved, but the transition from non-STBC group addressed transmissions to STBC group addressed transmissions shall be preceded by the transmission of an STBC Beacon frame and the transition from STBC group addressed transmissions to non-STBC group addressed transmissions shall be preceded by the transmission of a non-STBC Beacon frame.

References:

# Text boxes

Abstract

This document contains the proposed resolution for TGv LB 133 CID 101.