IEEE P802.11
Wireless LANs

| “OSQAP” and OBSS Requirements |
| --- |
| Date: 2008-11-03 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Graham Smith | DSP Group | 2491 Sunrise Blvd, #100, Rancho Cordova CA 95742 | 916 851 9191 x209 | Graham.smith@dspg.com |

# Introduction

The P802.11aa PAR has an item in its scope for “Increased robustness in overlapping BSS environments, without the requirement for a centralized management entity”.  An overlapping BSS is defined as two or more BSSs that are operating on the same centre frequency in radio range of each other.

This document contains a list of the technical requirements/criteria for improved overlapping BSS coexistence against which proposals can be evaluated.

The “OSQAP” solution is evaluated against each criterion.

# Criteria Comparison for “OSQAP”

The “OSQAP” proposal is evaluated against each of the criteria listed in 08/0944r4.

- Enables improved Quality of Service

When a video transport stream has been accepted, additional traffic from other BSSs should not cause the video transport stream to fail to meet its QoS requirements.
COMPLIES
The QAPs can exchange information on their respective QLoads and share the bandwidth accordingly.  A new stream may only be admitted if the sharing APs know that there is enough bandwidth to handle it.

It is not required to provide OBSS protection for video transport streams that have not used an admission control protocol.
COMPLIES
“OSQAP” depends upon the exchange of QLoads which are derived from TSPECs.

Should improve network performance when there are overlapping BSS
COMPLIES
Provides mechanism for APS to communicate.

Contention based medium access protocols

Pre-11aa EDCA-AC admissions shall be preserved
COMPLIES
No change to the basic EDCA Admission Control is proposed

Shall support a mechanism to avoid beacon collision and multicast collision
NOT ADDRESSED

Controlled medium access protocols

Shall support protection for controlled medium access reservations
COMPLIES
Includes proposals for TXOP scheduling exchanges and control

Shall support a mechanism to avoid beacon collision and multicast collision
NOT ADDRESSED

Inter-AP communication for improved OBSS robustness

If inter-AP communication is required, it shall be possible to perform this communication using the WM.
COMPLIES
Proposes use of Wireless DS QoS CF-Polls to communicate between APs

If inter-AP communication is required, it should be possible to perform this communication using the DS.
NOT ADDRESSED but probably complies
he same information used in the WDS QoS CF-Polls could be sent using the DS

Shall be resistant to denial of service and other attacks and provide mitigation against such attacks.
NOT ADDRESSED

Management

Shall not mandate that an AP to be configured as the supervisor controller, e.g. providing a centralized admission control function, or a timing reference
COMPLIES
The “Supervisor” QAP is a dynamic function, not pre-set.

If the solution requires an AP to be automatically chosen as supervisor, it shall be robust to signal fade and AP removal May support configuration of a supervisor controller 
COMPLIES
The proposal includes mechanism to account for the Supervisor AP being removed.

Shall provide a mechanism to control the dynamic aspects (as described in section 6)  of overlapping BSSs
COMPLIES (see 6)

Dynamic

User experience shall be invariant to the order in which APs are switched on or off
COMPLIES
Mechanisms are provided for when APs may be switched off

Removal of an AP shall not cause video streams in other BSSs to terminate
COMPLIES

Shall support dynamic stream creation and deletion
COMPLIES
No changes to the basic functions of EDCA Admsiion Control and HCCA are proposed

When it is necessary to exchange information to achieve performance requirements, this should maintain the current 802.11 levels of  privacy and security
NOT ADDRESSED but probably complies

Fairness, Cooperation and Coexistence

For each 802.11 medium access mechanism, the right to access the WM shall be comparable with the currently provided levels of fairness.
COMPLIES
No changes to the medium access mechanisms are proposed

If the solution requires an AP to be chosen as supervisor, the act of providing the supervisor role does not gain increased priority in medium time allocation over other overlapping BSS.
COMPLIES
The sharing rules are probably out-of-scope but there is no implicit advantage in priority given to the Supervisor AP

The division of time may differ in each BSS, due to differing loads in each BSS.
COMPLIES

The solution should include mechanisms to limit allocations based upon total capacity of the WM.
COMPLIES
The mechanism is provided to allow APs to share with knowledge of each others requirements.

The solution should not significantly reduce the total system throughput nor significantly increase the delay or jitter compared to legacy non-11aa systems.
COMPLIES

ESS / BSS

The solution shall support overlapping BSS that are in the same ESS
COMPLIES

The solution shall support overlapping BSS that are in different ESSs
COMPLIES

Security

The solution shall not require the reduction in the security policy of a BSS
COMPLIES

The solution shall be as robust to attacks from rogue APs / non-AP STAs as legacy non-11aa systems
NOT ADRESSED

Compatible with legacy non-11aa equipment

The solution shall be tolerant of legacy non-11aa non-AP STAs
COMPLIES
There is no fundamental change required for an EDCA Admission Control non-AP STA.  The QAP can ‘learn’ the QLoad from actual TSPECs.  An 11aa non-AP STA may be able to have the ability to send the ‘zero inactivity period’ TSPEC

The solution should be tolerant of legacy non-11aa APs
COMPLIES.
The proposal tries to avoid legacy APs.  If sharing with a legacy AP, the legacy AP is at no more disadvantage that if it were sharing with a non-11aa QAP.

The solution should improve the performance of an 11aa BSS in the presence of overlapping non-11aa BSSs while still coexisting with them.
DEPENDS
The proposal tries to avoid legacy non-11aa APs.  For Admission Control the “OSQAP” could take note of the Loads in the other network and take account.  For HCCA there is the existing advantage.  In practice all HCCA QAPs could be 11aa and this would greatly improve the performance of an Admission Control QAP.

Provides a mode of operation that minimizes the potential for requiring hardware modifications
COMPLIES
It is believed that the OSQAP proposal does not require any hardware modifications.

Frequency bands

The solution shall support any frequency band in which 802.11 operates
COMPLIES

The solution shall support any 802.11 physical layer with the possible exception of infra-red and frequency hopping
COMPLIES

Diagnostics

The solution shall provide a mechanism to enable metrics on the current performance of the OBSS solution
COMPLIES – Sort of
The QLoad IE provides a measurement of the overlapping networks.

# Text boxes

Abstract

Document 08/0944r4 contains the requirements for any OBSS solution as discussed and agreed by the 11aa task group.

This document compares the proposed OBSS Solution for QAPs-“OSQAP” against those requirements.