IEEE P802.11
Wireless LANs

| Dec 2008-Jan 2009 Teleconference Meeting Minutes |
| --- |
| Date: 2008-03-09 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Ganesh Venkatesan | Intel Corporation | 2111NE 25th Ave, Hillsboro, OR 97124 | 503 334 6720 | ganesh.venkatesan@intel.com |

Agenda:

- Administrivia

  - Questions on IEEE SA Policies and Procedures -- none

  - Essential Patents or knowledge of holders of Essential Patents -- none

- Review of joint meeting material (if needed)

- OBSS

  - 09/285r0

  - 09/230r0

  - 08/1470r4

OBSS Presentations:

09/285r0 -- Andrew Myles

(*) Channel allocation in typical/realistic scenarios result in long chains (more than 3 overlapping BSSs)

(*) APs can come and go randomly

(*) Algorithms to get to a configuration of BSSs with minimal chain length

(*) What is the settling time?

(*) 5GHz -- OBSS is not a serious problem yet

Solution must need marketing needs

A complete solution may be over-engineering

If a solution for chain length 3-4 is specified -- this may be good

(*) A chosen solution should provide enough benefit for the implementation complexity

(*)  APs coming ON/OFF is not common. APs are usually always ON. If all APs come on at the same time, settling time may be an issue

(*) Does channel selection algorithm use 'traffic load' as a parameter? No

(*) Does the 'intolerant bit' apply to the 5GHz band?

(*) How is extent defined? Need to harmonize on definitions

08/1470r4 -- Graham Smith

(*) Proper Channel selection avoids getting into OBSS

(*) TGaa may need a mechanism to drop to 20 MHz

(*) Transmit Power Control -- also mitigates OBSS

(*) Bullet-3 of summary slide (#33) contradicts the previous (09/285r0) presentation

(*) How does the presence of non-TGaa AP affect the simulation results? -- slide #22 shows it (makes the OBSS problem worse)

(*) Dropping to 20MHz maybe good for video. But what about the case where the BSS is doing both video and data?

(*) We need to handle cases where there are up to 8 APs overlapping

(*) EDCA to EDCA-AC reduces contention --> this is better. However HCCA to HCCA with OBSS is a cliff down in performance -- makes user disappointed

09/230r0 -- Graham Smith

(*) Are we reserving medium time? Isn't this a problem? Reserving medium time that may not be used (and limiting others from using the otherwise available medium) is bad.

You have to trade-off flexibility in using the medium on demand with the expectations on guaranteed bandwidth.

One could build policies around this -- 802.11aa would provide mechanisms to exchange appropriate data. A policy engine can enforce rules based on policies and values for pertinent data.

(*) A better method as an alternate to reserving medium time apriori is needed -- Voice over Wi-Fi was mentioned as an example.

(*) The mechanism outlined in document 09/230r0 does not extend to the case of 8 overlapping BSSs -- it does. However, it does not support the case of 8 overlapping BSSs where all of them are using HCCA. When 3 HCCA BSSs are detected and it is determined that the 3rd AP coming into this set cannot use HCCA, the 3rd AP will backoff  from HCCA and use EDCA-AC

(*) The OBSS requirements document (08/944r7) requires the mechanism/solution specified for OBSS in TGaa be limited to 4 overlapping BSSs. This has to be revisited in the context of 09/285r0 and 08/1470r4.

(*) Channel selection procedure -- there seems to be many different ways of doing this -- the discussion was prematurely aborted due to lack of time. It will be resumed in the Tuesday AM1 meeting.

The ad hoc meeting adjourned at 1402 Hrs EDT.

# Text boxes

Abstract

This document contains minutes of TGaa Ad Hoc meeting on Monday Mar 09, 2009 (1100-1400 Hrs EDT)