IEEE P802.11
Wireless LANs

| LB-142 Network Type Update |
| --- |
| Date: 2009-03-09 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Dave Stephenson | Cisco Systems, Inc. | 170 W. Tasman Dr. San Jose, CA 95134 | +1 408 527 7991 | daves@cisco.com |

3	Definitions

Insert the new definition alphabetically re-numbering as necessary

3.u.x network type:  the primary conditions under which a user or subscriber will access an IEEE 802.11 network.  For example, an enterprise network has a condition of access of private network and users, which are employees of the enterprise, would expect to have user accounts to access the network and that other users will also be employed by the enterprise.

7	Frame formats

7.3	Management frame body components

7.3.2	Information elements

7.3.2.83	Interworking information element

Change the text as shown below

The Network Types are shown in Table 7-43bt. It is set by AP to advertise its Network Type to non-AP STAs. A non-AP STA uses this field to indicate the desired Network Type in an active scan. See Annex V.1 for informative text on usage of fields contained within the Interworking element.

Table 7-43bt—Network Type codes

| Network Type Codes | Meaning | Description |
| --- | --- | --- |
| 0 | Private network | Non-authorized users are not permitted on this network. Examples of this network type are home networks and enterprise networks, which may employ user accounts. These networks may or may not employ encryption. |
| 1 | Private network with guest access | Private network but guest accounts are available. Examples of this network type are enterprise networks offering access to guest users. |
| 2 | Chargeable public network | The network is accessible to anyone, however, access to the network requires payment. Further information on types of charges may be available through other methods (e.g., 802.21, http:/https redirect or DNS redirection). Examples of this network type is a hotspot in a coffee shop offering internet access on a subscription basis or a hotel offering in-room internet access service for a fee. |
| 3 | Free public network | The network is accessible to anyone and no charges apply for the network use. An example of this network type is an airport hotspot or municipal network providing free service. |
| 4 | Personal Device Network | A small network of personal devices such as camera and computer. An example of this type of network is a camera attaching to a printer, thereby forming a network for the purpose of printing pictures. |
| 5 to 13 | Reserved | Reserved |
| 14 | Test or experimental | The network is used for test or experimental purposes only. |
| 15 | Wildcard | Wildcard network type |

# Text boxes

Abstract

This submission addresses CID 5009.

This document is based on 802.11u-d5.0.