IEEE P802.11
Wireless LANs

| TGac Functional Requirements and Evaluation Methodology Rev. 0 |
| --- |
| Date: 2009-04-09 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Peter Loc | Ralink Technology | 20833 Stevens Creek Blvd, Suite 200., Cupertino CA 95014 | 408 807-0868 | peterloc@gmail.com |
| Minho Cheong | ETRI | 161 Gajeong-dong, Yuseong-gu, Daejeon, Korea | +82 42 860 5635 | minho@etri.re.kr |

# 1. Overview

This document specifies the functional requirements for TGac as stated in the VHT below 6 GHz PAR Plus 5C’s. The emphasis is on the following aspects of TGac devices

- System performance

- Backward compatibility with 802.11a/n devices operating in 5 GHz

- Coexistence with 802.11a/n devices operating in 5 GHz

- Compliance to PAR

This document also specifies the evaluation methodology for TGac devices.

# 2. Functional Requirements

# 2.1 System Performance

2.1.1 Supporting band

TGac R1 - TGac devices shall operate in 5GHz frequency band.

2.1.2 Max multi-STA throughput measured at the MAC SAP to be at least 1 Gbps.

TGac R2 - TGac devices shall demonstrate a mode of operation that supports an aggregate throughput of at least 1 Gbps at the top of the MAC data service access points (MAC SAPs) utilizing no more than 80 MHz of channel bandwidth in 5GHz band. There is no restriction on the number of transmit or receive antennas being used on any devices.

A typical test scenario may include multiple STAs that are simultaneously and actively communicating with an AP in 5 GHz band. Note that the PAR gives an example of an AP simultaneously actively-communicating with 3 STAs in the explanatory note. However, the number of STAs may actually be 2 or more in a test set up.

2.1.3 Max single-STA throughput measured at the MAC SAP to be at least 500 Mbps.

TGac R3 - TGac devices shall demonstrate a mode of operation that supports a throughput of at least 500 Mbps at the top of the MAC data service access point (MAC SAP) utilizing no more than 80 MHz of channel bandwidth in 5GHz band. There is no restriction on the number of transmit or receive antennas being used on AP or STA.

A typical test scenario includes a single STA actively communicating with an AP in 5 GHz band.

2.1.4 Spectrum efficiency

TGac R4 - In the highest throughput mode, TGac devices shall achieve a spectral efficiency of at least 7.5 bps/Hz for the PSDU.

How we calculate this: TGn requirement is 100 Mbps and at least 3 bps/Hz utilizes up to 40 MHz of bandwidth

TGac requirement for single link throughput is at least 500 Mbps uses up to 80 MHz bandwidth (5 times TGn @ 2 times BW). Therefore bps/Hz = 2.5 * 3 = 7.5

2.1.5 802.11e QoS support

TGac R5 - The proposal shall support the QoS enhancements of the IEEE802.11-2007 within a TGac STA.

2.1.6 Control of support for 802.11a/n STA from TGac AP

TGac R6 – TGac AP can be configured to reject or accept associations from 802.11a/n STAs.

## 2.2 Backward Compatibility

2.2.1 802.11a backward compatibility

TGac R7- TGac devices shall ensure backward compatibility with IEEE802.11a devices operating in the 5 GHz frequency band.

A test scenario may include an 802.11a device successfully associated and passing traffic with a TGac device.

2.2.2 802.11n backward compatibility

TGac R8- TGac devices shall ensure backward compatibility with IEEE802.11n devices operating in the 5 GHz frequency band.

A test scenario includes an 802.11n device successfully associated and passing traffic with a TGac device.

# 2.3 Coexistence

TGac R9 - TGac devices provide mechanisms to enable coexistence and spectrum sharing with IEEE802.11a/n devices operating in the same frequency band.

# 2.4 Compliance to PAR

TGac R10 - The proposal complies with the PAR and 5 Criteria [1].

# 3. Evaluation Methodology

The evaluation methodology defines PHY performance, conditions for PAR compliance and a limited set of simulation scenarios and comparison criteria for TGac evaluatation.

As TGac agreed on the approach outlined in the 802.11/09/0376r1, the evaluation methodology for TGac can be build up based on 802.11n one by some modifications.

# 3.1 PHY Performance

3.1.1 PHY channel model

Channel models defined in 802.11n channel model document [8] shall be used. Channel model G for corridor environments is newly included and AoA and AoD diversity are also considered for TGac [11].

3.1.2 PHY impairments

PHY impairments are updated from ones desribed in 802.11n comparison criteria document [7].

| Number | Name | Definition | Comments |
| --- | --- | --- | --- |
| IM1 | PA non-linearity | Simulation should be run at an oversampling rate of at least 4x. Use RAPP power amplifier model as specified in document 00/294 with p = 3. Calculate backoff as the output power backoff from full saturation: PA Backoff = ­10 log10(Average TX Power/Psat). Total TX power shall be limited to no more than 17 dBm. Disclose: (a) EIRP and how it was calculated, (b) PA Backoff, and (c) Psat per PA. Note: the intent of this IM is to allow different proposals to choose different output power operating points. Note: the value Psat = 25dBm is recommended. | Unchanged fron 802.11n |
| IM2 | Carrier frequency offset | Single-user simulations for all comparisons except Offset Compensation shall be run using a fixed carrier frequency offset of –13.675 ppm at the receiver, relative to the transmitter. The symbol clock shall have the same relative offset as the carrier frequency offset. Simulations shall include timing acquisition on a per-packet basis. Multi-user simulations for all comparisons except offset compensation shall be run using a fixed carrier frequency offset selected from the array [N(1) ,N(2),……,N(16) ], relative to the transmitter, where N(j) corresponds to the frequency offset of the j-th client and is randomly chosen from [-20,20] ppm with a uniform distribution. We can assume that a maximum of 16 clients may be served simultaneously in a multi-user simulation. | Added a set of possible offsets to be used for several STAs. 802.11n specified a single offset of -13.67 ppm |
| IM4 | Phase noise | The phase noise will be specified with a pole-zero model. PSD(0) = -100 dBc/Hz pole frequency fp = 250 kHz zero frequency fz = 7905.7 kHz Note, this model results in PSD(infinity) = -130 dBc/Hz Note, this impairment is modeled at both transmitter and receiver. | Unchanged from 802.11n |
| IM5 | Noise figure | Input referred total noise figure from antenna to output of the A/D will be 10dB. | Unchanged from 802.11n |
| IM6 | Antenna Configuration | The antenna configuration at both ends of the radio link shall be a uniform linear array of isotropic antennas with separation of one-half wavelength, with an antenna coupling coefficient of zero. All antennas shall have the same vertical polarization. The antennas are assumed to either be all vertically polarized or a mix of vertical and horizontal polarizations, as specified in the TGac channel model addendum document [11] | Mix of vertically and horizontally polarized antennas is considered for TGac devices |

3.1.3 Comparison criteria

- PER vs. SNR curves

- all MCS’s

- Simulate all of channel models

- Simulation must include:

- updated PHY impairments

- timing acquisition on a per-packet basis

- preamble detection on a per-packet basis

# 3.2 Traffic Models

TGac evaluation shall consider traffic models defined 802.11n usage model documents [3] including lightly-compressed video and high-speed file transfer.

| Num. | Application | Offered Load (Mbps) | Protocol | MSDU Size (B) | Max. PLR | Max. Delay (ms) | Source [ref] |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Lightly-compressed video | 150 | UDP | TBD | 10^-7 | 10 | Motion JPEG2000 |
| 2 | Lightly-compressed video | 200 | UDP | TBD | 10^-7 / 8 | 20 | H.264 |
| 3 | DV Audio/video | 28.8 | UDP | 1024, Is this true? All other video/audio (SDTV, HDTV) transfers has this parameter set to 1500. | 10^-7 (corresponds to a rate of 0.5 loss/hour) | 200 | SD Specifications of Consumer-Use Digital VCRs Max PLR: 15-03-276r0 |
| 4 | VoD control channel | 0.06 | UDP | 64 | 10^-2 | 100 | Guess |
| 5 | SDTV | 4-5 | UDP | 1500 | 5*10^-7 | 200 | 1 |
| 6 | HDTV (Video/Audio) | 19.2-24 | UDP | 1500 | 10^-7 | 200 | 1 |
| 7 | DVD | 9.8 peak | UDP | 1500 | 10^-7 | 200 | 1 |
| 8 | Video Conf | 0.128 - 2 | UDP | 512 | 10^-4 | 100 | 1 |
| 9 | Internet Streaming video/audio | 0.1 – 4 | UDP | 512 | 10^-4 | 200 | 1 |
| 10 | Internet Streaming audio | 0.064~0.256 | UDP | 418 | 10^-4 | 200 | Group guess |
| 11 | VoIP | 0.096 | UDP | 120 | 5% | 30 | ITU-T G.114 300ms round-trip delay G.711 Codec |
| 12 | Reserved |  |  |  |  |  |  |
| 13 | Reserved |  |  |  |  |  |  |
| 14 | MP3 Audio Other formats are taking over (AAC/MPEG-4, OggVorbis, etc) | 0.064 – 0.32 | UDP | 418 | 10^-4 | 200 | 1 |
| 14.5 | Reserved |  |  |  |  |  |  |
| 15 | Content download (photo camera) | 11 | TCP | 1500 | N/A |  | Corresponds to USB and flash speed |
| 16 | Internet File transfer (email, web, chat) | 1 | TCP | 300 | N/A |  |  |
| 17 | Local File transfer, printing | 50 | TCP | 1500 | N/A |  | Aps guess |
| 18 | Interactive Gaming [Controller to Console x 1] | 0.5 | UDP | 50 | 10^-4 | 16 | 2 |
| 19 | Interactive Gaming [Console to Display] | 100+ | UDP | 1500 | 10^-2 | 10 | 2 video image: 320x240x15 @ 60Hz |
| 20 | Interactive Gaming [Console to Internet Access] *NOTE : Depends on Game Type | 1 | UDP | 512 | 10^-4 | 50ms | Group consensus |
| 21 | Netmeeting application/desktop sharing | 0.5 | TCP | 512 | N/A |  | Group guess |
| 22 | Reserved |  |  |  |  |  |  |
| 23 | Reserved |  |  |  |  |  |  |
| 24 | Reserved |  |  |  |  |  |  |
| 25 | Video phone | 0.5 | UDP | 512 | 10^-2 | 100 | Aps guess |
| 26 | Remote user interface (X11, Terminal Server Client) (remote display/keyboard/mouse) | 0.5-1.5 (peak) | UDP | 700 | N/A | 100 | 11-03-0696r0 |

ref.) High-quality video service requirements for VHT [12]

| Video Compression |  | Description | Rate, Mbps | Packet Error Rate | Jitter, ms | Delay,ms |
| --- | --- | --- | --- | --- | --- | --- |
| Uncompressed | 720p | (RGB): 1280x720 pixels, 24bits/pixels,60frames/s | 1300 | 10^-8 | 5 | 5 |
|  | 1080i | (RGB): 1920x1080/2pixels, 24bits/pixels,60frames/s | 1300 | 10^-8 |  |  |
|  | 1080p | (YCrCb): 1920x1080 pixels, 12bits/pixels,60frames/s | 1500 | 10^-8 |  |  |
|  | 1080p | (RGB): 1920x1080 pixels, 24bits/pixels,60frames/s | 3000 | 10^-8 |  |  |
| Lightly Compressed |  | Motion JPEG2000 H.264 | 150 70 - 200 | 10^-7 10^-7 / 8 | 10 20 | 10 20 |
| Compressed |  | Blu-ray™ | 50 | 10^-7 | 20 | 20 |
|  |  | HD MPEG2 | 20 | 3x10^-7 | 20 | 20 |

# 4. Simulation Scenarios

Simulation scenarios for TGac evaluation are summarized as:

| Scenario Number | Purpose | Note |
| --- | --- | --- |
| 1 | Test compliance to PAR. | Single STA 500Mbps throughput at the MAC SAP |
| 2 | Test compliance to PAR. | Multi STA 1Gbps throughput at the MAC SAP |
| 3 | Test backward compatibility to 802.11n. | Single 802.11n STA 100Mbps throughput at the MAC SAP |
| 4 | Test backward compatibility to 802.11n with mixed 802.11n and TGac STAs. | Single 802.11n STA at 100Mbps throughput at the MAC SAP + Single TGac STA with 250Mbps throughput at the MAC SAP. |
| 5 | In-home entertainment application. | Multiple flows with varied QoS requirements Includes several lightly-compressed video flows. Aligns with Category 1 and Category 2 applications. |
| 6 | Enterprise network | Stress test for TGac operation. Scenario with large number of flows. Aligns with Category 2 and Category 3 applications. |

# 4.1 Test for Compliance to PAR

4.1.1 Point-to-point link test (scenario #1)

Synthetic test case to demonstrate single STA 500Mbps throughput at the MAC SAP.

This scenario is derived from scenario #19 defind in 802.11n usage model document.

Two stations

One TGac AP is source.

One TGac STA is sink.

Traffic from AP to STA

Protocol: UDP

Offered load : infinite

MSDU size: TBD

PHY channel model

Channel model B

Locations of stations

Fixed locations: (0,0) meters for AP and (0,10) meters for STA

Meet requirements in [functional requirements Sections 2.1.3]

4.1.2 Point-to-multi-point link test (scenario #2)

Synthetic test case to demonstrate multi STA aggregated 1Gbps throughput at the MAC SAP.

This scenario is also derived from scenario #19 defind in 802.11n usage model document.

Five stations

One TGac AP is source

Four TGac STAs are sinks

Traffic from AP to STA

Protocol: UDP

MSDU size: TBD

PHY channel model

Channel model B

Locations of stations

Fixed locations

Meet requirements in [functional requirements Sections 2.1.2]

| Flow No. | Source | Source Location (meters) | Sink | Channel Model | Sink Location (meters) | Application | Bit Rate (Mbps) | Rate Distribution | MSDU Size (B) | Max Delay (ms) | PLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Downlink Flows |  |  |  |  |  |  |  |  |  |
| 1 | AP | (0,0) | STA1 | B | (0,10) | Data | 250.00 | Constant, UDP | TBD | N/A | 0 |
| 2 | AP | (0,0) | STA2 | B | (10,0) | Data | 250.00 | Constant, UDP | TBD | N/A | 0 |
| 3 | AP | (0,0) | STA3 | B | (6,8) | Data | 250.00 | Constant, UDP | TBD | N/A | 0 |
| 4 | AP | (0,0) | STA4 | B | (-6,-8) | Data | 250.00 | Constant, UDP | TBD | N/A | 0 |

# 4.2 Test for Backward Compatibility to 802.11n

4.2.1 Test for backward compatibility to 802.11n (scenario #3)

Synthetic test case to demonstrate 100Mbps throughput to a single 802.11n STA at the MAC SAP.

This scenario is derived from scenario #18 defind in 802.11n usage model document.

Two stations

One TGac AP is source

One 802.11n STA is sink

Traffic from AP to STA

Protocol: UDP

MSDU size: 1500

PHY channel model

Channel model B

Locations of stations

Fixed locations

Meet requirements in 802.11n functional requirements No. 1 in Section 2 [2].

| Flow No. | Source | Source Location (meters) | Sink | Channel Model | Sink Location (meters) | Application | Bit Rate (Mbps) | Rate Distribution | MSDU Size (B) | Max Delay (ms) | PLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Downlink Flows |  |  |  |  |  |  |  |  |  |
| 1 | AP | (0,0) | STA1 (11n) | B | (0,10) | Data | 100.00 | Constant, UDP | 1500 | N/A | 0 |

4.2.2 Test for backward compatibility to 802.11n with mix 802.11n and TGac (scenario #4)

Synthetic test case to demonstrate throughput sharing between a 802.11n STA (100Mbps) and a TGac STA (250Mbps).

This scenario is derived from scenario #19 defind in 802.11n usage model document.

Three stations

One TGac AP is source.

One TGac STA is sink.

One 802.11n STA is sink

Traffic from AP to STA

Protocol: UDP

MSDU size: 1500

PHY channel model

Channel model B

Locations of stations

Fixed locations

Meet requirements in 802.11n functional requirements No. 1 in Section 2 [2].

| Flow No. | Source | Source Location (meters) | Sink | Channel Model | Sink Location (meters) | Application | Bit Rate (Mbps) | Rate Distribution | MSDU Size (B) | Max Delay (ms) | PLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Downlink Flows |  |  |  |  |  |  |  |  |  |
| 1 | AP | (0,0) | STA1(11n) | B | (0,10) | Data | 100.00 | Constant, UDP | 1500 | N/A | 0 |
| 2 | AP | (0,0) | STA2(11ac) | B | (10,0) | Data | 250.00 | Constant, UDP | TBD | N/A | 0 |

# 4.3 In-Home Entertainment Application (scenario #5)

Test case to demonstrate in-home entertainment application with multiple flows with varied QoS requirements including lightly-compressed video.

This scenario is derived from scenario #1 defind in 802.11n usage model document.

11 stations

One TGac AP is source and sink.

10 STAs are souces and sinks. (STA2 is reserved)

Traffic from AP to STAs

Lightly-compressed video, Internet file, VoIP, Internet streaming video, MP3 audio

Traffic from STAs to AP

VoD control channel, VoIP, console to Internet

Traffic STAs to STAs

Local file transfer, video phone, controller to console

PHY channel for each link

Channel model type applied : TBD

Only channel model B’s or mixing B’s and D’s for more realistic scenario

Channel model break point (unchanged from 802.11n scenarios)

Distance between STAs can be used to select between LOS and NLOS according to the breakpoint distance defined in 802.11n channel model document [8].

e.g.) 5 meters for model B and 10 meters for model D

Shadowing term is 0dB (unchanged from 802.11n scenarios)

In 802.11n channel model document [8], shadow fading std. dev. is specified for each channel model between 3dB and 6dB at page 7.

In 802.11n usage model document [3], shadowing term applied to all the 802.11n simulation scenarios is set to 0dB for generating a channel realization at page 22.

Locations of stations

Fixed locations (unchagend from 802.11n scenario #1)

Meet requirements specified in PLR and Max. Delay per each flow

Total throughput condition

Total throughput (about 465Mbps) is not a heavy burden similar to that of scenario #1 defined in 802.11n usage model document (about 64Mbps).

| Flow No. | Source | Source Location (meters) | Sink | Sink Location (meters) | Channel Model | Application | Bit Rate (Mbps) | Rate Distribution | MSDU Size (B) | Max. Delay (ms) | PLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Downlink Flows |  |  |  |  |  |  |  |  |  |
| 1 | AP | (0,0) | STA1 | (0,5) |  | LC Video | 150.00 | Constant, UDP | TBD | 10 | 10^-7 |
| 2 | AP | (0,0) | STA3 | (5,0) |  | LC Video | 150.00 | Constant, UDP | TBD | 10 | 10^-7 |
| 3 | AP | (0,0) | STA4 | (-7,7) |  | LC Video | 150.00 | Constant, UDP | TBD | 10 | 10^-7 |
| 4 | AP | (0,0) | STA4 | (-7,7) |  | Internet file | 1.00 | TCP | 300 | Inf. | N/A |
| 5 | AP | (0,0) | STA7 | (20,0) |  | VoIP | 0.10 | Constant, UDP | 120 | 30 | 5% |
| 6 | AP | (0,0) | STA8 | (0,20) |  | VoIP | 0.10 | Constant, UDP | 120 | 30 | 5% |
| 7 | AP | (0,0) | STA9 | (0,-20) |  | VoIP | 0.10 | Constant, UDP | 120 | 30 | 5% |
| 8 | AP | (0,0) | STA10 | (10,10) |  | Internet Streaming video | 2.00 | UDP | 512 | 200 | 10^-4 |
| 9 | AP | (0,0) | STA11 | (10,5) |  | MP3 audio | 0.13 | UDP | 418 | 200 | 10^-4 |
|  | Uplink Flows |  |  |  |  |  |  |  |  |  |
| 10 | STA1 | (0,5) | AP | (0,0) |  | VoD control channel | 0.06 | Constant, UDP | 64 | 100 | 10^-2 |
| 11 | STA3 | (5,0) | AP | (0,0) |  | VoD control channel | 0.06 | Constant, UDP | 64 | 100 | 10^-2 |
| 12 | STA7 | (20,0) | AP | (0,0) |  | VoIP | 0.10 | Constant, UDP | 120 | 30 | 5% |
| 13 | STA8 | (0,20) | AP | (0,0) |  | VoIP | 0.10 | Constant, UDP | 120 | 30 | 5% |
| 14 | STA9 | (0,-20) | AP | (0,0) |  | VoIP | 0.10 | Constant, UDP | 120 | 30 | 5% |
| 15 | STA10 | (10,10) | AP | (0,0) |  | Console to Internet | 1.00 | Constant, UDP | 512 | 50 | 10^-4 |
|  | STA to STA Flows |  |  |  |  |  |  |  |  |  |
| 16 | STA4 | (-7,7) | STA10 | (10,10) |  | Local file transfer | 10.00 | TCP | 300 | Inf. | N/A |
| 17 | STA5 | (-15,0) | STA6 | (0,-15) |  | Video Phone | 0.50 | Constant, UDP | 512 | 100 | 10^-2 |
| 18 | STA6 | (0,-15) | STA5 | (-15,0) |  | Video Phone | 0.50 | Constant, UDP | 512 | 100 | 10^-2 |
| 19 | STA11 | (10,5) | STA10 | (10,10) |  | Controller to Console | 0.50 | Constant, UDP | 50 | 16 | 10^-4 |
|  |  |  |  |  |  | Total Thruput | 466.35 |  |  |  |  |

Note) STA2 is reserved.

# 4.4 Enterprise Network (scenario #6)

Test case to demonstrate enterprise network application with large number of flows (over 40).

This scenario is derived from scenario #4 defind in 802.11n usage model document.

31 stations

One TGac AP is source and sink

30 STAs are souces and sinks.

Traffic from AP to STAs

Internet file, video conferencing, Internet streaming video + MP3, local file transfer

VoIP

Traffic from STAs to AP

Click, file upload, video conferencing, VoIP

PHY channel for each link

Channel model type applied : TBD

Only channel model D’s or mixing D’s and B’s for more realistic scenario

Channel model break point (unchanged from 802.11n scenarios)

Distance between STAs can be used to select between LOS and NLOS according to the breakpoint distance defined in 802.11n channel model document [8].

e.g.) 5 meters for model B and 10 meters for model D

Shadowing term is 0dB (unchanged from 802.11n scenarios)

In 802.11n channel model document [8], shadow fading std. dev. is specified for each channel model between 3dB and 6dB at page 7.

In 802.11n usage model document [3], shadowing term applied to all the 802.11n simulation scenarios is set to 0dB for generating a channel realization at page 22.

Locations of stations

Fixed locations (unchagend from 802.11n scenario #4)

Meet requirements specified in PLR and Max. Delay per each flow

Total throughput condition

Total throughput (about 740Mbps) is not a heavy burden compared to that of scenario #4 defined in 802.11n usage model document (about 460Mbps).

| Flow No. | Source | Source Location (meters) | Sink | Sink Location (meters) | Channel | Application | Bit Rate (Mbps) | Rate Distribution | MSDU Size (B) | Max. Delay (ms) | PLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Downlink Flows |  |  |  |  |  |  |  |  |  |
| 1 | AP | (0,0) | STA1 | (5,-9.5) |  | Internet file | 1.00 | TCP | 300 | Inf. | N/A |
| 2 | AP | (0,0) | STA2 | (3.5,7.5) |  | Internet file | 1.00 | TCP | 300 | Inf. | N/A |
| 3 | AP | (0,0) | STA3 | (7.5,-9.5) |  | Internet file | 1.00 | TCP | 300 | Inf. | N/A |
| 4 | AP | (0,0) | STA4 | (-4,0.5) |  | Internet file | 1.00 | TCP | 300 | Inf. | N/A |
| 5 | AP | (0,0) | STA5 | (-1.5,6) |  | Internet file | 1.00 | TCP | 300 | Inf. | N/A |
| 6 | AP | (0,0) | STA6 | (-5.5,4.5) |  | Internet file, downloading large email attachments | 10.00 | TCP | 300 | Inf. | N/A |
| 7 | AP | (0,0) | STA7 | (-9,-5) |  | Video conferencing | 1.00 | Constant, UDP | 512 | 100 | 10^-4 |
| 8 | AP | (0,0) | STA8 | (-8.5,8.5) |  | Video conferencing | 1.00 | Constant, UDP | 512 | 100 | 10^-4 |
| 9 | AP | (0,0) | STA9 | (7,-7.5) |  | Internet Streaming video + MP3 audio | 2.00 | UDP | 512 | 200 | 10^-4 |
| 10 | AP | (0,0) | STA10 | (-3,0.5) |  | Internet Streaming video + MP3 audio | 2.00 | UDP | 512 | 200 | 10^-4 |
| 11 | AP | (0,0) | STA11 | (-0.5,8) |  | Local File transfer | 50.00 | TCP | 1500 | Inf. | N/A |
| 12 | AP | (0,0) | STA12 | (7,7) |  | Local File transfer | 50.00 | TCP | 1500 | Inf. | N/A |
| 13 | AP | (0,0) | STA13 | (-4,-4) |  | Local File transfer | 50.00 | TCP | 1500 | Inf. | N/A |
| 14 | AP | (0,0) | STA14 | (7.5,-1) |  | Local File transfer | 50.00 | TCP | 1500 | Inf. | N/A |
| 15 | AP | (0,0) | STA15 | (3,-0.5) |  | Local File transfer | 50.00 | TCP | 1500 | Inf. | N/A |
| 16 | AP | (0,0) | STA16 | (8,-6) |  | Local File transfer | 50.00 | TCP | 1500 | Inf. | N/A |
| 17 | AP | (0,0) | STA17 | (0,-7.5) |  | Local File transfer | 50.00 | TCP | 1500 | Inf. | N/A |
| 18 | AP | (0,0) | STA18 | (10,0.5) |  | Local File transfer | 50.00 | TCP | 1500 | Inf. | N/A |
| 19 | AP | (0,0) | STA19 | (-2.5,-4.5) |  | Local File transfer | 50.00 | TCP | 1500 | Inf. | N/A |
| 20 | AP | (0,0) | STA20 | (0.5,-2) |  | Local File transfer | 50.00 | TCP | 1500 | Inf. | N/A |
| 21 | AP | (0,0) | STA25 | (3.5,-5) |  | VoIP | 0.10 | Constant, UDP | 120 | 30 | 5% |
| 22 | AP | (0,0) | STA26 | (9,9.5) |  | VoIP | 0.10 | Constant, UDP | 120 | 30 | 5% |
| 23 | AP | (0,0) | STA27 | (-6,2.5) |  | VoIP | 0.10 | Constant, UDP | 120 | 30 | 5% |
| 24 | AP | (0,0) | STA28 | (-8,-5.5) |  | VoIP | 0.10 | Constant, UDP | 120 | 30 | 5% |
| 25 | AP | (0,0) | STA29 | (1.5,3.5) |  | VoIP | 0.10 | Constant, UDP | 120 | 30 | 5% |
| 26 | AP | (0,0) | STA30 | (9.5,3.5) |  | VoIP | 0.10 | Constant, UDP | 120 | 30 | 5% |
| Flow No. | Source | Source Location (meters) | Sink | Sink Location (meters) |  | Application | Bit Rate (Mbps) | Rate Distribution | MSDU Size | Max Delay (ms) | PLR |
|  | Uplink Flows |  |  |  |  |  |  |  |  |  |
| 27 | STA1 | (5,-9.5) | AP | (0,0) |  | Click | 0.256 | TCP | 64 | Inf. | N/A |
| 28 | STA2 | (3.5,7.5) | AP | (0,0) |  | Click | 0.256 | TCP | 64 | Inf. | N/A |
| 29 | STA3 | (7.5,-9.5) | AP | (0,0) |  | Click | 0.256 | TCP | 64 | Inf. | N/A |
| 30 | STA4 | (-4,5,0.5) | AP | (0,0) |  | File Upload | 5 | TCP | 1000 | Inf. | N/A |
| 31 | STA5 | (-1.5,6) | AP | (0,0) |  | File Upload | 10 | TCP | 1500 | Inf. | N/A |
| 32 | STA6 | (-5.5,4.5) | AP | (0,0) |  | Click | 0.256 | TCP | 64 | Inf. | N/A |
| 33 | STA7 | (-9,-5) | AP | (0,0) |  | Video conferencing | 1.00 | Constant, UDP | 512 | 100 | 10^-4 |
| 34 | STA8 | (-8.5,8.5) | AP | (0,0) |  | Video conferencing | 1.00 | Constant, UDP | 512 | 100 | 10^-4 |
| 35 | STA21 | (-6.5,-3) | AP | (0,0) |  | File Upload | 50.00 | TCP | 1500 | Inf. | N/A |
| 36 | STA22 | (0,-4.5) | AP | (0,0) |  | File Upload | 50.00 | TCP | 1500 | Inf. | N/A |
| 37 | STA23 | (-1.5,7) | AP | (0,0) |  | File Upload | 50.00 | TCP | 1500 | Inf. | N/A |
| 38 | STA24 | (3,2.5) | AP | (0,0) |  | File Upload | 50.00 | TCP | 1500 | Inf. | N/A |
| 39 | STA25 | (3.5,-5) | AP | (0,0) |  | VoIP | 0.10 | Constant, UDP | 120 | 30 | 5% |
| 40 | STA26 | (9,9.5) | AP | (0,0) |  | VoIP | 0.10 | Constant, UDP | 120 | 30 | 5% |
| 41 | STA27 | (-6,2.5) | AP | (0,0) |  | VoIP | 0.10 | Constant, UDP | 120 | 30 | 5% |
| 42 | STA28 | (-8,-5.5) | AP | (0,0) |  | VoIP | 0.10 | Constant, UDP | 120 | 30 | 5% |
| 43 | STA29 | (1.5,3.5) | AP | (0,0) |  | VoIP | 0.10 | Constant, UDP | 120 | 30 | 5% |
| 44 | STA30 | (9.5,3.5) | AP | (0,0) |  | VoIP | 0.10 | Constant, UDP | 120 | 30 | 5% |
|  |  |  |  |  |  | Total Measured Thruput | 740.2 |  |  |  |  |

# 4.5 Comparison Criteria

MAC SAP throughput (goodput)

Aggregated throughput (downlink + uplink)

Throughput of each flow in the simulation scenario

Packet Loss Rate for each flow in the simulation scenario

Lost packets include

Packets that exceed maximum latency requirement

Packets that are dropped after exceeding maximum number of re-tries

# 4.6 Results Presentation Format

e.g.) for scenario #5

| Flow No. | Source | Sink | Application | Bit Rate (Mbps) | Rate Distribution | Max Delay (ms) | PLR | Pass/Fail | Latency Compliant (%) | Measured Throughput (Mbps) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Downlink Flows |  |  |  |  |  |  |
| 1 | AP | STA1 | LC Video | 150.00 | Constant, UDP | 10 |  |  |  |  |
| 2 | AP | STA3 | LC Video | 150.00 | Constant, UDP | 10 |  |  |  |  |
| 3 | AP | STA4 | LC Video | 150.00 | Constant, UDP | 10 |  |  |  |  |
| 4 | AP | STA4 | Internet file | 1.00 | TCP | Inf. |  |  |  |  |
| 5 | AP | STA7 | VoIP | 0.10 | Constant, UDP | 30 |  |  |  |  |
| 6 | AP | STA8 | VoIP | 0.10 | Constant, UDP | 30 |  |  |  |  |
| 7 | AP | STA9 | VoIP | 0.10 | Constant, UDP | 30 |  |  |  |  |
| 8 | AP | STA10 | Internet Streaming video | 2.00 | UDP | 200 |  |  |  |  |
| 9 | AP | STA11 | MP3 audio | 0.13 | UDP | 200 |  |  |  |  |
|  | Uplink Flows |  |  |  |  |  |  |
| 10 | STA1 | AP | VoD control channel | 0.06 | Constant UDP | 100 |  |  |  |  |
| 11 | STA3 | AP | VoD control channel | 0.06 | Constant UDP | 100 |  |  |  |  |
| 12 | STA7 | AP | VoIP | 0.10 | Constant, UDP | 30 |  |  |  |  |
| 13 | STA8 | AP | VoIP | 0.10 | Constant, UDP | 30 |  |  |  |  |
| 14 | STA9 | AP | VoIP | 0.10 | Constant, UDP | 30 |  |  |  |  |
| 15 | STA10 | AP | Console to Internet | 1.00 | Constant, UDP | 50 |  |  |  |  |
|  | STA to STA Flows |  |  |  |  |  |  |
| 16 | STA4 | STA10 | Local File Transfer | 10.00 | TCP | Inf. |  |  |  |  |
| 17 | STA5 | STA6 | Video Phone | 0.50 | Constant, UDP | 100 |  |  |  |  |
| 18 | STA6 | STA5 | Video Phone | 0.50 | Constant, UDP | 100 |  |  |  |  |
| 19 | STA11 | STA10 | Controller to Console | 0.50 | Constant, UDP | 16 |  |  |  |  |
|  |  |  | Total Given Thruput | 466.35 |  |  |  |  | Total Measured Thruput | 0.00 |

# 5. Summary of Functional Requirements

| Requirement Number | Description | Requirement Statement | Status of Requirement | Notes (informative) |
| --- | --- | --- | --- | --- |
| R1 | Operational in 5 GHz | TGac devices shall operate in 5GHz frequency band. |  |  |
| R2 | Maximum multi-STA throughput | Support at least 1 Gbps at the top of the MAC SAP. |  |  |
| R3 | Maximum single link throughput | Support 500 Mbps throughput at the top of the MAC SAP |  |  |
| R4 | Spectrum efficiency | In the highest throughput mode, TGac devices shall achieve a spectral efficiency of at least 7.5 bps/Hz for the PSDU. |  |  |
| R5 | Support 802.11 QoS Enhancements support | The proposal shall support the QoS enhancements of the IEEE802.11-2007 within an TGac STA. |  |  |
| R6 | Control of support for legacy STA from TGac AP | A TGac AP can be configured to reject or accept associations from 802.11a/n STAs |  |  |
| R7 | 802.11a backward compatibility | TGac devices shall ensure backward compatibility with IEEE802.11a devices operating in the 5 GHz frequency band. . |  |  |
| R8 | 802.11n backward compatibility | TGac devices shall ensure backward compatibility with IEEE802.11n devices operating in the 5 GHz frequency band |  |  |
| R9 | Coexistence with 802.11a/n devices | TGac devices provide mechanisms to enable coexistence and spectrum sharing with IEEE802.11a/n devices operating in the same frequency band. |  |  |
| R10 | Compliance to PAR | The proposal complies with the PAR and 5 Criteria [1]. |  |  |

# 6. References

- 11-08-0807-04-0vht-below-6-ghz-par-nescom-form-plus-5cs

- 11-03-0813-13-000n-functional-requirements

- 11-03-0802-23-000n-usage-models

- 11-08-0307-01-0vht-on-the-feasibility-of-1gbps-for-various-mac-phy-architectures

- 11-08-0535-00-0vht-phy-and-mac-throughput-analysis-with-80-mhz-for-vht-below-6-ghz

- 11-09-0071-01-00ac-discussion-on-functional-requirements

- 11-03-0814-31-000n-comparison-criteria

- 11-03-0940-04-000n-tgn-channel-models

- 11-09-0059-04-00ac-tgac-802.11ac-proposed-selection-procedure

- 11-09-0376-01-00ac-proposal-for-tgac-evaluation-methodology

- 11-09-0308-01-00ac-tgac-channel-model-addendum-document

- 11-09-0161-02-00ac-802.11ac-usage-model-document

# Footnotes

Note, this corresponds to a loss of a 1024B MSDU per hour.   The TS PDU PLR is higher than this.  It is not known what is the effect to the decoder of giving it burst packet losses.

Note, a PLR of 10^-7 will not be measurable in our simulation technologies.

# Text boxes

ABSTRACT

This document describes the functional requirements and the evaluation methodology for TGac. These requirements are derived from the document “11-08-0807-04-0vht-below-6-ghz-par-nescom-form-plus-5cs”. All proposals submitted in response to the IEEE802.11 TGac call for proposal must address the functional requirements that are shown as mandatory in this document.