IEEE P802.11
Wireless LANs

| PICS resolution text |
| --- |
| Date: 2009-07-08 |
| Author(s): |
| Name | Company | Address | Phone | Email |
| Kazuyuki Sakoda | Sony Corporation | 5-1-12 Kita-Shinagawa, Shinagawa-ku, Tokyo, 141-0001 Japan | +81-3-5448-4017 | sako(at)wcs.sony.co.jp |

## Summary of the intention of this document

- Provide more detailed items in the PICS table.

## Suggested changes to the draft spec

- Revise the PICs table for Mesh Capabilities.
( CID397

Apply the following changes.
Corresponding changes to D3.02 are indicated in the following text with “Track Changes” on, to clarify the direction to the editor. Please update the part indicated by the “Track Changes” only.

- Mesh Protocol Capabilities

- General Mesh Support

| Item | Protocol Capability | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| *MP1 | Support of Mesh Capability | 5.2.12 (Mesh BSS: The 802.11 Wireless mesh network) | PC36:M | Yes No N/A  |
| MP2 | Mesh Control field | 7.1.3.5b (Mesh Control field ) | MP1:M | Yes No N/A  |
| MP2.1 | Address Extention recognition | 7.1.3.5b (Mesh Control field ) | MP2:M | Yes No N/A  |
| MP2.2 | Decrement of Mesh Frame TTL | 7.1.3.5b (Mesh Control field ) | MP2:M | Yes No N/A  |
| MP3 | Mesh STA Beaconing | 11C.13.3 (Beaconing) | MP1:M | Yes No N/A  |
| MP4 | Mesh STA Synchronization | 11C.13.2 (Extensible synchronization framework) | MP1:M | Yes No N/A  |
| MP4.1 | Neighbor Offset Protocol | 11C.13.2.2 (Neighbor Offset Protocol) | MP4:M | Yes No N/A  |
| *MP5 | MCCA | 9.9a.2 (MCF controlled channel access (MCCA)) | MP1:O | Yes No N/A  |
| MP5.1 | MCCAOP Advertisement | 9.9a.2.8 (MCCAOP Advertisements) | MP5:M | Yes No N/A  |
| MP5.2 | Neighbor MCCAOP Recognition | 9.9a.2.4 (Neighborhood MCCAOP times at a mesh STA) - 9.9a.2.6 (MCCA access fraction (MAF)) | MP5:M | Yes No N/A  |
| MP5.3 | MCCAOP Setup | 9.9a.2.7 (MCCAOP setup procedure) | MP5:M | Yes No N/A  |
| MP5.4 | Access during MCCAOPs | 9.9a.2.10 (Access during MCCAOP) | MP5:M | Yes No N/A  |
| *MP6 | Intra Mesh Congestion Control | 11C.12 (Intra-mesh congestion control) | MP1:O | Yes No N/A  |
| MP6.1 | Local congestion monitoring and detection | 11C.12 (Intra-mesh congestion control) | MP6:M | Yes No N/A  |
| MP6.2 | Congestion control signaling | 11C.12 (Intra-mesh congestion control) | MP6:M | Yes No N/A  |
| MP6.3 | Local rate control | 11C.12 (Intra-mesh congestion control) | MP6:M | Yes No N/A  |
| *MP7 | Mesh Beacon Collision Avoidance | 11C.13.4 (Mesh Beacon Collision Avoidance (MBCA) mechanism) | MP4:O | Yes No N/A  |
| MP7.1 | Beacon timing announcement | 11C.13.4.1 | MP7:O | Yes No N/A  |
| MP7.2 | TBTT adjustment | 11C.13.4.2 | MP7:O | Yes No N/A  |
| MP8 | Mesh Power Management | 11C.14 (Power save in a mesh BSS) | MP1:O | Yes No N/A  |
| MP8.1 | Mesh power modes | 11C.14.1, 11C.14.8 | MP8:M | Yes No N/A  |
| MP8.2 | STA power state transisions | 11C.14.3 | MP8:M | Yes No N/A  |
| MP8.3 | Mesh Awake Window and frame transmission | 11C.14.6 | MP8:M | Yes No N/A  |
| MP9 | Mesh Power Save Support | 11C.14 (Power save in a mesh BSS) | MP1:M | Yes No N/A  |
| MP9.1 | TIM transmission | 11C.14.4 | MP9:M | Yes No N/A  |
| MP9.2 | Link specific mesh power modes | 11C.14.1 | MP9:M | Yes No N/A  |
| MP9.3 | Non-peer power modes | 11C.14.2 | MP9:M | Yes No N/A  |
| MP9.4 | Frame transmission to mesh STAs in light sleep mode | 11C.14.7, 11C.14.9 | MP9:M | Yes No N/A  |
| MP9.5 | Frame transmission to mesh STAs in deep sleep mode | 11C.14.7, 11C.14.9 | MP9:M | Yes No N/A  |
| *MP10 | MBSS channel selection | 11C.7 (MBSS channel switching) | MP1:M | Yes No N/A  |
| MP10.1 | Channel switch announcement | 11C.7 (MBSS channel switching) | MP10:M | Yes No N/A  |
| MP10.2 | Channel switch execution | 11C.7 (MBSS channel switching) | MP10:M | Yes No N/A  |
| *MP11 | Airlink Time metric transaction | 11C.10 (Airtime link metric) | MP1:M | Yes No N/A  |
| MP11.1 | Airlink Time metric computation | 11C.10 (Airtime link metric) | MP11:M | Yes No N/A  |
| MP11.2 | Airlink Time metric request | 11C.10 (Airtime link metric) | MP11:M | Yes No N/A  |
| MP11.3 | Airlink Time metric report | 11C.10 (Airtime link metric) | MP11:M | Yes No N/A  |
| *MP12 | Proxy operation | 11C.9.5 (Proxy protocol) | MP1:O | Yes No N/A  |

References:

[1] Draft Amendment: Mesh Networking.  doc.: IEEE P802.11s/D3.02, May 2009.

# Text boxes

Abstract

This document provides suggested resolutions to CID397.