IEEE P802.11
Wireless LANs

| PICS resolution text |
| --- |
| Date: 2009-07-13 |
| Author(s): |
| Name | Company | Address | Phone | Email |
| Kazuyuki Sakoda | Sony Corporation | 5-1-12 Kita-Shinagawa, Shinagawa-ku, Tokyo, 141-0001 Japan | +81-3-5448-4017 | sako(at)wcs.sony.co.jp |

## Summary of the intention of this document

- Provide more detailed items in the PICS table.

## Suggested changes to the draft spec

- Revise the PICs table for Mesh Capabilities.
( CID397

Apply the following changes.
Corresponding changes to D3.02 are indicated in the following text with “Track Changes” on, to clarify the direction to the editor. Please update the part indicated by the “Track Changes” only.

- MAC frames

Insert the following after the table entry for “FT25” in A.4.4.2:

| Item | Protocol Capability | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| FT26 | Mesh Data frames | 7.1.3.1 (Frame control field ), 7.1.3.5b (Mesh Control field ) | MP1:M | Yes No N/A  |
| FT27 | Peering Open frame | 7.4.12.1 ( Peering Open frame format) | MP1:M | Yes No N/A  |
| FT28 | Peering Confirm frame | 7.4.12.2 (Peering Confirm frame format) | MP1:M | Yes No N/A  |
| FT29 | Peering Close frame | 7.4.12.3 (Peering Close frame format) | MP1:M | Yes No N/A  |
| FT30 | Mesh Link Metric Request frame | 7.4.13.1 (Mesh Link Metric Request frame format) | MP11.1:M | Yes No N/A  |
| FT31 | Mesh Link Metric Report frame | 7.4.13.2 (Mesh Link Metric Report frame format) | MP11.2:M | Yes No N/A  |
| FT32 | Mesh Path Selection frame | 7.4.14.1 ( Mesh Path Selection frame format) | HWM1:M | Yes No N/A  |
| FT33 | Portal Announcement frame | 7.4.15.1 ( Portal Announcement frame format), 11C.9 (Interworking) | HWM1:M | Yes No N/A  |
| FT34 | Congestion Control Notification frame | 7.4.16.1 (Congestion Control Notification frame format), 11C.12 (Intra-mesh congestion control) | MP6.2:M | Yes No N/A  |
| FT35 | MCCA Setup Request frame | 7.4.16.2 (MCCA Setup Request frame format) | MP5:M | Yes No N/A  |
| FT36 | MCCA Setup Reply frame | 7.4.16.3 (MCCA Setup Reply frame format) | MP5:M | Yes No N/A  |
| FT37 | MCCAOP Advertisement Request frame | 7.4.16.4 (MCCAOP Advertisement Request frame format) | MP5:M | Yes No N/A  |
| FT38 | MCCAOP Advertisements frame | 7.4.16.5 (MCCAOP Advertisements frame format) | MP5:M | Yes No N/A  |
| FT39 | MCCAOP Reservation Teardown frame | 7.4.16.6 (MCCAOP Reservation Teardown frame format) | MP5:M | Yes No N/A  |
| FT40 | TBTT Adjustment Request frame | 7.4.16.7 (TBTT Adjustment Request frame format) | MP4.2.2:M | Yes No N/A  |
| FT41 | Mesh Channel Switch Announcement frame | 7.4.16.8 (Mesh Channel Switch Announcement frame format) | MP7.1:M | Yes No N/A  |
| FT42 | Proxy Update frame | 7.4b.1.1 (Proxy Update frame format ) | MP12:M | Yes No N/A  |
| FT43 | Proxy Update Confirmation frame | 7.4b.1.2 (Proxy Update Confirmation frame format ) | MP12:M | Yes No N/A  |

Insert the following after the table entry for “FR25” in A.4.4.2:

| Item | Protocol Capability | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| FR26 | Mesh Data frames | 7.1.3.1 (Frame control field ), 7.1.3.5b (Mesh Control field ) | MP1:M | Yes No N/A  |
| FR27 | Peering Open frame | 7.4.12.1 ( Peering Open frame format) | MP1:M | Yes No N/A  |
| FR28 | Peering Confirm frame | 7.4.12.2 (Peering Confirm frame format) | MP1:M | Yes No N/A  |
| FR29 | Peering Close frame | 7.4.12.3 (Peering Close frame format) | MP1:M | Yes No N/A  |
| FR30 | Mesh Link Metric Request frame | 7.4.13.1 (Mesh Link Metric Request frame format) | MP11.1:M | Yes No N/A  |
| FR31 | Mesh Link Metric Report frame | 7.4.13.2 (Mesh Link Metric Report frame format) | MP11.2:M | Yes No N/A  |
| FR32 | Mesh Path Selection frame | 7.4.14.1 ( Mesh Path Selection frame format) | HWM1:M | Yes No N/A  |
| FR33 | Portal Announcement frame | 7.4.15.1 ( Portal Announcement frame format), 11C.9 (Interworking) | HWM1:M | Yes No N/A  |
| FR34 | Congestion Control Notification frame | 7.4.16.1 (Congestion Control Notification frame format), 11C.12 (Intra-mesh congestion control) | MP6.2:M | Yes No N/A  |
| FR35 | MCCA Setup Request frame | 7.4.16.2 (MCCA Setup Request frame format) | MP5:M | Yes No N/A  |
| FR36 | MCCA Setup Reply frame | 7.4.16.3 (MCCA Setup Reply frame format) | MP5:M | Yes No N/A  |
| FR37 | MCCAOP Advertisement Request frame | 7.4.16.4 (MCCAOP Advertisement Request frame format) | MP5:M | Yes No N/A  |
| FR38 | MCCAOP Advertisements frame | 7.4.16.5 (MCCAOP Advertisements frame format) | MP5:M | Yes No N/A  |
| FR39 | MCCAOP Reservation Teardown frame | 7.4.16.6 (MCCAOP Reservation Teardown frame format) | MP5:M | Yes No N/A  |
| FR40 | TBTT Adjustment Request frame | 7.4.16.7 (TBTT Adjustment Request frame format) | MP4.2.2:M | Yes No N/A  |
| FR41 | Mesh Channel Switch Announcement frame | 7.4.16.8 (Mesh Channel Switch Announcement frame format) | MP7.1:M | Yes No N/A  |
| FR42 | Proxy Update frame | 7.4b.1.1 (Proxy Update frame format ) | MP12:M | Yes No N/A  |
| FR43 | Proxy Update Confirmation frame | 7.4b.1.2 (Proxy Update Confirmation frame format ) | MP12:M | Yes No N/A  |

- Mesh Protocol Capabilities

- General Mesh Support

| Item | Protocol Capability | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| *MP1 | Support of Mesh Capability | 5.2.12 (Mesh BSS: The 802.11 Wireless mesh network) | PC36:M | Yes No N/A  |
| MP2 | Mesh Control field | 7.1.3.5b (Mesh Control field ) | MP1:M | Yes No N/A  |
| MP2.1 | Address Extention recognition | 7.1.3.5b (Mesh Control field ) | MP2:M | Yes No N/A  |
| MP2.2 | Decrement of Mesh Frame TTL | 7.1.3.5b (Mesh Control field ) | MP2:M | Yes No N/A  |
| MP3 | Mesh STA Beaconing | 11C.13.3 (Beaconing) | MP1:M | Yes No N/A  |
| MP4 | Mesh STA Synchronization | 11C.13.2 (Extensible synchronization framework) | MP1:M | Yes No N/A  |
| MP4.1 | Neighbor Offset Protocol | 11C.13.2.2 (Neighbor Offset Protocol) | MP4:M | Yes No N/A  |
| MP4.2 | Mesh Beacon Collision Avoidance | 11C.13.4 (Mesh Beacon Collision Avoidance (MBCA) mechanism) | MP4:O | Yes No N/A  |
| MP4.2.1 | Beacon timing announcement | 11C.13.4.1 | MP4:O | Yes No N/A  |
| *MP4.2.2 | TBTT adjustment | 11C.13.4.2 | MP4:O | Yes No N/A  |
| *MP5 | MCCA | 9.9a.2 (MCF controlled channel access (MCCA)) | MP1:O | Yes No N/A  |
| MP5.1 | MCCAOP Advertisement | 9.9a.2.8 (MCCAOP Advertisements) | MP5:M | Yes No N/A  |
| MP5.2 | Neighbor MCCAOP Recognition | 9.9a.2.4 (Neighborhood MCCAOP times at a mesh STA) - 9.9a.2.6 (MCCA access fraction (MAF)) | MP5:M | Yes No N/A  |
| MP5.3 | MCCAOP Setup | 9.9a.2.7 (MCCAOP setup procedure) | MP5:M | Yes No N/A  |
| MP5.4 | Access during MCCAOPs | 9.9a.2.10 (Access during MCCAOP) | MP5:M | Yes No N/A  |
| MP6 | Intra Mesh Congestion Control | 11C.12 (Intra-mesh congestion control) | MP1:O | Yes No N/A  |
| MP6.1 | Local congestion monitoring and detection | 11C.12 (Intra-mesh congestion control) | MP6:M | Yes No N/A  |
| *MP6.2 | Congestion control signaling | 11C.12 (Intra-mesh congestion control) | MP6:M | Yes No N/A  |
| MP6.3 | Local rate control | 11C.12 (Intra-mesh congestion control) | MP6:M | Yes No N/A  |
| MP7 | MBSS channel selection | 11C.7 (MBSS channel switching) | MP1:M | Yes No N/A  |
| *MP7.1 | Channel switch announcement | 11C.7 (MBSS channel switching) | MP7:M | Yes No N/A  |
| MP7.2 | Channel switch execution | 11C.7 (MBSS channel switching) | MP7:M | Yes No N/A  |
| MP8 | Mesh Power Management | 11C.14 (Power save in a mesh BSS) | MP1:O | Yes No N/A  |
| MP8.1 | Mesh power modes | 11C.14.1, 11C.14.8 | MP8:M | Yes No N/A  |
| MP8.2 | STA power state transisions | 11C.14.3 | MP8:M | Yes No N/A  |
| MP8.3 | Mesh Awake Window and frame transmission | 11C.14.6 | MP8:M | Yes No N/A  |
| MP9 | Mesh Power Save Support | 11C.14 (Power save in a mesh BSS) | MP1:M | Yes No N/A  |
| MP9.1 | TIM transmission | 11C.14.4 | MP9:M | Yes No N/A  |
| MP9.2 | Link specific mesh power modes | 11C.14.1 | MP9:M | Yes No N/A  |
| MP9.3 | Non-peer power modes | 11C.14.2 | MP9:M | Yes No N/A  |
| MP9.4 | Frame transmission to mesh STAs in light sleep mode | 11C.14.7, 11C.14.9 | MP9:M | Yes No N/A  |
| MP9.5 | Frame transmission to mesh STAs in deep sleep mode | 11C.14.7, 11C.14.9 | MP9:M | Yes No N/A  |
| MP10 | Airtime link metric computation | 11C.10 (Airtime link metric) | MP1:M | Yes No N/A  |
| MP11 | Link metric reporting | 11C.8.4 (Link metric reporting) | MP1:M | Yes No N/A  |
| *MP11.1 | Link metric request | 11C.8.4 (Link metric reporting) | MP11:M | Yes No N/A  |
| *MP11.2 | Link metric report | 11C.8.4 (Link metric reporting) | MP11:M | Yes No N/A  |
| *MP12 | Proxy operation | 11C.9.5 (Proxy protocol) | MP1:O | Yes No N/A  |

References:

[1] Draft Amendment: Mesh Networking.  doc.: IEEE P802.11s/D3.02, May 2009.

# Text boxes

Abstract

This document provides suggested resolutions to CID397.