## Slide 1: Contention Mechanisms for Quality of Service and Energy Conservation
July 2009
John A. Stine, Self
Slide <number>
Date: 2009-07-14
Authors:
John Stine is employed by The MITRE Corporation but represents himself in this presentation. The MITRE Corporation is a not for profit company and has no economic interest in the outcome of the 802 standards process. The author's affiliation with The MITRE Corporation is provided for identification purposes only, and is not intended to convey or imply MITRE's concurrence with, or support for, the positions, opinions or viewpoints expressed by the author.
MITRE Public Release #09-2574
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page <number>

## Slide 2: Patent Statement
Methods described in this presentation are covered in claims in patents and patents pending.
The MITRE Corporation is a not for profit company that does not own the patents and has no economic stake in the outcome of the 802 standards activity
John A. Stine, Self
Slide <number>
July 2009

## Slide 3: Abstract
TGad intends to create a very high throughput technology that can support streaming video and the use of mobile battery operated terminals
This presentation provides an overview of the Synchronous Collision Resolution (SCR) contention-based MAC protocol and its ability
  To arbitrate access based on priority
  To support capacity reservation without the exchange of schedules
  To support the use of low energy states to conserve energy.
John A. Stine, Self
Slide <number>
July 2009
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page <number>

## Slide 4: The Larger Story
Designing for Coexistence | Design by rules coexistence Arbitrating the use of space, time, and frequency
Multichannel Multi-directional Contention Access | Arbitrating channel use Creating directional diversity Enabling adaptation
Contention Mechanisms for Quality of Service and Energy Conservation | Differentiated services Bandwidth reservation for streaming Multiple dozing modes (default, opportunistic, coordinated)
Synchronization Mechanisms | Course synchronization Fine synchronization ToA Techniques
Slide <number>
July 2009
John A. Stine, Self

## Slide 5: REVIEW
July2009
John Stine, Self
Slide <number>

## Slide 6: Characteristics of Synchronous Collision Resolution
Time slotted channels with common time boundaries
Nodes with packets to send contend in every slot
Signaling is used to arbitrate contention
Packet transmissions occur simultaneously
A paradigm not a specific design
CR Signaling
Transmission Slot
…
John A. Stine, Self
Slide <number>
July 2009

## Slide 7: Purpose of Collision Resolution Signaling
Prune the set of contenders to a subset which can transmit without colliding
John A. Stine, Self
Slide <number>
July 2009

## Slide 8: Two Types of Signaling
Without Echoing – results in tighter compaction of contention winners that relies on physical layer techniques to improve capacity
With Echoing – provides one hop separation from potential destinations
Slide <number>
July 2009
John A. Stine, Self

## Slide 9: Basic benefits of SCR
Arbitrates space, time, and frequency
Does not suffer
  Hidden terminal effects
  Exposed terminal effects
  Deafness or muteness
  Congestion collapse
Creates the conditions that allows the use of
  Multiple channels in a single network
  CDMA
  All types of directional and smart antennas
  SDMA
Differentiates quality of service
  Prioritized access
  Reservations for streaming without scheduling
Multiple energy conservation modes
Slide <number>
July 2009
John A. Stine, Self

## Slide 10: QUALITY OF SERVICE
July 2009
Slide <number>
John A. Stine, Self

## Slide 11: Special features through a priority phase
We add a multi-slot phase to the front end of the collision resolution signaling that assigns slots to specific services
This example design illustrates three services
  Priority access
  Resource reservation
  Channel management
...
...
1
2
3
4
5
6
7
8
9
Signaling slots
Signaling phases
EI
QoS
Data 2
Data 3
VBR
CBR
Broadcast
Data 1
Priority Phase
July 2009
John A. Stine, Self
Slide <number>

## Slide 12: Prioritizing Access
In multi-slot first-to-assert phases the node that signals first will win the contention
Signaling slots may be mapped to differentiate access priority
Potential characteristics to differentiate priority
  Packet time-to-live parameter
  Source significance
  Operational significance
  Packet type
Nodes with the highest priority packets will always gain access first
QoS
Data 2
Data 3
VBR
CBR
Broadcast
Data 1
Priority Phase
July 2009
John A. Stine, Self
Slide <number>

## Slide 13: Effectiveness of prioritized access
Issue: How well does priority access work.
Experiment:
  156 nodes randomly placed on a toroidally wrapped square surface with a side (7* radio_range) which results in a network with an average degree of 10
  Perfect routing assuming a potential connection when SNR is >10dB
  Poisson arrival of packets uniformly distributed amongst the nodes with randomly and uniformly selected destinations
  Packets are randomly and evenly distributed among four priority levels
  Packets queued by priority earliest expiration time first
July 2009
John A. Stine, Self
Slide <number>

## Slide 14: The effectiveness of prioritized access
End-to-end throughput
End-to-end delay
Ideal packet prioritization
Low priority packets not penalized in lightly-loaded networks
(packets/sec)
Load (packets/sec)
1
2
3
4
Total
MAC packet exchanges
Load (packets/sec)
(seconds)
1
2
3
4
1
2
3
4
July 2009
John A. Stine, Self
Slide <number>

## Slide 15: SCR Modifications for Reservations
1
2
3
4
n-1
n
…
1
2
3
4
n-1
n
…
1
2
…
CBR Frame
CBR Frame
CR Signaling
RTS
CTS
Protocol Data Unit
ACK
Transmission Slot
...
...
1
2
3
4
5
6
7
8
9
EI
QoS
Data 2
Data 3
VBR
CBR
Broadcast
Data 1
Priority Phase
CBR Cooperative Signaling Slot
Add a cooperative signaling slot
Divide the transmission slots into frames
July 2009
John A. Stine, Self
Slide <number>

## Slide 16: Resource reservation process (1)
Contenders with a real time stream first contend using the QoS priority
If packet exchange is successful, that node may use the CBR priority in the same ordinal transmission slot of every subsequent CBR Frame.
QoS
Data 2
Data 3
VBR
CBR
Broadcast
Data 1
1
2
3
4
n-1
n
…
1
2
3
4
n-1
n
…
1
2
…
CBR Frame
CBR Frame
July 2009
John A. Stine, Self
Slide <number>

## Slide 17: Resource reservation process (2)
CBR destinations use the CBR cooperative signaling slot to assist in ensuring two-hop exclusive access. Only CBR sources and destinations may use this signaling slot.
CBR destinations know who they are since they received traffic in the same ordinal slot of the previous frame that they hear the CBR signaling priority being used
Sources with a CBR reservation may use the VBR priority in a best-effort sense to send packets from the same stream. This provides efficient support for bursty streams like video.
...
...
1
2
3
4
5
6
7
8
9
EI
QoS
Data 2
Data 3
VBR
CBR
Broadcast
Data 1
July 2009
John A. Stine, Self
Slide <number>

## Slide 18: Resource reservation process (3)
The process may be repeated by a node to reserve as much bandwidth as is needed.
The process can be repeated by multiple nodes in a series to provide services for multihop streams.
Multihop reservations can be cascaded to ensure an end-to-end delivery time.
Nodes hold reservations on a “use-it or lose-it” basis (Unused slots are immediately available).
1
2
3
4
n-1
n
…
1
2
3
4
n-1
n
…
1
2
…
CBR Frame
CBR Frame
Reserves 2 slots per frame
Slot 1
Slot 2
Slot 3
A 3 slot end-to-end delay
July 2009
John A. Stine, Self
Slide <number>

## Slide 19: ENERGY CONSERVATION
July 2009
Slide <number>
John A. Stine, Self

## Slide 20: Energy conservation
Methods to conserve energy
  Help nodes enter low energy states
    Low energy states created by turning off circuitry or signal processing
    Assumes the access protocol can control entering these states
    Opportunities to conserve energy by using low energy states occur when
      Other nodes are using the channel thus precluding the dozing candidate
      There is no traffic on the network
      The node has only a small amount of activity on the network
  Adjust transmit power
    Transmit power adaptation during RTS-CTS handshake
July 2009
John A. Stine, Self
Slide <number>

## Slide 21: Challenges in using low energy states
Entering a low energy state usually means removing a node from the network while it is in the low energy state
In ad hoc networks, nodes make their own decision when to enter a low energy state
  Need policies or mechanisms that enable nodes to know when to doze and when to stay awake
  Access protocols that resolve contentions based on time of access (i.e. CSMA, Aloha) are especially challenged. Nodes never know when they might receive a packet.
Sources need to be aware of when nodes are in low energy states
  Should hold traffic when in a low energy state
  Should forward traffic when destinations are awake
Best protocols
  Make dozing schedules implicit
  Minimize the time nodes must remain awake before learning that they can enter a low energy state
July 2009
John A. Stine, Self
Slide <number>

## Slide 22: Default energy conservation mode in SCR
Nodes enter a low energy state in every slot that they do not participate in a packet exchange
Prior to the PDU transmission, every node in the network knows if it will participate in an exchange
Nodes not exchanging packets in the transmission slot enter a low energy state until the beginning of the next slot
CR Signaling
RTS
CTS
Protocol Data Unit
ACK
Transmission Slot
July 2009
John A. Stine, Self
Slide <number>

## Slide 23: Periodic dozing method
A single dozing period (i.e. x transmission slots starting at time t) is established for the network
A node that senses no nodes contending may enter the doze state. (Indicates a low load condition.)
Nodes wake-up at the end of the period and stay awake until they next sense an idle transmission slot.
July 2009
John A. Stine, Self
Slide <number>

## Slide 24: Coordinated dozing method
Energy constrained nodes establish their dozing period and announce it to their neighbors.
Neighbors hold traffic for the dozing node but can use a special “energy save” priority to access the channel.
Dozing nodes wake-up and stay awake so long as contenders contend using the “energy save” or higher access priority signaling slot.
This technique allows battery powered nodes to exploit nodes with better power sources to conserve energy
July 2009
John A. Stine, Self
Slide <number>

## Slide 25: Conclusion
Synchronous Collision Resolution
  Is a highly effective paradigm for wireless contention-based medium access control
  It provides a distributed means to
    Prioritize access
    Reserve bandwidth for streaming traffic
  It provides multiple energy conservation modes
    Default (Doze when the channel is busy)
    Opportunistic (Doze when there is no activity in the network)
    Coordinated (Doze when this node has little activity)
July 2009
John A. Stine, Self
Slide <number>

## Slide 26: References
J.A. Stine and G. de Veciana, “A paradigm for quality of service in wireless ad hoc networks using synchronous signaling and node states,” IEEE J. Selected Areas of Communications, Sep 2004.
J. A. Stine and G. de Veciana, “A comprehensive energy conservation solution for mobile ad hoc networks,” IEEE Int. Communication Conf., 2002, pp. 3341 - 3345.
J. A. Stine, “Exploiting processing gain in wireless ad hoc networks using synchronous collision resolution medium access control schemes,” Proc. IEEE WCNC, Mar 2005.
J.A. Stine, “Cooperative contention-based MAC protocols and smart antennas in Mobile Ad Hoc Networks,” Chapter 8 in Distributed Antenna Systems: Open Architecture for Future Wireless Communications, Auerbach Publications, Editors H. Hu, Y. Zhang, and J. Luo. 2007.
K. H. Grace, J. A. Stine, R. C. Durst, “An approach for modestly directional communications in mobile ad hoc networks,” Telecommunications Systems J., March/April 2005, pp. 281 – 296.
J. A. Stine, “Modeling smart antennas in synchronous ad hoc networks using OPNET’s pipeline stages,” Proc. OPNETWORK, 2005.
J. A. Stine, “Exploiting smart antennas in wireless mesh networks,” IEEE Wireless Comm Mag. Apr 2006.
J. A. Stine, “Enabling secondary spectrum markets using ad hoc and mesh networking protocols,” Academy Publisher J. of Commun., Vol. 1, No. 1, April 2006, pp. 26 - 37.
J. Stine, G. de Veciana, K. Grace, and R. Durst, “Orchestrating spatial reuse in wireless ad hoc networks using Synchronous Collision Resolution,” J. of Interconnection Networks, Vol. 3 No. 3 & 4, Sep. and Dec. 2002, pp. 167 – 195.
K. Grace, “”SUMA – The synchronous unscheduled multiple access protocol for mobile ad hoc networks,” IEEE ICCCN, 2002.
John A. Stine, Self
Slide <number>
July 2009

## Slide 27: The Larger Story
Designing for Coexistence | Design by rules coexistence Arbitrating the use of space, time, and frequency
Multichannel Multi-directional Contention Access | Arbitrating channel use Creating directional diversity Enabling adaptation
Contention Mechanisms for Quality of Service and Energy Conservation | Differentiated services Bandwidth reservation for streaming Multiple dozing modes (default, opportunistic, coordinated)
Synchronization Mechanisms | Course synchronization Fine synchronization ToA Techniques
Slide <number>
July 2009
John A. Stine, Self

## Slide 28: Backup Summary
CRS Rules
  Without Echoing
  With Echoing
Signaling Walkthrough
Signaling Design
CRS effectiveness
Spatial reuse
MAC Comparison
CR Signals
  Assumptions & desired characteristics
  Timing parameters
  Signal Slot Sizing
July 2009
Slide <number>
John A. Stine, Self

## Slide 29: BACKUP
Slide <number>
July 2009
John A. Stine, Self

## Slide 30: Rules of Collision Resolution Signaling (CRS)
Rules of single slot signaling
  At the beginning of each signaling phase a contending node determines if it will signal. (The contending node will signal with the probability assigned to that phase.)
  A contender survives a phase by signaling in a slot or by not signaling and not hearing another contender’s signal. A contender that does not signal and hears another contender’s signal loses the contention and defers from contending any further in that transmission slot.
  Nodes that survive all phases win the contention
John A. Stine, Self
Slide <number>
July 2009
Notes: <number>

## Slide 31: Rules of Collision Resolution Signaling (CRS)
Rules of signaling phases that use echoing
  At the beginning of the signaling phase a contending node determines if it will signal. A contending node will signal in the first slot with the probability assigned to that phase.
  Any node that does not signal in the first slot but hears a signal sends a signal in the second slot.
  A contender survives the phase by signaling in the first slot or by not signaling and not hearing another contender’s signal in the first slot nor an echo in the second slot. A contender that does not signal and hears another contender’s signal or hears an echo loses the contention and defers from contending any further in that transmission slot
John A. Stine, Self
Slide <number>
July 2009
Notes: <number>

## Slide 32: Collision Resolution Signaling Example - 1
In this example all nodes start off as contenders
All contending nodes do a random number draw and those beneath a specified threshold transmit a signal. Signalers and those that do not hear the signal survive this phase of the signaling
Red = contender
Gray = non-contender
John A. Stine, Self
Slide <number>
July 2009

## Slide 33: Collision Resolution Signaling Example - 2
Signaling and attrition proceeds for several iterations with the threshold for signaling changing for each phase
John A. Stine, Self
Slide <number>
July 2009

## Slide 34: Collision Resolution Signaling Example - 3
John A. Stine, Self
Slide <number>
July 2009

## Slide 35: Collision Resolution Signaling Example - 4
John A. Stine, Self
Slide <number>
July 2009

## Slide 36: Collision Resolution Signaling Example - 5
The end result of collision resolution signaling
  When all nodes are in range of each other – one surviving node
  In a multihop environment as shown – a set of surviving nodes separated by the range of their signals
The range of signaling’s effect can be extended by using echoing (See subsequent slides)
Demonstration
John A. Stine, Self
Slide <number>
July 2009

## Slide 37: Echoing Example
Red = contender
Gray = non-contender
Blue square = echoer
75 contenders after contention
19 contenders after echoing
Demonstration
John A. Stine, Self
Slide <number>
July 2009

## Slide 38: How well does signaling isolate just one survivor?
Consider a signaling design where all phases have one slot
Let px be the probability that a contending node will signal in phase x
A transition matrix may be populated where the element k,s corresponds to the probability that s of k contending nodes survive the signaling phase
John A. Stine, Self
Slide <number>
July 2009
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page <number>

## Slide 39: How well does signaling isolate just one survivor? (2)
The transition matrix of the signaling process with n phases may be calculated
The probability that just 1 of k contending nodes survives signaling is
It is easy to optimally select a set of probabilities that maximizes the probability that there will be 1 survivor when there are some k = k1 contenders at the beginning but this problem formulation may result in a lower probability that one survivor remains when there are k < k1 contenders.
P(one survivor)
k
Improvement at k1 may results in decreased performance at k < k1
k1
John A. Stine, Self
Slide <number>
July 2009
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page <number>

## Slide 40: How well does signaling isolate just one survivor? (3)
A redefined optimization problem
  Let qn be the set of px for an n phase CRS design
  Let kt be a target density of contending nodes
  Let m be the total number of signaling slots allowed (in this case n = m)
  Let S(qn,kt,m) be the probability that there will be only one surviving contender
4, 5, 6 , 7, 8, and 9 single-slot phase designs optimized for a 50 contender density
Comparison of 9 single-slot phase designs optimized for various target densities of contenders
John A. Stine, Self
Slide <number>
July 2009
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page <number>

## Slide 41: How effective is CRS in resolving contention ?
It is a function of design, # of signaling phases, threshold probabilities for signaling
We have a simple design methodology that yields the performance illustrated
4, 5, 6 , 7, 8, and 9 single-slot phase designs optimized for a 50 contender density
Comparison of 9 single-slot phase designs optimized for various target densities of contenders
> 99% of the transmissions slots can be resolved to one transmitter for all practical densities of contenders!
John A. Stine, Self
Slide <number>
July 2009

## Slide 42: Spatial Reuse-1
Density of range to the nearest surviving neighbor when the average contending neighbor density is10
Simulated survivor densities using a 9-phase CRS design, kt = 50
Simulations of signaling without echoes reveal
  The density of survivors levels off at about 1.4 survivors per signaling area (the area covered by the range of a signal)
  Depending on signaling effectiveness, survivors are separated by at least the range of their signals
John A. Stine, Self
Slide <number>
July 2009

## Slide 43: Spatial Reuse-2
Simulations of signaling with echoes reveal
  The density of survivors decreases with contender density
  Average separation range increases with the density of the contenders
Simulated survivor densities using SUMA version of signaling
Density of range to the nearest surviving neighbor using SUMA version of signaling
2
5
8
10
15
20
25
John A. Stine, Self
Slide <number>
July 2009

## Slide 44: MAC Comparison
Capability | S-Aloha | TDMA | CSMA | SCR
Contention Protocol |  | – |  | 
Arbitrates space and frequency | – | – |  | +
Protection from congestion collapse | – | NA |  | +
Protection from hidden & exposed terminals | NA | NA | – | 
Reliability mechanisms (Acknowledgements) | – | – |  | 
Supports technology evolution (guaranteed coexistence) |  |  |  | +
Supports using multiple channels in a network | – |  | – | +
Supports CDMA (Mitigates near far effect) | – |  | – | +
Enables one to many communications | – |  | – | +
Supports directional and adaptive antennas |  |  | – | +
Arbitrates antenna pointing | – | – |  | +
Prevents coincident transmissions |  |  |  | +
Provides opportunity for full adaptation |  |  | – | +
Preserves the condition |  |  | – | +
Enables one to many communications | – |  | – | +
Slide <number>
July 2009
John A. Stine, Self

## Slide 45: MAC Comparison - 2
Capability | S-Aloha | TDMA | CSMA | SCR
Supports Quality of Service | – |  |  | +
Prioritized access | – |  |  | +
Reservations | – | + | – | +
Unscheduled Reservation | – |  | – | +
Supports Energy Conservation | – | + |  | +
Dozing during transmission | – |  |  | 
Opportunistic dozing |  | + | – | +
Coordinated dozing | – | – |  | +
Transmit power adaptation | – |  |  | +
Access without overheads | + |  |  | 
Backoff |  |  | – | 
Signaling | + | + |  | –
Scheduling |  | – |  | 
Performance independent of synchronization |  |  | + | –
Adaptive payload size (i.e. not slotted) |  |  | + | 
Slide <number>
July 2009
John A. Stine, Self

## Slide 46: Criticial Assumptions About Signaling
Slide <number>
The presence of signals is detected and there is no requirement to recover symbols or bits (PHY)
A signal is detected as present when receiving many signals (PHY)
The signaling slot in which a signal was sent is unambiguous (PHY or MAC)
John A. Stine, Self
July 2009

## Slide 47: Desired (not necessary) characteristics of signals
Slide <number>
Short
  Contributes to efficiency
Easily distinguished from noise and other transmissions
  Allows operation in noisy environments where physical layer capabilities can reject interference
Have unique characteristics that are associated with the signaling slot in which they are sent
  Reduces overhead requirements to prevent slot of transmission ambiguity
  Provides security preventing some cases of malicious DoS
John A. Stine, Self
July 2009

## Slide 48: Timing Parameters
Slide <number>
Parameter | Description
tS | Duration of a signal
tsf: | Selected minimum time to sense a signal in a signaling slot to detect it
tp | Selected propagation time to define the propagation limit of a signal
tg | Guard time between signaling slots
Parameter | Description
p | Propagation delay between nodes displaced the maximum receiving distance from each other
rt | Maximum time required by a transceiver to transition from the receive to the transmit state
tr | Maximum time required by a transceiver to transition from the transmit to the receive state
sy | Maximum difference in the synchronization of two nodes
sd | Minimum duration of a signal allowed by the PHY
sm | Minimum time to sense a signal in order to detect its presence as allowed by the PHY
sn | Time a node senses a signal in the wrong slot
ss | Time a node senses a signal in the correct slot
Table 1. Design Choices
Table 2. Modem Capabilities and Physics
John A. Stine, Self
July 2009

## Slide 49: Signaling Slot Assumptions
Slide <number>
Assume the signal slot size is selected as
Assume signal transmission or signal reception starts at the beginning of a signaling slot
Assume required sensing time, tsf, can be specified
ts is selected to account for PHY limitations in sending and sensing signals, propagation times, and synchronization differences
tg is selected to account for PHY transitions between receiving and transmitting states, propagation times, and synchronization differences
ts
ts
tg
tg
tsignaling slot
tsignaling slot
John A. Stine, Self
July 2009

## Slide 50: Late Signal Transmission
Slide <number>
We select the minimum time to sense a signal, tsf, such that tsf > sn and tsf  ss
Observations
July 2009
John A. Stine, Self

## Slide 51: Early Signal Transmission
Slide <number>
Observations
Recall late signal transmission observations
Largest sn
Smallest ss
John A. Stine, Self
July 2009

## Slide 52: Design Equations – Specified Sensing Time
Slide <number>
Ensures tsf > sn
Ensures ss ≥ sf
Ensures tsf > sn
John A. Stine, Self
July 2009

## Slide 53: Design Equations – Variable Sensing Time
Slide <number>
Assume sm1 is the minimum time to sense and sm2 is the maximum time it takes to sense then the design seeks tsm1 > sn and tsm2  ss
Ensures tsf > sn
Ensures ss ≥ sm2
Ensures sm1 > sn
John A. Stine, Self
July 2009

## Slide 54: Using tp
Slide <number>
If signals can be differentiated between slots, tp rather than p can be used in the previous designs and the equations become
Ensures ss ≥ sm2
John A. Stine, Self
July 2009

## Slide 55: Signal Slot Sizing Summary
Amount of overhead depends on the characteristics of the radio and their maximum range
  Consider the method for sizing the 802.11 time slot
  An SCR signaling slot is increased by the maximum difference in time reference between two nodes
t
Propagation time
Minimum time to detect a signal
Time to transition from the receive to transmit state
p
sf
rt
tslot
t
Propagation time
Minimum time to detect a signal
Time to transition from the receive to transmit state
p
sf
rt
tslot
sy
Maximum synchronization difference
Slide <number>
John A. Stine, Self
July 2009