IEEE P802.11
Wireless LANs

| TGad Conference Call Minutes |
| --- |
| Date: 2010-07-22 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Eldad Perahia | Intel Corporation | 2111 NE 25th Ave Hillsboro, OR 97124 | 503-712-8081 | eldad.perahia@intel.com |
| Vinko Erceg | Broadcom |  |  | verceg@broadcom.com |

# Conference Call Times

| Date | Start Time | End Time |
| --- | --- | --- |
| January 7, 2010 | 10 AM Eastern Time | 12 PM Eastern Time |
| February 25, 2010 | 10 AM Eastern Time | 12 PM Eastern Time |
| April 29, 2010 | 10 AM Eastern Time | 12 PM Eastern Time |
| July 1, 2010 | 10 AM Eastern Time | 12 PM Eastern Time |
| July 22, 2010 | 10 AM Eastern Time | 12 PM Eastern Time |

# Minutes from January 7, 2010 Conference Call

## Agenda

- Check to see if anyone is not familiar with the IEEE patent policy http://standards.ieee.org/board/pat/pat-slideset.pdf

- Attendance by email

- Presentations

  - Channel Model discussion

  - 11-10/0011r0, Radio over Fiber for an optimal 60 GHz Home Area Network

  - 11-09/1317r1, Internet Traffic Modeling, Sai Nandagopalan

## Patent Policy

No one was not familiar with the IEEE patent policy.

No essential patent disclosure

## Channel modeling

- Preparing human blockage statistics (TU Braunschwieg)  for fading  in Los Angeles

  - PDF of depth and PDF of number of taps affected

- Conference channel model being updated

  - Pathloss

  - Is now complete, no TBDs

- Living room being updated

  - Statistical results from NICT on inter-cluster parameters added

  - Pathloss will be done by LA meeting

- Enterprise cubicle

  - Inter and intra cluster almost done, will be presented in LA meeting

- Complete document should be ready by LA

- Continue discussion with NICT on polarization and inter cluster parameters

- Question: What are Cubicle environment assumptions?

  - Ray tracing plus reflection measurements used

- Question: what are the positions?

  - AP on ceiling, devices in cube

- Question: how is blocking being included, since normalization is being performed in Matlab?

  - Need to be discussed

- Question: independent channel instantiation for packet?

  - yes

## 09/1317r1

- Question: HTTP parameters taken from references from slide 9? references are old

- Taken from references and simulators like NS2 and Opnet, also what LTE and Wimax using

- Question: What issues of TCP that will differentiate proposals?

  - Transfer time

  - Stabalization time

## 10/0011r0

- Question: Slide 20 says optimizes global efficiency, but system operates as one AP over the whole home.  Wouldn’t AP/room be more efficient?

- Question: What additional delays does the system incur with RF/optical conversions?

  - Delay is dependent on length of the fiber, and not an issue based on 802.15.3c/ECMA

# Minutes from February 25, 2010 Conference Call

## Agenda

- Check to see if anyone is not familiar with the IEEE patent policy http://standards.ieee.org/board/pat/pat-slideset.pdf

- Attendance by email

- Presentations

  - 11-10/0242r0, SCR Synchronization, John Stine

## Patent Policy

No one was not familiar with the IEEE patent policy.

No essential patent disclosure

## 10/0242r0

- Question: What happens two systems with two references move closer together?

# Minutes from April 29, 2010 Conference Call

Vinko chairing meeting.

## Agenda

- Check to see if anyone is not familiar with the IEEE patent policy http://standards.ieee.org/board/pat/pat-slideset.pdf

- Attendance by email

- Presentations

  - 11-10/0489r0, PHY Performance evaluation with 60GHz WLAN channel models, Alexander Maltsev

  - 11-10/0490r0, Intra cluster response model and parameter for the enterprise cubicle environments at 60GHz, Hirokazu Sawada

## Patent Policy

No one was not familiar with the IEEE patent policy.

No essential patent disclosure

## 10/0489r0

- PER vs. SNR curves, beamforming adaptation used (for maximum power), OFDM simulation, normalization per channel snapshot. Comparison of AWGN curves to omni-directional and directional-directional antenna cases for different channel models.

- Q/A

  - James: is modulation and coding from some proposal ?

    - Alexander: standard coding

  - James: is it soft decision decoder? Can you give more detail

    - Alexander: standard coding, I can send you the information

    - Kato-san: answer is in one of the slides

  - Martin: did you assume equalization?

    - Alexander: yes

  - Brian: differences are because normalization influences the results

    - Alexander: yes, antenna gain is not accounted for, differences would be larger in reality

  - Brian: flat channel?

    - Alexander: no, there is intercluster interference creating frequency selectivity

  - Vinko: what kind of equalization did you use?

    - Alexander: per tone equalization

  - Kato-san: question about beam adaptation: how do you normalize?

    - Alexander: evaluation methodology uses normalization per each channel impulse response

  - Nokia: same channel impulse response per packet? How may packets?

    - Alexander: yes, 10000 packets

  - Kato-san: in slide 10, I see that performance is close to LOS performance for omni and directional case

    - Alexander: this is because of normalization and intracluster parameters

  - James: your differences are because of the fading on each tone

    - Vinko: yes, because of the frequency selectivity

## 10/0242r0

- Measurements were presented and impulse responses, reflection from walls and metal frame and metal pipe, strong reflections from metal surfaces

- Q/A

  - Vinko: very interesting, how many locations don’t have metal reflections?

    - Kato-san: answer is in slide 10

  - James: did you adjust angle of antenna to point into direction of reflection, are they facing the ceiling?

  - James:  there is no reflection from plaster board?

    - Sawada-san: yes, no reflection

  - Vinko: both pipe and metal frame are metal but reflection is much different

    - Kato-san: this is because of the metal shape

  - Vinko: pipe disperses the signal

  - Alexander: thank you very much for measurement and parameters , let’s discuss off line which parameters to use, maybe some averaging is needed

    - Kato-san: agreed

  - Vinko: I would also like to thank you for the measurements and results, we can now complete the channel models

  - Cisco: directional antenna was used?

    - Sawada-san: antenna is described on slide 17

End of call, ended at 8:10am PDT

# Minutes from July 1, 2010 Conference Call

Vinko chairing meeting.

## Agenda

- Check to see if anyone is not familiar with the IEEE patent policy http://standards.ieee.org/board/pat/pat-slideset.pdf

- Attendance by email

- Comment resolution spreadsheet discussion, 11-10-0717r1

## Patent Policy

No one was not familiar with the IEEE patent policy.

No essential patent disclosure

## 10/0717r1

- Presenter: Carlos Cordeiro

- Carlos went over the spreadsheet organization: column meaning, filtering, type of comments, etc. Work needs to be done regarding grouping. Beamforming may need subgroups. Coexistence has only 3 comments so that grouping is not necessary for this category.

- Thomas: Is there a limit on number of comments for each sub group?

- Carlos: it is very hard to put a number on it. 20-30 comments per group seems reasonable. Anyone can bring submissions. Groups of people can work on comment resolution.

- Kapseok: classification of the groups seems fine. Comment 54 in General group is a mistake, I would like to delete the comment.

- Carlos: you can withdraw the comment.

- Vinko: please send a “withdraw CID #” notice to the TGad reflector for record keeping.

- Kapseok: I propose comment group PHY subgroups: SC, OFDM, common preamble, and control PHY.

- Carlos: next week we can work on grouping and ask for submissions.

- Avinash: does every comment need to be represented by a presentation?

- Carlos: not all, some of them may be done in the meeting, if they are simple enough.

- Assaf: editor may resolve editorial comments.

- There were no additional questions, conference call ended at 7:45am PST.

# Minutes from July 22, 2010 Conference Call

## Agenda

- Check to see if anyone is not familiar with the IEEE patent policy http://standards.ieee.org/board/pat/pat-slideset.pdf

- Attendance by email

- Comment resolution of Assaf’s assigned CIDs

## Patent Policy

No one was not familiar with the IEEE patent policy.

No essential patent disclosure

## 10/0944r0

- Presenter: Assaf

- CIDs:

  - 3: no objection to resolution

  - 405

    - Modify to “figure 30”

    - discussion on aggregation and block ack

    - no objection to resolution

  - 406

    - Modified grammar

    - no objection to resolution

  - 407: no objection to resolution

  - 408: no objection to resolution

  - 412: no objection to resolution

  - 413: move to 10/0894

  - 414: no objection to resolution

  - 416: no objection to resolution

  - 417: no objection to resolution

  - 56: no objection to resolution

  - 418: no objection to resolution

  - 346: no objection to resolution

- Will upload 10/944r1 to server

## 10/0894r0

- Presenter: Assaf

- CIDs:

  - 447: no objection to resolution

  - 448

    - change to counter, and refer to CID 73

    - no objection to resolution

  - 449: no objection to resolution

  - 353: remove from this document, assigned to Daniel

  - 316

    - discussion on where operations occur in TXOP and how to start TXOP

    - add “is deleted” to resolution

    - no objection to resolution

  - 58 & 59: no objection to resolution

  - 317

    - Fixed grammar

    - no objection to resolution

  - 318 & 319

    - Fixed grammar

    - no objection to resolution

  - 461: no objection to resolution

  - 438: no objection to resolution

  - 386 & 413

    - Padam: BRP is iterative, any limit to # of iterations

    - Assaf: no limit

    - Padam: should there be a limit

    - Assaf: may difficult to define, and not related to this comment

    - MIDC can be done two difference ways, split into two

    - no objection to resolution

# Attendance

| Participant | Jan 7 | Feb 25 | Apr 29 | July 1 | July 22 |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| John Barr (NICT) | x |  | x | x |  |  |  |  |  |  |  |
| Ted Booth (Sony) | x | x |  | x | x |  |  |  |  |  |  |
| George Bumiller (RIM) |  | x |  |  |  |  |  |  |  |  |  |
| Philippe Chambelin (Technicolor) |  |  |  | x |  |  |  |  |  |  |  |
| Kapseok Chang (ETRI) |  |  |  | x |  |  |  |  |  |  |  |
| Carlos Cordeiro (Intel) |  |  |  | x | x |  |  |  |  |  |  |
| Lee Drennan (Buffalo Technology) |  | x |  |  | x |  |  |  |  |  |  |
| Thomas DERHAM (France Telecom (Orange Labs Tokyo, Japan)) | x |  |  | x |  |  |  |  |  |  |  |
| Chunjie Duan (Mitsubishi Electric Corp) |  |  |  |  | x |  |  |  |  |  |  |
| Vinko Erceg (Broadcom) | x |  | x | x |  |  |  |  |  |  |  |
| Sudheer Grandhi (InterDigital) | x | x |  |  | x |  |  |  |  |  |  |
| Joffray Guillory (France Telecom / Orange Labs) | x |  |  |  |  |  |  |  |  |  |  |
| Christopher Hansen (Broadcom) |  |  |  | x | x |  |  |  |  |  |  |
| Brian Hart (Cisco) |  | x | x | x | x |  |  |  |  |  |  |
| Martin Jacob (TU Braunschwieg) | x |  | x |  |  |  |  |  |  |  |  |
| Avinash Jain (Qualcomm) |  |  |  | x |  |  |  |  |  |  |  |
| Padam Kafle (Nokia) | x | x |  |  | x |  |  |  |  |  |  |
| Naveen Kakani (Nokia) |  | x |  |  |  |  |  |  |  |  |  |
| Assaf Kasher (Intel) |  |  |  | x | x |  |  |  |  |  |  |
| Shu Kato (NICT) | x |  | x |  |  |  |  |  |  |  |  |
| Brad Lynch (Peraso Technologies) | x | x |  |  |  |  |  |  |  |  |  |
| Alexander Maltsev (Intel) |  |  | x |  |  |  |  |  |  |  |  |
| Roman Maslennikov (University of Nizhny Novgorod) | x |  |  |  |  |  |  |  |  |  |  |
| George Miller |  |  |  | x |  |  |  |  |  |  |  |
| Sai Nandagopalan (Broadcom) | x |  |  |  |  |  |  |  |  |  |  |
| Eldad Perahia (Intel) | x | x |  |  | x |  |  |  |  |  |  |
| Sandrine ROBLOT (France Telecom / Orange Labs) | x |  |  |  |  |  |  |  |  |  |  |
| Hirokazu Sawada (Tohoku University) | x | x | x |  |  |  |  |  |  |  |  |
| John Stine (Self) | x | x |  |  |  |  |  |  |  |  |  |
| Hossein Taghavi (Qualcomm) | x | x |  | x | x |  |  |  |  |  |  |
| Ichihiko Toyoda (NTT) |  |  |  | x |  |  |  |  |  |  |  |
| James Yee (Mediatek) |  |  |  |  |  |  |  |  |  |  |  |
| SK Yong (Marvell) |  |  |  | x | x |  |  |  |  |  |  |
| Xin Zhang (NICT) |  |  |  |  | x |  |  |  |  |  |  |

# Text boxes

Abstract

TGad conference call minutes for 2010.