IEEE P802.11
Wireless LANs

| TGae Requirements and Use Cases |
| --- |
| Date: 2010-01-18 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Michael Montemurro | Research in Motion | 4701 Tahoe Blvd, Mississauga, ON. L4W 0B4 | +1-905-629-4746 | mmontemurro@rim.com |

### Overview

This summarizes the Use Cases and Requirements for prioritization of management frames.

# Requirements

The following table summarizes the requirements for Prioritization of Management Frames.

|  | Requirement | Use Case Description |
| --- | --- | --- |
| 1 | AP advertises Management Frame Prioritization. | 1 |
| 2 | AP is configured and advertises Management Frame Prioritization Policy. | 1 |
| 3 | Management Frame Prioritization capable STA indicates management frame prioritization capability when it associates. | 1 |
| 4 | Management frame priortization covers RRM and WNM requests and reports. | 1 |
| 5 | STA and AP adhere to Management Frame prioritization policy to transmit managmeent frames. | 1 |
| 6 |  |  |
| 7 |  |  |
| 8 |  |  |

# Use cases

### 1. Use of Radio Resource Management(RRM) or Wireless Network Management(WNM) Frames during Voice Call

- Voice-capable STA associates to a AP that supports RRM or WNM.

- STA and AP exchange Management Frame Prioritzation capabilities

  - Frame Prioritization is configured in the AP infrastructure and advertised by the AP.

  - WNM and RRM frames are included as supported for Frame Prioritization.

- The STA initiates a Voice Call on the WLAN network (call can be incoming or outgoing)

  - Voice frames are transmitted at AC-VO

  - AP initiates RRM or WNM report requests (the RRM or WNM report request is transmitted at the configured AC).

  - STA responds to the RRM or WNM at the configured/negotiated AC.

- STA’s do not support Management Frame Prioritization use legacy behaviour for medium access. AP uses legacy behavior for medium access to communicate with a legacy STA

### 2. Use of management frames (e.g. native GAS) in pre-associated state

- A STA discovers an AP using either active or passive scanning procedures.

- The AP advertises management frame prioritization information for pre-association frames(?)

- The STA issues a Native GAS request to the AP using the (advertised?) AC.

- The AP issues a Native GAS response to the STA using the (advertised?) AC.

- Could the STA use a different AC after it has been associated?