## Slide 1
[Intra-cluster response model and parameter for channel modeling at 60GHz (Part 3)]
Date: 2010-1-19
Authors:

## Slide 2: Abstract
This paper will give all intra-cluster parameters for 3 different environments defined by TGad
To align intra-cluster channel models, this paper has adopted K-factor and ready to be integrated with inter-cluster channel models given by doc. 09/334r4 by Alexander
For simpler PHY simulations:
Single channel model for each living, conference, and cubicle room environment is good preferable rather than too many channel models
We suggest to use the channel model with 30 degree HPBW antennas and vertical polarization for simulation scenarios for directional antenna communications.

## Slide 3: Measurement system
Instrument: Vector network analyzer
Antenna: Conical horn antenna
q
f

## Slide 4: Measurement set up
Parameter | Value
Center frequency | 62.5 GHz
Band width | 3 GHz
Number of frequency points | 801
Frequency step | 3.75 MHz
HPBW of antenna (Gain) | 30degree(STA), 90 degree(AP)
Polarization | Vertical(STA), Circular(AP)
Calibration | Direct port connection without antennas

## Slide 5: Living room environment ‘defined by TGad’
Antenna height:
1.5m (LoS scenario)
1.0 m (NLoS scenario)
D = 3m

## Slide 6: Conference room environment “defined by TGad”

## Slide 7: Floor plan of cubicle office

## Slide 8: STA-STA link
Rx
Tx
Measurement set up
N.A.
Rx
Tx
Manually rotation (30deg step)
This is a very short transmission scenario.

## Slide 9: AP-STA link
AP-STA Link
Tx
Rx
Inside of a cubicle
This is a vertical transmission link scenario.

## Slide 10: Circular polarization is adopted for AP antenna
Rotation
E
E
C Pol.
C Pol.
AP antenna
AP antenna
Polarization mismatch is generated by rotation of PC
Circular polarized signal wave has adopted for AP antenna

## Slide 11: Intra-cluster parameters for all environments (Ant. HPBW: 30deg, V pol.)
Environments |  | kf [dB] | kb [dB] | gf [ns] | gb [ns] | lf [ns-1] | lb [ns-1] | Distribution | Distribution
Living room |  | 11.5 | 10.9 | 1.25 | 8.7 | 0.277 | 0.996 | Rayleigh | Rayleigh
Conference room |  | 16.8 | 18.4 | 6.13 | 6.29 | 0.547 | 0.501 | Rayleigh | Rayleigh
Cubicle | STA-STA LOS | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A
 | AP-STA | N/A | 24.5 | N/A | 0.690 | N/A | 1.13 | N/A | Rayleigh
t = 0
Time of arrival
kb
kf
Central ray of intra-cluster
Arrival rate, lb
Arrival rate, lf
Ray decay factor, gb
Ray decay factor, gf
Rayleigh distribution
Rayleigh distribution

## Slide 12: Summary of Intra-cluster Parameters for Conference Room Environment
Parameter | Notation | Value Doc.09/433r4 | Averaged Value
Pre-cursor rays K-factor | Kf | 5 dB | 10 dB
Pre-cursor rays power decay time | gf | 1.3 ns | 3.7 ns
Pre-cursor arrival rate | lf | 0.20 ns-1 | 0.37 ns-1
Pre-cursor rays amplitude distribution |  | Rayleigh | Rayleigh
Number of pre-cursor rays | Nf | 2 | 6
Post-cursor rays K-factor | Kb | 10 dB | 14.2 dB
Post-cursor rays power decay time | gb | 2.8 ns | 4.5 ns
Post-cursor arrival rate | lb | 0.12 ns-1 | 0.31 ns-1
Post-cursor rays amplitude distribution |  | Rayleigh | Rayleigh
Number of post-cursor rays | Nb | 4 | 8
Proposal; Averaged intra-cluster parameters are used for conference room channel model –two measured environments (Doc.09/433r4 and Doc.10/112r1)

## Slide 13: Summary of Intra-cluster Parameters for Living Room Environment
Parameter | Notation | Value
Pre-cursor rays K-factor | Kf | 11.5 dB
Pre-cursor rays power decay time | gf | 1.25 ns
Pre-cursor arrival rate | lf | 0.28 ns-1
Pre-cursor rays amplitude distribution |  | Rayleigh
Number of pre-cursor rays | Nf | 6
Post-cursor rays K-factor | Kb | 10.9 dB
Post-cursor rays power decay time | gb | 8.7 ns
Post-cursor arrival rate | lb | 1.0 ns-1
Post-cursor rays amplitude distribution |  | Rayleigh
Number of post-cursor rays | Nb | 8
Proposal; Intra-cluster parameters extracted from measured data (Doc.10/112r1)

## Slide 14: Conclusion
Intra-cluster channel models for two environments are integrated and proposed (Doc.09/433r4 and Doc.10/112r1): 30 degree HPBW antennas for both Tx/Rx and vertical polarization
Ready to merge with inter-cluster channel models
Preliminary intra-cluster parameters for cubicle environment are presented