IEEE P802.11
Wireless LANs

Support for 802.1Qat in 802.11

Date: 2010-05-18

| Name | Company | Address | Phone | email |
| --- | --- | --- | --- | --- |
| Ganesh Venkatesan | Intel Corp | 2111 NE 25th Ave, Hillsboro, OR | +1-503-334-6720 | Ganesh.Venkatesan@intel.com |

Abstract

This submission contains the normative text related to changes required in 802.11 in order to support 802.1Qat SRP over 802.11. This document is based on the presentation in document 10/219r7 (implements support for proposal 2a in slide-17). In addition, this document fixed omissions/errors in the original submission (10/137r0): missing MLME interface. This document is based on 802.11aa Draft 0.04. Editorial instructions are relative to the contents of 802.11aa Draft 0.04.

Editor: Insert a definition for the Higher Layer Stream ID element to Table 7-26

| Information Element | Element ID | Length (in octets) | Extensible |
| --- | --- | --- | --- |
| Higher Layer Stream ID (See 7.3.2.aa96) | <ANA> | Variable | Yes |

Editor: Insert a definition for the Higher Layer Stream ID element to Clause 7.3.2

7.3.2.aa96  Higher Layer Stream ID Element

The Higher Layer Stream ID element identifies a higher layer stream. This element is used to bind non-atomic operations between the non-AP STA and the AP, required to support the higher layer stream. See 11.4.4 AP Initiated TS Setup.

|  | Element ID | Length | Higher Layer Stream ID |
| --- | --- | --- | --- |
| Octets | 1 | 1 | Variable |

Figure 7-aa20—Higher Layer Stream ID element format

The Element ID field is set to the Higher Layer Stream ID value in Table 7-26

The value of the Length field is variable and is set to the length of the Higher Layer Stream ID.

The Higher Layer Stream ID field is an octet string identifying the stream.

7.4.2 QoS Action frame details

Editor: Insert a row for ADDTS Complete to Table 7-45 – QoS Action field values

Several Action frame formats are defined for QoS purposes. The Action field values associated with each frame format within the QoS category are defined in Table 7-45 (QoS Action field values).

Table 7-45—QoS Action field values

| Action Field Value | Meaning |
| --- | --- |
| 0 | ADDTS Request |
| 1 | ADDTS Response |
| 2 | DELTS |
| 3 | Schedule |
| 4 | ADDTS Complete |
| 5-255 | Reserved |

7.4.2.1 ADDTS Request frame format

The ADDTS frames are used to carry TSPEC and optionally TCLAS elements to set up and maintain TSs using the procedures defined in 11.4 (TS operation).

The frame body of the ADDTS Request frame contains the information shown in Table 7-46 (ADDTS Request frame body).

Table 7-46—ADDTS Request frame body

| Order | Information |
| --- | --- |
| 1 | Category |
| 2 | Action |
| 3 | Dialog Token |
| 4 | TSPEC |
| 5-n | TCLAS (optional) |
| n+1 | TCLAS Processing (optional) |
| n+2 | Higher Layer Stream ID (only in AP initiated TS Setup) |

Editor: Add a new paragraph to the end of the definition ADDTS Request QoS Action Frame

The Higher Layer Stream ID element identifies the higher layer stream corresponding to which this ADDTS Request frame is exchanged between the non-AP STA and the AP.

7.4.2.2 ADDTS Response frame format

The ADDTS Response frame is transmitted to a non-AP STA

- in response to an ADDTS request frame from the non-AP STA or

- autonomously by the SME at the AP in response to a higher layer protocol. See 11.4.4 TS Setup,

The frame body of the ADDTS Response frame contains the information shown in Table 7-47 (ADDTS Response frame body).

Table 7-47—ADDTS Response frame body

| Order | Information |
| --- | --- |
| 1 | Category |
| 2 | Action |
| 3 | Dialog Token |
| 4 | Status Code |
| 5 | TS Delay |
| 6 | TSPEC |
| 7-n | TCLAS (optional) |
| n+1 | TCLAS Processing (optional) |
| n+2 | Schedule |
| n+3 | Higher Layer Stream ID (only in AP initiated TS Setup) |

The Category field is set to 1(representing QoS).

The Action field is set to 1 (representing ADDTS response).

The Status Code field is defined in 7.3.1.9 (Status Code field).

The Dialog Token, TS Delay, TSPEC, TCLAS, and TCLAS Processing fields in this frame are contained in an MLME-ADDTS.response primitive that causes the frame to be sent. The TS Delay information element is present in an ADDTS Response frame only if the status code is set to 47. The Schedule element, defined in 7.3.2.34, is present in an ADDTS Response frame only if the status code is set to 0 (i.e., when the TS is admitted).

The Higher Layer Stream ID element identifies the higher layer stream corresponding to which this ADDTS Response frame is exchanged between the non-AP STA and the AP.

If a TSPEC is admitted as a result of an AP initiated TS Setup, an ADDTS Response frame is sent autonomously to the non-AP STA where,

- the Dialog Token field is set to zero,

- TSPEC is set to the TSPEC that the AP has admitted autonomously for the non-AP,

- TCLAS and TCLAS processing fields are not present,

- the Status Code is set to 0 (the corresponding TSPEC is admitted),and

- the Schedule element is set to reflect schedule information corresponding to the TSPEC specification

- the corresponding Higher Layer Protocol ID element is included

Editor: Add a new subclause to 7.4.2 as follows:

7.4.2.5 ADDTS Complete frame format

The ADDTS Complete action frame is used in the AP Initiated TS Setup procedure and is sent by a non-AP STA to an AP. The frame body of the ADDTS Complete frame contains the information shown in Table 7-48.aa (ADDTS Complete frame body).

Table 7-48—ADDTS Complete frame body

| Order | Information |
| --- | --- |
| 0 | Category |
| 1 | Action |
| 2 | Higher Layer Stream ID |
| 3 | Status Code |

The Category field is set to 1 (representing QoS).

The Action field is set to 4 (representing ADDTS Complete).

The Higher Layer Stream ID is defined in 7.3.2.aa96 (Higher Layer Stream ID element).

The Status Code field is defined in 7.3.1.7 (Status Code field).

An ADDTS Complete action frame is used to by a non-AP STA to indicate the completion of an AP Initiated TS Setup procedure (11.4.4 TS Setup).

10.3.24.4 MLME-ADDTS.response

10.3.24.4.1 Function

This primitive responds to the request for a TS addition (or modification) by a specified non-AP STA MAC

entity.

10.3.24.4.2 Semantics of the service primitive

The primitive parameters are as follows:

MLME-ADDTS.response (

ResultCode,

DialogToken,

Non-APSTAAddress,

TSDelay,

TSPEC,

Schedule,

TCLAS,

TCLASProcessing,

Higher Layer Stresam ID,

VendorSpecificInfo)

| Name | Type | Valid Range | Description |
| --- | --- | --- | --- |
| Resultcode | Enumeration | SUCCESS, INVALID_PARAMETERS, REJECTED_WITH_SUGGESTED_ CHANGES, REJECTED_FOR_DELAY_PERIOD, TIMEOUT, TRANSMISSION_FAILURE | Indicates the results of the corresponding MLMEADDTS. Indication primitive. Set to SUCCESS, if the response is generated AP is responding to a higher layer protocol |
| DialogToken | Integer | 0 or as defined in the corresponding MLMEADDTS. indication | DialogToken of the matching MLME-ADDTS.indication primitive. Set to 0, if the response is generated AP is responding to a higher layer protocol |
| Non AP STA Address | MAC Address |  | Contains the non-AP STA address of the matching MLME-ADDTS.indication primitive or the non-AP STA address specified by the higher layer protocol in response to which the SME at the AP invokes this primitive |
| TSDelay | Integer | >= 0 | When the result code is REJECTED_FOR_DELAY_ PERIOD, provides the amount of time a STA should wait before attempting another ADDTS request frame. Set to 0, if the response is generated AP is responding to a higher layer protocol |
| TSPEC | As defined in frame format | As defined in frame format | Specifies the QoS parameters of the TS. |
| Schedule | As defined in frame format | As defined in frame format | Specifies the schedule information, service start time, SI, and the specification interval. |
| TCLAS (0 or more) | As defined in frame format | As defined in frame format | Specifies the rules and parameters by which an MSDU may be classified to the specified TS. This parameter is not may not be present if this primitive is invoked by the SME at the AP in response to a higher layer protocol. |
| TCLASProcessing | As defined in frame format | As defined in frame format | Specifies how the TCLAS elements are to be processed when there are multiple TCLAS elements. This parameter is may not be not present if this primitive is invoked by the SME at the AP in response to a higher layer protocol. |
| Higher Layer Stream ID | As defined in frame format | As defined in frame format | Identifies the higher layer stream corresponding to which this primitive is invoked. This parameter is only present if this primitive is invoked by the SME at the AP in response to a higher layer protocol. |
| VendorSpecificInfo | A set of information elements | As defined in 7.3.2.26 (VendorSpecific information element) | Zero or more information elements. |

The following apply to the case where this primitive is generated as a result of the SME at the HC receiving a MLME-ADDTS.indication:

- The DialogToken and non-AP STA Address parameters contain the values from the matching MLMEADDTS. indication primitive.

- If the result code is SUCCESS, the TSPEC and (optional) TCLAS parameters contain the values from the matching MLME-ADDTS-indication.

- If the result code is REJECTED_WITH_SUGGESTED_CHANGES, the TSPEC and TCLAS parameters represent alternative proposed TS. The TS, however, is not created. The TSID and direction values within the TSPEC are as in the matching MLME-ADDTS.indication primitive. The difference may lie in the QoS(e.g., minimum data rate, mean data rate, and delay bound) values, as a result of admission control performed at the SME of the HC on the TS requested to be added (or modified) by the non-AP STA. If sufficient bandwidth is not available, the QoS values may be reduced. In one extreme, the minimum data rate, mean data rate, and delay bound may be all set to 0, indicating that no QoS is to be provided to this TS.

10.3.24.4.3 When generated

This primitive is generated by the SME at the HC

- as a result of an MLME-ADDTS.indication primitive to initiate addition (or modification) of a TS with a specified peer MAC entity or entities, or

- in response to higher layer protocol

10.3.24.4.4 Effect of receipt

This primitive approves addition (or modification) of a TS requested by or on behalf of a specified non-AP STA MAC entity, with or without altering the TSPEC.

This primitive causes the MAC entity at the HC to send an ADDTS Response frame in the corresponding QoS Action management frame to the requesting non-AP STA containing the specified parameters.

10.3.24.4.aa ADDTS Response Indication

10.3.24.4.1 Function

This primitive is generated by the MLME when it receives an ADDTS response from the HC.

10.3.24.4.2 Semantics of the service primitive

The primitive parameters are as follows:

MLME-ADDTSResponse.indication (

ResultCode,

DialogToken,

Non-APSTAAddress,

TSDelay,

TSPEC,

Schedule,

TCLAS,

TCLASProcessing,

Higher Layer Stream ID,

VendorSpecificInfo)

| Name | Type | Valid Range | Description |
| --- | --- | --- | --- |
| Resultcode | Enumeration | SUCCESS, INVALID_PARAMETERS, REJECTED_WITH_SUGGESTED_ CHANGES, REJECTED_FOR_DELAY_PERIOD, TIMEOUT, TRANSMISSION_FAILURE | Indicates the results of the corresponding MLMEADDTS. Indication primitive. Set to SUCCESS, if the response is generated AP is responding to a higher layer protocol |
| DialogToken | Integer | 0 or as defined in the corresponding MLMEADDTS. indication | DialogToken of the matching MLME-ADDTS.indication primitive. Set to 0, if the response is generated AP is responding to a higher layer protocol |
| Non AP STA Address | MAC Address |  | Contains the non-AP STA address of the matching MLME-ADDTS.indication primitive or the non-AP STA address specified by the higher layer protocol in response to which the SME at the AP invokes this primitive |
| TSDelay | Integer | >= 0 | When the result code is REJECTED_FOR_DELAY_ PERIOD, provides the amount of time a STA should wait before attempting another ADDTS request frame. Set to 0, if the response is generated AP is responding to a higher layer protocol |
| TSPEC | As defined in frame format | As defined in frame format | Specifies the QoS parameters of the TS. |
| Schedule | As defined in frame format | As defined in frame format | Specifies the schedule information, service start time, SI, and the specification interval. |
| TCLAS (0 or more) | As defined in frame format | As defined in frame format | Specifies the rules and parameters by which an MSDU may be classified to the specified TS. This parameter is may not be present if this primitive is invoked by the SME at the AP in response to a higher layer protocol. |
| TCLASProcessing | As defined in frame format | As defined in frame format | Specifies how the TCLAS elements are to be processed when there are multiple TCLAS elements. This parameter is may not be present if this primitive is invoked by the SME at the AP in response to a higher layer protocol. |
| Higher Layer Stream ID | As defined in frame format | As defined in frame format | Identifies the higher layer stream corresponding to which this frame was sent by the AP. This parameter is only present if this primitive is invoked by the SME at the AP in response to a higher layer protocol. |
| VendorSpecificInfo | A set of information elements | As defined in 7.3.2.26 (VendorSpecific information element) | Zero or more information elements. |

10.3.24.4.3 When generated

This primitive is generated by the MLME at the non-AP STA when an ADDTS Response action frame is received from the HC.

10.3.24.4.4 Effect of receipt

This primitive indicates that resource corresponding to the TSPEC included in the indication has been committed by the HC on behalf of the non-AP STA.

10.3.24.8 ADDTS Complete Request

10.3.24.8.1 Function

This primitive requests to indicate that the AP initiated TS setup procedure is completed.

10.3.24.8.2 Semantics of the service primitive

The primitive parameters are as follows:

MLME-ADDTSComplete.request (

Higher Layer Stream ID,

Status Code,

VendorSpecificInfo

)

| Name | Type | Valid Range | Description |
| --- | --- | --- | --- |
| Stream ID | Higher Layer Stream ID |  | Higher Layer Stream ID corresponding to which the AP initiated this TS setup. |
| Status Code | Successful or Unspecified Failure | 0 or 1 (as defined in Table 7-23 – Status codes) | Indicates the status of the AP initiated TS Setup procedure |
| VendorSpecificInfo | A set of elements | As defined in 7.3.2.26 (Vendor Specific element) | Zero or more elements |

10.3.24.5.3 When generated

This primitive is generated by the SME at a non-AP STA to indicate the completion of an AP initiated TS Setup procedure to the AP.

.

10.3.24.5.4 Effect of receipt

This primitive indicates the completion of the AP initiated TS setup procedure. The MLME subsequently issues an MLME-ADDTS.confirm primitive that reflects the results.

This primitive causes the local MAC entity to send out a ADDTS Complete action frame containing the specified parameters.

10.3.24.9 ADDTS Complete Confirm

10.3.24.9.1 Function

This primitive reports the transmission status of a ADDTS Complete action frame.

10.3.24.9.2 Semantics of the service primitive

The primitive parameters are as follows:

MLME-ADDTSComplete.confirm (

ResultCode,

Higher Layer Stream ID

)

| Name | Type | Valid Range | Description |
| --- | --- | --- | --- |
| ResultCode | Enumeration | SUCCESS, INVALID_PARAMETERS, FAILURE | Indicates the results of the corresponding MLMEADDTSComplete. request primitive. |
| Stream ID | Higher Layer Stream ID |  | Higher Layer Stream ID from the TSPEC element included in the autonomous ADDTS Response from the AP |

10.3.24.9.3 When generated

This primitive is generated by the MLME as a result of an MLME-ADDTSComplete.request primitive after the

ADDTS Complete action frame has been sent (or attempts to send it have failed).

10.3.24.9.4 Effect of receipt

The SME is notified of the results of the ADDTSComplete procedure.

10.3.24.10 ADDTS Complete Indication

10.3.24.10.1 Function

This primitive reports the completion of the AP initiated TS setup procedure.

.

10.3.24.7.2 Semantics of the service primitive

The primitive parameters are as follows:

MLME-ADDTSComplete.indication (

STA Address

Higher Layer Stream ID,

StatusCode,

VendorSpecificInfo

)

| Name | Type | Valid Range | Description |
| --- | --- | --- | --- |
| STA Address | MAC Address |  | Specifies the MAC address of the non-AP STA from which the ADDTS Complete action frame was received |
| Stream ID | Higher Layer Stream ID |  | Higher Layer Stream ID from the TSPEC element included in the autonomous ADDTS Response from the AP |
| Status Code | Successful or Unspecified Failure | 0 or 1 (as defined in Table 7-23 – Status codes) | Indicates the status of the AP initiated TS Setup procedure |
| VendorSpecificInfo | A set of elements | As defined in 7.3.2.26 (Vendor Specific element) | Zero or more elements |

10.3.24.7.3 When generated

This primitive is generated by the MLME when it receives a ADDTS Complete action frame from the specified peer MAC entity.

10.3.24.7.4 Effect of receipt

The SME is notified of the completion of the AP initiated TS setup procedure by the specified peer MAC entity.

11.4 TS operation

11.4.1 Introduction

A TSPEC describes the traffic characteristics and the QoS requirements of a TS. The main purpose of the TSPEC is to reserve resources within the HC and modify the HC’s scheduling behavior. It also allows other parameters to be specified that are associated with the TS, such as a traffic classifier and acknowledgment policy.

A TS may have one or more TCLAS (within the discretion of the STA that sets up the stream) associated with it. The AP uses the parameters in the TCLAS elements to filter the MSDUs belonging to this TS so that they can be delivered with the QoS parameters that have been set up for the TS.

TSPEC and the optional TCLAS elements are transported on the air by the ADDTS, in the corresponding QoS Action frame and across the MLME SAP by the MLME-ADDTS primitives.

Following a successful negotiation, a TS is created, identified within the non-AP STA by its TSID and direction, and identified within the HC by a combination of TSID, direction, and non-AP STA address.

It is always the responsibility of the non-AP STA to initiate the creation of a TS regardless of its direction, except in the case where a TS is created by the AP in response to a higher layer protocol

11.4.4 TS setup

A TS is setup can be initiated by an AP or a non-AP STA.

Editor:  Wrap the first paragraph in 11.4.4 and Figure 11-8 TS Setup under an unnumbered header non-AP initiated TS Setup

Editor: Created a new unnumbered clause titled “AP initiated TS Setup” and include the following under it.

Figure 11-8aa shows the sequence of messages occurring at a TS setup when initiated by the AP. Figure 11-8 shows the sequence of messages occurring at a TS setup when initiated by a non-AP STA. This message sequence in this figure and in the subsequent figures does not show the acknowledgment.

Editor: Replace Figure 11-8aa with the following:

Figure 11-8aa TS Setup when initiated by the AP

TS Setup can be initiated by an AP in response to request originating from higher layer protocols. In these cases a higher layer Stream ID is defined by the higher layer. The Higher Layer Stream ID shall be included in the autonomous ADDTS Response. This Higher Layer Stream ID is used in the TS Setup procedure between the AP and the non-AP STA.

The AP initiates the TS Setup by sending an autonomous ADDTS Response that includes the Higher Layer Stream ID element to the non-AP STA. The non-AP STA may on receipt of the autonomous ADDTS Response from the AP send an ADDTS Request to the AP to negotiate the TSPEC parameters. This negotiation may involve multiple ADDTS Request/ADDTS Response between the non-AP STA and the AP. In all these frames exchanged between the non-AP STA and the AP, the Higher Layer Stream ID corresponding to the AP initiated TS Setup procedure shall be included.

At the end of the negotiation, the non-AP STA shall complete the AP initiated TS Setup procedure by sending an ADDTS Complete action frame that includes the Higher Layer Stream ID corresponding to the AP initiated TS Setup procedure.

Editor: The second paragraph under 11.4.4. TS Setup from the base specification follows from here