IEEE P802.11
Wireless LANs

| TGae Areas of Technical Proposals |
| --- |
| Date: 2010-03-10 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Santosh Pandey | Cisco | 170 West Tasman Drive, San Jose, CA | +1 408 853 5990 | sanpande@cisco.com |

### Overview

This document identifies areas where the TGae group need to consider developing technical proposals. The goals are as follows:

- Agree on areas we need technical proposals and their rough content

- Agree on order in which we develop those proposals (if sequencing is required)

# Areas of Technical Proposals

|  | Area | Details | Requirements # |
| --- | --- | --- | --- |
| 1 | Frame priority mechanism | Define frame prioritation Group/Individual prioritation Capabiltiy to change priority with time/session Depend on network? BSS, IBSS, not-BSS(11p), Mesh or home/ enterprise How does HCCA/EDCA affect the TGae solution? Consider management frame inside data frame? How does TGae address Vendor-specific Action frames, Public Action, or Protected Dual Action frames? For request/response management frames, should the response be set to the same priority as the request? Need to consider how to prioritize frames associated with Emergency Services. | 4, 5, 7, 8, 10, 11, 13, 15, 16, 19, 20, 25, 26, Issues |
| 2 | Frame priority management | Define policy with frame prioritization Can management frames be aggregated? Should TGae provide a means to aggregate prioritized management frames? Should be easy to exchange during capability exchange Does it define change in priority of frames based on STA state/activity, e.g. power save, voice call? Change with time/session Priority range? Allowed lowest-highest priority Capability to extend with future 802.11 changes Should be easy to exchange between STAs The priority policy should be managed on a task basis. Some management frames should remain at a fixed priority (i.e. cannot be addressed by a policy) How are IEEE 802.11n management frames addressed for fixed priority? Should the management prioritization policy be secured for both data confidentiality and integrity. Do we need to modify management frames to signal priority Should sequence numbers be assigned based on priority | Issues |
| 3 | 11ae capability exchange | Advertise 11ae capability Individual/Group frame prioritization exchange or policy enchange If a group is always going to be a set priority, should that priority be exchanged Define setting priorities post-association/pre-association for all 11ae capable clients Define change in priorities post-association/pre-association Security of policy/capability exchange Does the priority information need to be communicated in the header of the TGae frame. (with 11w, each frame requires a sequence number for CCMP to do replay detection). Should the management prioritization policy be communicated in a unicast or group-addressed manner. Should the management prioritization policy be secured for both data confidentiality and integrity. A non-AP STA should not be able to request a management frame prioritization policy. How policy is determined when the STA transitions from one BSS to another BSS. How policy is determined when a STA joins a new BSS. What happens if there is a gap between when the STA associates and when the STA determines the policy? If there is a gap, can the AP query the STA for the management frame prioritization policy? Should a TGae-capable STA apply a new management frame policy when it has been received? Should we be sending as management frames or other type of frame | 1, 2, 3, 6, 9, 10, 12, 14, 15, 17, 18, 20, 21, 22, 23, 24 |
| 4 | Enforcing policy | How to check to see if the STA is observing 11ae prioritization ? Any way to preventing misbehaving STA from disrupting network Should the policy enforcing depend on the frames and STA state, e.g. power save, voice call What does the AP or non-AP STA do when it receives a frame that does not meet the management frame prioritization policy? If legacy clients are present, co-existance | 17, 19, 20, 21, 22, 24 |
| 5 | Backward compatibility | If legacy clients are present, co-existance |  |

The requirements are mapped from doc.: IEEE 802.11-10/0093r5