## Slide 1: OFDM PHY Proposal
Date: 2010-05-01
Author(s): |  |  |  | 
Name | Company | Address | Phone | email
Abu-Surra, Shadi | Samsung |  |  | sasurra@sta.samsung.com
Ban, Koichiro | Toshiba |  |  | koichiro.ban@toshiba.co.jp
Banerjea, Raja | Marvell |  |  | rajab@marvell.com
Basson, Gal | Wilocity |  |  | gal.basson@wilocity.com
Blanksby, Andrew | Broadcom |  |  | andrew.blanksby@broadcom.com
Borges, Daniel | Apple |  |  | drborges@apple.com
Borison, David | Ralink |  |  | david_borison@ralinktech.com
Chang, Kapseok | ETRI |  |  | kschang@etri.re.kr
Chu, Liwen | STMicroelectronics |  |  | Liwen.chu@st.com
Chung, Hyun Kyu | ETRI |  |  | hkchung@etri.re.kr
Coffey, Sean | Realtek |  |  | coffey@realtek.com
Cordeiro, Carlos | Intel |  |  | Carlos.Cordeiro@intel.com
Dorsey, John | Apple |  |  | jdorsey@apple.com
Elboim, Yaron | Wilocity |  |  | yaron.elboim@wilocity.com
Fischer, Matthew | Broadcom |  |  | mfischer@broadcom.com
Giraud, Claude | NXP |  |  | claude.giraud@nxp.com
Golan, Ziv | Wilocity |  |  | Ziv.golan@wilocity.com
Gong, Michelle | Intel |  |  | Michelle.x.gong@intel.com
Grieve, David | Agilent |  |  | david_grieve@agilent.com

## Slide 2
Author(s): |  |  |  | 
Name | Company | Address | Phone | email
Grodzinsky, Mark | Wilocity |  |  | Mark.grodzinsky@wilocity.com
Hansen, Christopher | Broadcom |  |  | chansen@broadcom.com
Hart, Brian | Cisco |  |  | brianh@cisco.com
Hassan, Amer | Microsoft |  |  | amerh@microsoft.com
Hong, Seung Eun | ETRI |  |  | iptvguru@etri.re.kr
Hosoya, Kenichi | NEC |  |  | k-hosoya@ce.jp.nec.com
Hosur, Srinath | Texas Instruments |  |  | hosur@ti.com
Hsu, Alvin | MediaTek |  |  | alvin.hsu@mediatek.com
Hsu, Julan | Samsung |  |  | Julan.hsu@samsung.com
Hung, Kun-Chien | MediaTek |  |  | kc.hung@mediatek.com
Jain, Avinash | Qualcomm |  |  | avinashj@qualcomm.com
Jauh, Alan | MediaTek |  |  | alan.jauh@mediatek.com
Jeon, Paul | LGE |  |  | bjjeon@lge.com
Jin, Sunggeun | ETRI |  |  | sgjin@etri.re.kr
Jones, VK | Qualcomm |  |  | vkjones@qualcomm.com
Joseph, Stacy | Beam Networks |  |  | stacy@beamnetworks.com
Jun, Haeyoung | Samsung |  |  | Haeyoung.jun@samsung.com
Kaaja, Harald | Nokia |  |  | harald.kaaja@nokia.com
Kafle, Padam | Nokia |  |  | padam.kafle@nokia.com
Kakani, Naveen | Nokia |  |  | naveen.kakani@nokia.com
Kasher, Assaf | Intel |  |  | Assaf.kasher@intel.com
Kasslin, Mika | Nokia |  |  | mika.kasslin@nokia.com
Kim, Hodong | Samsung |  |  | hodong0803.kim@samsung.com
Kim, Yongsun | ETRI |  |  | doori@etri.re.kr
Kreifeldt, Rick | Harman International |  |  | rick.kreifeldt@harman.com
Kwon, Edwin | Samsung |  |  | cy.kwon@samsung.com
Kwon, Hyoungjin | ETRI |  |  | kwonjin@etri.re.kr
Kwon, Hyukchoon | Samsung |  |  | hyukchoon.kwon@samsung.com
Laine, Tuomas | Nokia |  |  | tuomas.laine@nokia.com

## Slide 3
Author(s): |  |  |  | 
Name | Company | Address | Phone | email
Lakkis, Ismail | Tensorcom |  |  | ilakkis@tensorcom.com
Lee, Hoosung | ETRI |  |  | hslee@etri.re.kr
Lee, Keith | AMD |  |  | keith.lee@amd.com
Lee, Wooyong | ETRI |  |  | wylee@etri.re.kr
Liu, Yong | Marvell |  |  | yongliu@marvell.com
Lou, Hui-Ling | Marvell |  |  | hlou@marvell.com
Majkowski, Jakub | Nokia |  |  | jakub.majkowski@nokia.com
Marin, Janne | Nokia |  |  | janne.marin@nokia.com
Maruhashi, Kenichi | NEC |  |  | k-maruhashi@bl.jp.nec.com
Matsumoto, Taisuke | Panasonic |  |  | matsumoto.taisuke@jp.panasonic.com
Meerson, Yury | Wilocity |  |  | Yury.meerson@wilocity.com
Mese, Murat | Broadcom |  |  | mesem@broadcom.com
Montag, Bruce | Dell |  |  | bruce_montag@dell.com
Myles, Andrew | Cisco |  |  | amyles@cisco.com
Nandagopalan, Saishankar | Broadcom |  |  | nsai@broadcom.com
Ngo, Chiu | Samsung |  |  | Chiu.ngo@samsung.com
Nikula, Eero | Nokia |  |  | eero.nikula@nokia.com
Park, DS | Samsung |  |  | dspark@samsung.com
Park, Minyoung | Intel |  |  | Minyoung.park@intel.com
Pi, Zhouyue | Samsung |  |  | zpi@sta.samsung.com
Ponnampalam, Vish | MediaTek |  |  | vish.ponnampalam@mediatek.com
Prasad, Narayan | NEC |  |  | prasad@nec-labs.com
Prat, Gideon | Intel |  |  | Gideon.prat@intel.com
Ramachandran, Kishore | NEC |  |  | kishore@nec-labs.com
Raymond, Yu Zhan | Panasonic |  |  | Raymond.Yuz@sg.panasonic.com
Ronkin, Roee | Wilocity |  |  | Roee.ronkin@wilocity.com
Rozen, Ohad | Wilocity |  |  | Ohad.rozen@wilocity.com
Sachdev, Devang | NVIDIA |  |  | dsachdev@nvidia.com
Sadri, Ali | Intel |  |  | Ali.S.Sadri@intel.com
Sampath, Hemanth | Qualcomm |  |  | hsampath@qualcomm.com

## Slide 4
Author(s): |  |  |  | 
Name | Company | Address | Phone | email
Sanderovich, Amichai | Wilocity |  |  | Amichai.sanderovich@wilocity.com
Sankaran, Sundar | Atheros |  |  | Sundar.Sankaran@Atheros.com
Scarpa, Vincenzo | STMicroelectronics |  |  | vincenzo.scarpa@st.com
Seok, Yongho | LGE |  |  | yongho.seok@lge.com
Shao, Huai-Rong | Samsung |  |  | hr.shao@samsung.com
Shen, Ba-Zhong | Broadcom |  |  | bzshen@broadcom.com
Sim, Michael | Panasonic |  |  | Michael.Simhc@sg.panasonic.com
Singh, Harkirat | Samsung |  |  | har.singh@sisa.samsung.com
Soffer, Menashe | Intel |  |  | Menashe.soffer@intel.com
Song, Seungho | SK Telecom |  |  | shsong@sktelecom.com
Sorin, Simha | Wilocity |  |  | Simha.sorin@wilocity.com
Smith, Matt | Atheros |  |  | matt.smith@atheros.com
Stacey, Robert | Intel |  |  | Robert.stacey@intel.com
Sutskover, Ilan | Intel |  |  | Ilan.sutskover@intel.com
Taghavi, Hossain | Qualcomm |  |  | mtaghavi@qualcomm.com
Takahashi, Kazuaki | Panasonic |  |  | takahashi.kazu@jp.panasonic.com
Trachewsky, Jason | Self |  |  | jtrachewsky@gmail.com
Trainin, Solomon | Intel |  |  | Solomon.trainin@intel.com
Usuki, Naoshi | Panasonic |  |  | usuki.naoshi@jp.panasonic.com
Varshney, Prabodh | Nokia |  |  | prabodh.varshney@nokia.com
Vertenten, Bart | NXP |  |  | bart.vertenten@nxp.com
Vlantis, George | STMicroelectronics |  |  | george.vlantis@st.com
Wang, Chao-Chun | MediaTek |  |  | chaochun.wang@mediatek.com
Wang, Homber | TMC |  |  | homber@emcite.com
Wang, James | MediaTek |  |  | james.wang@mediatek.com
Yee, James | MediaTek |  |  | james.yee@mediatek.com
Yucek, Tevfik | Atheros |  |  | Tevfik.Yucek@Atheros.com
Yong, Su Khiong | Marvell |  |  | skyong@marvell.com
Zhang, Hongyuan | Marvell |  |  | hongyuan@marvell.com

## Slide 5: Proposal overview
This presentation is part and is in support of the complete proposal described in 802.11-10/432r0 (slides) and 802.11-10/433r0 (text) that:
  Supports data transmission rates up to 7 Gbps
  Supplements and extends the 802.11 MAC and is backward compatible with the IEEE 802.11 standard
  Enables both the low power and the high performance devices, guaranteeing interoperability and communication at gigabit rates
  Supports beamforming, enabling robust communication at distances beyond 10 meters
  Supports GCMP security and advanced power management
  Supports coexistence with other 60GHz systems
  Supports fast session transfer among 2.4GHz, 5GHz and 60GHz

## Slide 6: OFDM PHY Characteristics
Supports data rates up to ~7 Gbps
  Modulation formats: SQPSK, QPSK, 16-QAM and 64-QAM
  LDPC Coding: rates ½, 5/8, ¾ and 13/16
Designed to operate in NLOS environments
  Fixed Guard Interval (GI) of ~48 ns
  Coding tolerant to significant frequency selectivity
Significant commonality with associated SC PHY
  Common preamble
  Common LDPC coding scheme etc

## Slide 7: OFDM PHY MCS Table
MCS Index | Modulation | Code Rate | NBPSC | NCBPS | NDBPS | Data Rate (Mbps)
10 | SQPSK | 1/2 | 1 | 336 | 168 | 693.00
11 | SQPSK | 5/8 | 1 | 336 | 210 | 866.25
12 | QPSK | 1/2 | 2 | 672 | 336 | 1386.00
13 | QPSK | 5/8 | 2 | 672 | 420 | 1732.50
14 | QPSK | 3/4 | 2 | 672 | 504 | 2079.00
15 | 16-QAM | 1/2 | 4 | 1344 | 672 | 2772.00
16 | 16-QAM | 5/8 | 4 | 1344 | 840 | 3465.00
17 | 16-QAM | 3/4 | 4 | 1344 | 1008 | 4158.00
18 | 16-QAM | 13/16 | 4 | 1344 | 1092 | 4504.50
19 | 64-QAM | 5/8 | 6 | 2016 | 1260 | 5197.50
20 | 64-QAM | 3/4 | 6 | 2016 | 1512 | 6237.00
21 | 64-QAM | 13/16 | 6 | 2016 | 1638 | 6756.75
Info bits per OFDM symbol
coded bits per OFDM symbol
coded bits per subcarrrier

## Slide 8: OFDM Parameters
Parameter | Notation | Value
FFT Size | NFFT | 512
Number of data subcarriers | NSD | 336
Number of pilot subcarriers | NSP | 16
OFDM sampling frequency | Fs | 2640 MHz
Subcarrier frequency spacing | ΔF | 5.16 MHz
Guard Interval/Cyclic Prefix | TGI | 128/Fs= ~48ns

## Slide 9: OFDM PPDU Format
Preamble
  Consists of STF and CEF
  Duration of ~1.09 us
Header
  carries 64 bits
    Includes 8-bit HCS and 8 reserved bits
  Fits into one OFDM symbol
    duration of ~ 242 ns
TRN-T/R Subfields (optional)
  Used for beamforming training/tracking

## Slide 10: Preamble Format
Ga128 and Gb128 are 128-length Golay complimentary sequence pairs sampled at SC chip rate Fs=1760 MHz (Tc = 1/Fs ~ 57 ns)
  Allows common pre-amble processing for OFDM and SC PHYs
Short Training Field (STF)
  15x repetition of Ga128 sequence
  Used for timing/frequency acquisition
Channel Estimation Field (CEF)
  Consists of two 512-length complementary sequence pairs (GU512 and GV512) and a cyclic post-fix (GV128)
  Channel estimation in time or frequency domain
  Can auto-detect SC/OFDM PHY (different CEF formats employed)

## Slide 11: Preamble Re-sampling Filter
OFDM preamble sequences are defined at SC chip rate (Fc) to support common SC/OFDM preamble processing
3/2-rate re-sampling is required to convert from Fc = 1760 MHz to (nominal) OFDM sampling rate (Fs = 2640 MHz)
Re-sampling filter (73 taps) is specified so that Rx can undo filter response from channel estimate

## Slide 12: Header Coding & Modulation
Header contains 64 info bits
which are heavily protected
  168 parity bits generated by ¾ rate LDPC
  Info bits and parity repeated 3x
  Info bits not punctured
  Repetition of parity bits punctured differently
  Header mapped to OFDM symbol
  8-bit check sequence included

## Slide 13: Payload Coding & Modulation
Scrambling
  Data scrambled using 7-th order m-sequence
  Scrambler initialization sequence is tx-ed in the PHY header
LDPC Encoding
  Zero padding to fit into OFDM symbols
  Parity bits generated
  Multiple code blocks are concatenated
Modulation
  SQPSK: each code block is mapped to two OFDM symbols
  QPSK: each code clock is mapped to a single OFDM symbol
  16-QAM: two code blocks are interleaved and mapped to a single OFDM symbol
  64-QAM: three code blocks are interleaved and mapped to a single OFDM symbol

## Slide 14: OFDM Tone Mapping (QPSK/SQPSK)
SQPSK
QPSK
Index P(k) is dependent on Dynamic/Static Tone Mapping
(a) when Static Tone Mapping (STP) is used P(k) = k+168
(b) when Dynamic Tone Mapping (DTP) is used P(k) is derived from feedback

## Slide 15: OFDM Tone Mapping (16-QAM/64-QAM)
For 16-QAM and 64-QAM, 2 and 3 code blocks are interleaved on a subcarrier basis, respectively.
Only for 64-QAM

## Slide 16: Dynamic Tone Pairing for SQPSK and QPSK
First (NSD/2=168) half of data tones are sliced to NG (21 or 42 ) groups
  Each group consists of NTPG tones
Second half of data tones are slices to NG groups
Rx determines and feeds back pairings of groups
  l-th group of first half paired to GroupPairIndex(l)-th group of second half
Tx/Rx use fixed mapping of tone-pairs used within pairs of groups

## Slide 17: Conclusions
OFDM PHY Mode has been proposed
  Part of complete proposal in 802.11-10/432r0 (slides) and 802.11-10/433r0
Main characteristics
  Significant commonality with SC Mode Proposal
    See IEEE 802.11-10-0429-00-00ad-NT-8
  Optimized for NLOS environment
  Provides up to 7 Gbps data rate
Performance evaluation as per EVM document
  Presented in IEEE 802.11-10-0431-00-00ad-CP-PHY