## Slide 1
[Intra cluster response model and parameter for the enterprise cubicle environments at 60GHz (Part2)]
Date: 2010-4-29
Authors:

## Slide 2: Abstract
This paper shows reflection wave characteristics by ceiling for the enterprise cubicle environment channel modeling
For near location
Intra cluster channel model is developed “including reflection wave by metal frame” for the simulation of worst case.
The other case, the channel model may not be required.
For far location
High resolution measurement have clarified that kb and gb are reasonably low compared with the previous report
This lead to unnecessity channel model (direct path only)

## Slide 3: Floor plan of cubicle environments
Desk
160×70
STA
AP height:2.5m
STA height:0.7m
from floor
Impulse responses are measured at the left, center, right positions on desktop
STA
Near location
Far location

## Slide 4: Direct and reflection wave paths in cubicle environments
Far location
Near location
Multiple-time-reflected waves on desktop was observed
Reflection wave characteristics from ceiling should be clarified for channel modeling
Direct wave
Reflection wave
Tx

## Slide 5
Measurement for reflected wave by ceiling
for the cubicle environment (near location)
Reflection wave
Tx
Rx
1m
3m
The reflected waves by ceiling are measured at each grid point (separated by 1m) in the room (Total measured points are 20).
Measurement system
Measurement points
in the room
1m
1m

## Slide 6: Measurement set up of reflection wave by ceiling
Parameter | Value
Center frequency | 62.5 GHz
Band width | 3 GHz
Number of frequency points | 801
Frequency step | 3.75 MHz
Antenna type | Conical horn
HPBW of antenna | 30degree
Polarization | Vertical
Calibration | Direct port connection without antennas

## Slide 7: Measured impulse response examples
Reflected waves by metal frame, pipe and concrete wall were observed in measured impulse responses
Reflected wave power varies up to 15dB depending on the position
15dB
Metal frame reflection
Pipe reflection
Concrete wall reflection

## Slide 8: Cause of reflected wave power variation
Behind the ceiling
Metal frame
Concrete
Shielded pipe
Cable
The behind the ceiling are metal frames, pipes , and concrete wall
Metal frames cause strongest reflection waves
Incident wave
Plaster board
Concrete wall
Metal frame
60cm
Detail of two reflected waves
Pipe
30cm

## Slide 9: Plaster board penetration loss measurement
Tx
Rx
Snap shot of penetration loss measurement
Penetration loss
Penetration loss is about 0.7～2dB
Plaster board does not reflect strongly

## Slide 10: Reflected wave power
Power difference are about average 12dB in each position
Reflected wave power in cubicle environment depends heavily on the position
12dB down in average

## Slide 11: Impulse responses of AP-STA (AP antenna HPBW:90deg, C pol., STA antenna HPBW:30deg, V pol.)
The strong reflection wave by metal frame is included.
If there is no metal frame, reflection wave power is very small
Near location scenario
Direct waves
Reflection waves
18dB
12dB
No metal
frame

## Slide 12: Consideration of the channel model for the cubicle environment (near location)
There are two situations for reflected waves by ceiling.
Intra cluster channel model including reflection wave by metal frame is required for the simulation of worst case (See slide 13).
On the other hand, reflection wave is very small (30dB lower than direct wave) when there is no metal frame in the ceiling. In this case, channel model may not be required.

## Slide 13: Intra-cluster parameters for cubicle environments (near location)
Environments Far location |  | kf [dB] | kb [dB] | gf [ns-1] | gb [ns-1] | lf [ns-1] | lb [ns-1] | Distribution, for forward | Distribution for backward
Cubicle AP-STA | For worst case※ | 7.2 | 12 | 0.46 | 1.8 | 0.47 | 0.88 | Rayleigh | Rayleigh
 | Previous estimation Doc.10/372r0 | N/A | 24.5 | N/A | 0.690 | N/A | 1.13 | N/A | Rayleigh
t = 0
Time of arrival
kb
kf
Central ray of intra-cluster
Arrival rate, lb
Arrival rate, lf
Ray decay factor, gb
Ray decay factor, gf
Rayleigh distribution
Rayleigh distribution
Tx antenna (AP)
HPBW: 90deg
C pol.
Rx antenna (STA)
HPBW: 30deg
V pol.
※The parameters are extracted from reflected waves by ceiling

## Slide 14: High resolution measurements for cubicle environment (far location)

## Slide 15: High resolution measurements for cubicle environment (far location)
160cm
70cm
20cm
50cm
15cm
10cm
Measured points (Total: 26)
Small number of measurement makes a specific intra-cluster channel model, since multi-reflection waves depends heavily on the position
Measurement points were added at 10cm step×2 lines on desktop
The channel model parameter are re-extracted
Additional measured points on desktop

## Slide 16: Measurement system for cubicle environments (far location)
Instrument: Vector network analyzer
Network
Analyzer
Tx antenna is near the ceiling(AP)
Rx antenna is on the desktop(STA)

## Slide 17: Measurement set up for high resolution TGad defined enterprise cubicle environment (Far location)
Parameter | Value
Center frequency | 62.5 GHz
Band width | 3 GHz
Number of frequency points | 801
Frequency step | 3.75 MHz
Antenna type | Conical horn
HPBW of antenna | 30degree(STA), 90 degree(AP)
Polarization | Vertical(STA), Circular(AP)
Calibration | Direct port connection without antennas

## Slide 18: High resolution measurement for cubicle environment (far location)
Total number of measured response is 26
Reflection waves
Direct waves
23.4dB
kb=7.4dB
30.8dB
Direct path and single ray may be enough as the channel model for cubicle environment (far location)

## Slide 19: Revised intra-cluster parameters for cubicle environments
Environments Far location |  | kf [dB] | kb [dB] | gf [ns-1] | gb [ns-1] | lf [ns-1] | lb [ns-1] | Distribution, for forward | Distribution for backward
Cubicle AP-STA | High resolution | 5.1 | 7.4 | 3.1 | 6.0 | 0.55 | 0.53 | Rayleigh | Rayleigh
 | Previous Estimation Doc.10/372r0 | N/A | 22.5 | N/A | 14 | N/A | 0.81 | N/A | Rayleigh
t = 0
Time of arrival
kb
kf
Central ray of intra-cluster
Arrival rate, lb
Arrival rate, lf
Ray decay factor, gb
Ray decay factor, gf
Rayleigh distribution
Rayleigh distribution
Tx antenna (AP)
HPBW: 90deg
C pol.
Rx antenna (STA)
HPBW: 30deg
V pol.
kb and gb are reasonably low compared with the previous report

## Slide 20: Conclusion
For near location
Intra cluster channel model is developed “including reflection wave by metal frame” for the simulation of worst case.
The other case, the channel model may not be required.
For far location
High resolution measurement have clarified that kb and gb are reasonably low compared with the previous report
This lead to unnecessity channel model (direct path only)