IEEE P802.11
Wireless LANs

| TGs PAR Extension |
| --- |
| Date: 2010-05-20 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Dee Denteneer | Philips | HTC 37 5656AE Eindhoven The Netherlands | +31-40-2749743 | Dee.Denteneer@philips.com |

Project Authorization Request (PAR) Process

Extension Request for P802.11s, Approved on

2007-08-22(230283956.309)

Submitter Email: stuart@ok-brit.com

PAR Expiration Date: 2008-12-31

Number of Previous Extensions Requested: 1

Last Extension Approval Date:

2008-09-25

Number of Years being requested: 2

Sponsor: IEEE Computer Society/Local and Metropolitan Area Networks(C/LM)

Chair: Paul Nikolich

18 Bishops Lane

Lynnfield, MA 01940

US

Email: p.nikolich@ieee.org

Working Group: Wireless LAN Working Group(C/LM/WG802.11)

Chair: Bruce Kraemer
517 La Costa Court 
Melbourne, FL 32940
US

bkraemer@marvell.com

Title: Standard for Information Technology - Telecommunications and

information exchange between systems - Local and metropolitan area

networks - Specific requirements - Part 11: Wireless LAN Medium Access

Control (MAC) and Physical Layer (PHY) specifications Amendment: Mesh

Networking

Scope: This amendment describes an IEEE 802.11 Mesh network with an IEEE

802.11 Wireless Distribution System (WDS) using the IEEE 802.11 MAC/PHY

layers that supports both broadcast/multicast and unicast delivery over

self-configuring multi-hop topologies.

Purpose: The IEEE 802.11 standard provides a four-address frame format for

exchanging data packets between stations for the purpose of creating a

Wireless Distribution System (WDS), but does not define how to configure

or use a WDS. The purpose of this amendment is to provide a protocol for

auto-configuring paths between stations over self-configuring multi-hop

topologies in a WDS to support both broadcast/multicast and unicast

traffic in a Mesh using the four-address frame format or an extension.

Do the title, scope and purpose match that of the current draft? Yes

Why is an extension required? Mesh is a complex enhancement to 802.11.

802.11s has made enormous progress. Draft 3.0 was accepted with 76% approval rate. During the third recirculation, the current Draft 5.0 has received 89%. A detailed timeline is available for the completion of 802.11s, scheduling the first sponsor ballot for October 2010 and final NesCom approval for June 2011.

Document Development Information:

a. What date did you begin writing the first draft? 2006-01-31

b. How many people are actively working on the project? 20

c. How many times a year does the working group meet:

1. In person? 6

2. Via teleconference? 12

d. How many times a year is a draft circulated to the working group via

electronic means? 6

e. What percentage of the Draft is stable? 95%

f. How many significant work revisions has the Draft been through? 34

Project Plan:

When will IEEE sponsor balloting begin? 2010-10-11

When do you estimate that the final IEEE Sponsor ballot will be

completed? 2011-03-16

When do you expect to submit the proposed standard to RevCom? 2011-05-01

Adoption:

Will this document be adopted by another source? No

Explanation:

# Comments

See timelines page on website

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Abstract

2 year PAR Extension for P802.11s.