IEEE P802.11
Wireless LANs

| Location for DEI bit |
| --- |
| Date: 2010-05-18 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Alex Ashley | NDS Ltd | One London Road, Staines, Middlesex, TW18 4EX, UK | +44-1784-848770 | aashley@nds.com |
| Hang Liu | Technicolor Inc. | 2 Independence Way, Princeton NJ 08540 | 609-987-7335 | Hang.Liu@technicolor.com |

7.1.3.5 QoS Control field

Modify 7.1.3.5 as shown

EDITORIAL NOTE— The exact format of the information in the AVT field is to be defined and will be updated as the 11aa signaling requirements become clearer. The intention is to remove the AVT field by placing its subfields in existing MAC fields.

|  | B0 | B1 – B7 |
| --- | --- | --- |
|  | DEI | Reserved |
| Bits: | 1 | 6 |
| Figure 7-aa17 —AVT field |

7.1.3.5a HT Control field

Replace Figure 7-4a with the figure below:

EDITORIAL NOTE— This figure replaces reserved bit 29 with a DEI bit field.

References:

# Text boxes

Figure 7-4a—HT Control field

Abstract

Draft 0.05 of P802.11aa has a place holder “AVT Field” for information required by 11aa to be added to the MAC header.

This proposal replaces this place holder with use of a reserved bit in HT control field.

2

B25  B28

B20  B21

1

B24

1

2

2

2

16

Bits:

B22  B23

B16

1

B0  B15

Reserved

CSI / Steering

Reserved

Calibration Sequence

Calibration Position

Link

Adaptation

Control

NDP Announce-ment

DEI

AC Constraint

RDG/

More PPDU

B31

B30

B29

B17

B19

B18

4

1