IEEE P802.11
Wireless LANs

| TGae Teleconference Minutes Jun-Jul 2010 |
| --- |
| Date: 2009-07-08 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Michael Montemurro | Research In Motion | 4701 Tahoe Blvd. Mississauga, ON. L4W 0B4 | 905-629-4746 Ext. 4999 | mmontemurro@rim.com |

Thursday June 3, 2010

11:00am

### Attendees:

Michael Montemurro,

Santosh Pandey,

Roger Durand,

Mark Hamilton,

Henry Ptasinski,

Matt Fischer.

Call to order

Review of IEEE Intellectual Property Policy

No essential patents.

Review of TGae status:

  - Document 11-10/574r0 was accepted as D0.01 of TGae.

  - Action: Roger. Produce a submission which changes the default classification based on management frame types.

  - The policy that a TGae capable STA uses to transmit frame to a legacy STA needs to respect legacy behavior.

  - Action: Matt Fischer. Produce a submission which defines the normative changes to frame formats to TGae.

  - Matt will make an announcement to the reflector.

Adjourn until the call on July 8.

Thursday July 8, 2010

11:00am

### Attendees:

Michael Montemurro,

Santosh Pandey,

Roger Durand,

Mark Hamilton,

Henry Ptasinski.

Call to order

Review of IEEE Intellectual Property Policy

No essential patents.

Discussion on TGae Frame Format

  - Presentation of document 11-10/745r0 on MAC Sequence Numbering

    - The proposal uses another sequence number space for management frames separate from data frames.

    - Effectively, using the sequence control field sets sequence number ranges for each AC.

    - We need to discuss the MCAST behaviour.

    - The proposal has two elements: the treatment of unicast management frames and group-addressed management frames.

    - Legacy STA’s follow the “old rules”. One sequence number space and transmission at AC_VO.

    - When the policy changes while the STA is in PS-mode. With the AC signalling in the sequence number field, we resolve an issue with a dynamic change in management frame prioritization policy.

    - This proposal does not change the header so hardware implementation.

    - We need to look at the security impact of this proposal.

    - We may need to map the AC signalling in the Nonce construction for management frames.

    - We need to consider what happens with security when the management frame policy changes.

    - We need to address what happens when a policy transition occurs.

    - The management policy change should be successfully updated to all clients before transmission rules change.

    - There is a potential for a frame policy change to reorder the transmission of management frames at a STA.

    - Need to understand whether the lower-order or higher-order bits for signalling AC in the sequence number space.

Prepare for July Plenary meeting.

  - Call for editor

  - Discuss document 11-10/745r0 as a proposal.

  - Discuss the issue on how we deal with policy updates and management frame queuing.

  - Discuss default classification for management frame prioritization.

Adjourn until the plenary meeting on July 12.