## Slide 1: CSI Feedback Scheme using DCT for Explicit Beamforming
Slide 1
Date: 2010-7-
Authors:

## Slide 2: Introduction
Downlink (DL) MU-MIMO will be adopted to improve the spectrum efficiency in TGac.
We have shown that the difference in CSI report requirements between 11n and TGac in explicit feedback [1].
  Number of transmission parameters (Numbers of Tx/Rx antennas, STAs and subcarriers) increases in TGac.
  MU-MIMO requires more accurate CSI than SU-MIMO.
Reducing CSI feedback (FB) duration is needed to achieve higher MAC efficiency for MU-MIMO.
Furthermore, for throughput performance improvement in OBSS environment, CSI-FB duration is lengthened to apply several interference management schemes [2].
In [3], time-domain explicit feedback scheme was proposed to reduce the amount of CSI needed.
In this submission, we present a CSI-FB scheme in time-domain by using discrete cosine transform (DCT).

## Slide 3: Concept of CSI-FB scheme in time-domain
In frequency-domain (FD), CSI between a Tx antenna and a Rx antenna consists of Ns subcarrier components.
In contrast, assuming that the actual channel impulse response is present only the GI duration, CSI in time-domain (TD) consists of only Ng components.
Less CSI-FB needed with TD than with FD: factor is Ng/Ns.
Time-domain
conversion
freq.
NS
time
Ng
Power
Power
July 2010

## Slide 4: CSI-FB flow in time-domain for explicit beamforming
AP
STA
Transmit a sounding frame
Receive the sounding frame
Time
Estimate CSI in FD
Convert FD-CSI into TD-CSI
Receive the L components of TD-CSI
Transmit only the L components of Ns TD-CSI components
Convert TD-CSI into FD-CSI
Some extra calculations for TD conversion can reduce FB information from STA to AP.
July 2010

## Slide 5: Conversion schemes from FD-CSI into TD-CSI
Power
Freq.
Channel gain
Freq.
Freq.
Discontinuity
Inverse discrete Fourier transform (IDFT)
Discrete cosine transform (DCT)
Power
Time
DCT
IDFT
IDFT and DCT can create time-domain components.
In IDFT, the discontinuity at the band edges results in a spreading of energy in the impulse response since DFT assumes that the frequency response is periodic, which causes large CSI error.
DCT can reduce the high-frequency components compared to DFT since it assumes mirror extension of the original data.
Continuity
Ng
July 2010
DCT is suitable for time-domain conversion.

## Slide 6: CSI encoding procedure at each STA
The channel impulse response estimate is obtained by applying Ns-point DCT to each group of upper and lower consecutive FD-CSI estimates since there are no CSI components around DC.
The scaling ratio is calculated and quantized to 3 bits as FB encoding scheme in 11n; only the first L components are used.
The real and imaginary parts of each component in the L components of the impulse response are quantized to Nb bits.
Subcarrier k
Ns-point DCT
DC
Ns-point DCT
l: sample index, k: subcarrier index, n: Rx antenna index, m: Tx antenna index
July 2010

## Slide 7: CSI decoding procedure at AP
The real and imaginary parts of each impulse response component are decoded to create the complex component.
Each component is then scaled using the values in the amplitude field as in 11n.
FD-CSI of upper/lower group is obtained by applying Ns-point IDCT to the impulse response.
July 2010

## Slide 8: Performance comparison
July 2010
Simulation parameters
Channel model | Model E
Bandwidth | 80MHz
Number of subcarriers (Nsc) | 228
Number of antennas at AP (NT) | 8
Number of antennas at STA (NR) | 1
Number of TD-CSI components (L) | 64
Number of DCT-point (Ns) | 114
Nb=8bit
7bit
6bit
5bit
4bit
TD-CSI-FB
FD-CSI-FB (11n)
When the required MSE is -30dB for CDF=95%, TD-CSI-FB and FD-CSI-FB require 7 and 6bits, respectively to quantize each real/imaginary part of the CSI components.
TD-CSI-FB significantly reduces, by 34.8%, CSI-FB information compared to FD-CSI-FB even though TD-CSI uses more bits in quantization.
FB information bits
TD-CSI-FB | (3+2xNbxNTxNR)x2L
FD-CSI-FB | (3+2xNbxNTxNR)xNsc

## Slide 9: Simple example of CSI-FB in DL-MU-MIMO
July 2010
AP
Sounding
CSI report #1
Header
STA#1
SIFS
CTS
DL-MU-MIMO data
Simulation parameters
CSI-FB duration: 0.77ms@TD-CSI-FB, 1.04ms@FD-CSI-FB
In this scenario, FB duration with TD-CSI-FB scheme can reduce FB duration by 26.2% compared to conventional FD-CSI-FB scheme.
CSI report #2
Header
STA#2
CSI report #4
Header
STA#4
SIFS
SIFS
SIFS
Bandwidth | 80MHz
Number of subcarriers (Nsc) | 228
Number of antennas at AP | 8
Number of antennas at STA | 1
Number of STAs | 4
Data modulation at STA | 16QAM
Coding rate | 1/2

## Slide 10: Conclusion
We presented CSI-FB scheme using DCT to reduce the amount of FB information.
TD approach can reduce FB information since the number of channel impulse response components fits within GI period.
DCT is suitable for converting FD-CSI into TD-CSI since DCT can better reduce the high-frequency components compared to DFT.
TD-CSI-FB with DCT can significantly reduce FB information compared to FD-CSI-FB without MSE degradation.
July 2010

## Slide 11
July 2010
References
[1] K. Ishihara et al., CSI Report for Explicit Feedback Beamforming in Downlink MU-MIMO, IEEE 802.11-10/0332r0, Mar. 2010.
[2] Y. Asai et al., Interference Management Using Beamforming Technique in OBSS Environment, IEEE 802.11-10/0585r4, May 2010.
[3] L. Cariou and M. Diallo, Time Domain CSI report for explicit feedback, IEEE 802.11-10/0586r1, May 2010.