## Slide 1: PHY Abstraction for MU-MIMO
Date: 2010-07-11
Authors:
Name | Affiliations | Address | Phone | email
Riichi Kudo | NTT Corporation | Hikarino-oka Yokosuka-shi Japan | +81-46-859- 3140 | kudo.riichi@lab.ntt.co.jp
Yusuke Asai |  |  | +81-46-859-3578 | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  | +81-46-859- 4233 | ishihara.koichi@lab.ntt.co.jp
Masato Mizoguchi |  |  | +81-46-859- 3758 | mizoguchi.masato@lab.ntt.co.jp

## Slide 2: Introduction
Two approved strawpolls in TGac suggest to add PHY abstraction model to the FR-EM document [1]
  Do you think PHY abstraction method for MU-MIMO is needed?
  Do you agree to include PHY abstraction methods as a recommendation in FR&EM document?
Show problems of PHY abstraction for MU-MIMO
Present PHY abstraction method using a look-up-table

## Slide 3: Overview of PHY / MAC simulation
PER
Calculation
Channel Generation
Channel Data Set
PER Data Set
MAC
Simulation
MAC/SAP
throughput
One possible example of PHY/MAC simulation
Major problems of PHY abstraction for MU-MIMO
  Large computational load imposed by PER calculation
  How to reflect performance dependence of user combinations
  How to consider performance degradation caused by aged CSI
Channel model
Precoding scheme
MAC Protocol
This presentation focuses on

## Slide 4: PHY abstraction in TGn
Look up table (LUT) for PER reduces calculation complexity.
In [2] and [3] for IEEE 802.11 TGn, the relationships between PER and average SNR are shown for various MIMO configurations and MCS indices.
We calculated the relationship between PER and average SNR in MU-MIMO.

## Slide 5: PER versus average SNR
PER versus post processing SNR is shown for MU-MIMO.
PER inaccuracy is very large at certain SNR value.
Number of channel conditions for multiple users is also large.
PER of 500-byte packets in 2 Tx  1 Rx  2 user 40MHz, ZF precoding, Ch.C, and NLOS.
PER of 500-byte packets in 4 Tx  2 Rx  2 user
40MHz, ZF precoding, Ch.C, and NLOS.
64QAM
3/4 BCC
16QAM
3/4 BCC

## Slide 6: PHY Abstraction for MU-MIMO
We present a look up table for PER calculation block
Calculate post-processing SNR in all subcarriers
Calculate post-processing SNR
in all subcarriers
Calculate Average SNRs for all subcarriers
Calculate PER using LUT of PER versus average SNR
Calculate BER for each subcarrier with error function
Calculate PER using LUT of PER versus BER
  PHY abstraction using LUT holding PER and average SNR
  Proposed PHY abstraction using LUT holding PER and BER
PER
PER
Channel
Channel
i,j
i,j: SNR of j-th data stream at i-th subcarrier
 : Average SNR P: Calculated BER using error function
i,j

P

## Slide 7: PER versus Calculated BER in Proposed PHY Abstraction
PER versus uncoded BER shown.
Variance of PER for estimated BER is smaller than that for SNR
PER of 500-byte packets in 2Tx1Rx2user
40MHz, ZF precoding, Ch.C, and NLOS.
PER of 500-byte packets in 4Tx2Rx2user
40MHz, ZF precoding, Ch.C, and NLOS.
64QAM
3/4 BCC
16QAM
3/4 BCC

## Slide 8: Calculation Complexity
The required time for PER calculations is shown.
  PHY abstraction
  using average SNR
  Proposed PHY abstraction
  using uncoded BER
  Direct calculation of PER
Bit amount: 2.16108 , Coding rate: 3/4, Mod.: QPSK
556 sec
3.5 sec
3.6 sec
System: Microsoft Windows XP, Intel(R) Xeon(R) CPU X5472 @ 3.00GHz 2.99GHz

## Slide 9: Conclusion
Showed accuracy of PER estimation using average SNR and uncoded BER.
Proposed PHY abstraction on the basis of uncoded BER; has higher accuracy than that possible with average SNR.
Computational load of proposed PHY abstraction much lower than that of direct calculation.

## Slide 10
References
[1] 11-10/0334r0 PHY Abstraction for MU-MIMO in TGac
[2] 11-04/0895r6 TGn Sync TGn Proposal MAC Simulation Methodology
[3] 11-04/0877r9 WWiSE Proposal Response to Functional Requirements and Comparison Criteria

## Slide 11: Straw poll
Do you agree to add the following sentences in section 3 of FREM document to allow TGac proposal to use PHY abstraction?
“Each TGac porposal may use a PHY abstraction method. If a PHY abstraction method is used, the method must be described and disclosed.”
  Yes/ No / Abstain