## Slide 1: Stream Partition Index for MU-MIMO Transmissions
Date: 2010-07-12
Authors:

## Slide 2: Problem Definition
MU-MIMO transmission using spatial streams
  Need to communicate stream assignment in VHT-SIG-A
  Bit allocation has to be compact
  Minimize/Eliminate management frames overhead in defining any parameters required
    Fast adaptation to changes in channel conditions or user bandwidth requirements
    Per-packet assignment flexibility

## Slide 3: Partitions of Number of streams
NSTS or NSS | Distribution of streams across multiple STAs | Num cases
1 | (1) | 1
2 | (2)(1,1) | 2
3 | (3)(2,1)(1,1,1) | 3
4 | (4)(3,1)(2,2)(2,1,1)(1,1,1,1) | 5
5 | (5)(4,1)(3,2)(3,1,1)(2,2,1)(2,1,1,1)(1,1,1,1,1) | 6
6 | (6)(5,1)(4,2)(4,1,1)(3,3)(3,2,1)(3,1,1,1)(2,2,2)(2,2,1,1)(2,1,1,1,1)(1,1,1,1,1,1) | 8
7 | (7)(6,1)(5,2)(5,1,1)(4,3)(4,2,1)(4,1,1,1)(3,3,1)(3,2,2)(3,2,1,1)(3,1,1,1,1) (2,2,2,1)(2,2,1,1,1)(2,1,1,1,1,1)(1,1,1,1,1,1,1) | 8
8 | (8)(7,1)(6,2)(6,1,1)(5,3)(5,2,1)(5,1,1,1)(4,4)(4,3,1)(4,2,2)(4,2,1,1)(4,1,1,1,1) (3,3,2)(3,3,1,1)(3,2,2,1)(3,2,1,1,1)(3,1,1,1,1,1)(2,2,2,2)(2,2,2,1,1) (2,2,1,1,1,1)(2,1,1,1,1,1,1)(1,1,1,1,1,1,1,1) | 9
With not more than 4 streams per STA in multi-user case and not more than 4 STAs in a group
42 cases  6 bit “Partition Index” field
With NSTA known, we need 4 bits (1-STA: 8, 2-STA: 10, 3-STA: 13, 4-STA: 11 cases)

## Slide 4: Partitions of NSTS (or NSS) for fixed NSTA
NSTA | Distribution of streams across multiple STAs | Num cases
1 | (1)(2)(3)(4)(5)(6)(7)(8) | 8
2 | (1,1)(2,1)(3,1)(2,2)(4,1)(3,2)(4,2)(3,3)(4,3)(4,4) | 10
3 | (1,1,1)(2,1,1)(3,1,1)(2,2,1)(4,1,1)(3,2,1)(2,2,2)(4,2,1)(3,3,1)(3,2,2)(4,3,1)(4,2,2) (3,3,2) | 13
4 | (1,1,1,1)(2,1,1,1)(3,1,1,1)(2,2,1,1)(4,1,1,1)(3,2,1,1)(2,2,2,1)(4,2,1,1)(3,3,1,1) (3,2,2,1)(2,2,2,2) | 11
With not more than 4 streams per STA in multi-user case and not more than 4 STAs in a group
With NSTA known, we need 4 bits (1-STA: 8, 2-STA: 10, 3-STA: 13, 4-STA: 11 cases)

## Slide 5: STA_PHY_ID
Need STA PHY identifiers to go with partition index
  5 bit STA_PHY_ID assigned by AP
    0 is not assigned, assumed invalid – useful in providing NSTA count
    Supports 31 STAs which are capable of decoding multi-user packets
    Reassign IDs if necessary
    May use AID by allocating 1-31 for STA with multi-user receive capability
  8 bits possible if we extend VHT-SIGA to 3 OFDM symbols
    Support 255 multi-user receive capable STAs
    Reduces reuse associated overhead

## Slide 6: VHT-SIG-A : option 1 – Multi-user case
Field | Number of bits | Explanation and coding
Multi-user packet | 1 : set to 1 | 0: Single user packet, 1: Multi-user packet
STA_PHY_IDs | 5x4 | Indicate which STAs are assigned the streams in the correct order
Partition Index – NSTS | 4 | Indicate number of space-time streams and the assignment of streams to each of the STAs listed in STA_PHY_IDs NSTA is derived by counting valid STA_PHY_IDs
Partition Index – NSS | 4 | Indicate number of spatial streams and a valid partition to identify which streams are STBC encoded (needs to be valid for a given partition of NSTS: NSS,k ≤ NSTS,k) Alternatively, we can allocate 1 bit for each STA, but it limits STBC to just two options
CBW | 2 | Channel bandwidth 00-11 -> 20/40/80/160 MHz
 | 3 | TBD
CRC | 8 | 
Tail bits | 6 | 
Total up to 48 bits -> 2 OFDM symbols at 6Mbps
When Multi-user bit set to 0, we can merge VHT-SIG-B into VHT-SIG-A and eliminate VHT-SIG-B
With 3 OFDM symbols we can accommodate 8 bit STA_PHY_IDs which can reduce overhead in reassigning STA_PHY_IDs

## Slide 7: VHT-SIG-A : option 1 – Single-user case
Field | Number of bits | Explanation and coding
Multi-user packet | 1 : set to 0 | 0: Single user packet, 1: Multi-user packet
MCS | x | 
Length | 16 | 
NSTS | 3 | 
STBC | x | 
CBW | 2 | Channel bandwidth 00-11 -> 20/40/80/160 MHz
 | x | TBD
CRC | 8 | 
Tail bits | 6 | 
VHT-SIG-B not required in this case

## Slide 8: VHT-SIG-A : option 2
Field | Number of bits | Explanation and coding
GroupID | 6 | Indicate which STAs are assigned the streams (GroupID defines a set containing up to 4 STA IDs, not necessarily ordered)
Permutation Index | 5 | 24 permutations possible with 4 STAs
Partition Index for NSTS | 4 | Indicate number of space-time streams and the assignment of streams to the STAs defined by GroupID
Partition Index for NSS | 4 | Indicate number of spatial streams and a partition to identify which streams are STBC encoded (needs to be valid for a given partition of NSTS: NSS,k ≤ NSTS,k )
CBW | 2 | Channel bandwidth 00-11 -> 20/40/80/160 MHz
 | 5 | TBD
CRC | 8 | 
Tail bits | 6 | 
High Management Frame overhead in communicating GroupID to all STAs
Ordering of STAs may be included in GroupID definition but will need more than 6bits

## Slide 9: VHT-SIG-Bn, n=1,2,…,NSTA
Field | Number of bits | Explanation and coding
MCS | 4 | 
Length | 16 | 
Aggregation | 1 | 
FEC Coding | 1 | 
 | x | TBD
CRC | 8 | 
Tail bits | 6 | 
Total up to 48 bits  2 OFDM symbols at 6Mbps
SIG-Bs for different STAs transmitted in parallel

## Slide 10: Example 1
L-STF-LTF-SIG
20μs
NSTA = 2 with 4 RX antennas each
8 TX antennas
AP decides to transmit 4 streams, 2 each to the two STAs
No STBC
Partition Index NSTS = 3  (2,2)
Partition Index NSS = 3  (2,2)
VHT-SIG-A
8μs
VHT-STF
4μs
VHT-SIG-B1
8μs
VHT-LTF1 4μs
Expanded to NTX streams as in 11n
NSTA ≤ NSS ≤ NSTS ≤ NTX
VHT-SIG-B2
8μs
DATA
DATA
VHT-LTF2
4μs
VHT-LTF3
4μs
VHT-LTF4
4μs
DATA
DATA
4 LTFs for 4 streams
VHT-SIG-A [0:28] = [ 1 10000 01000 00000 00000 1100 1100 ]

## Slide 11: Example 2
NSTA = 2 with 4 RX antennas each
8 TX antennas
AP decides to transmit 4 streams, 2 each to the two STAs
STBC for both STAs
Partition Index NSTS = 3  (2,2)
Partition Index NSS = 0  (1,1)
L-STF-LTF-SIG
20μs
VHT-SIG-A
8μs
VHT-STF
4μs
VHT-SIG-B1
8μs
VHT-LTF1 4μs
Expanded to NTX streams as in 11n
NSTA ≤ NSS ≤ NSTS ≤ NTX
VHT-SIG-B2
8μs
DATA
VHT-LTF2
4μs
VHT-LTF3
4μs
VHT-LTF4
4μs
DATA
4 LTFs for 4 streams
VHT-SIG-A [0:28] = [ 1 10000 01000 00000 00000 1100 0000 ]

## Slide 12: Discussion
Advantages
  Per packet stream distribution possible resulting in fast adaptation to channel variations
  Parallel Per-STA length and MCS signaling in VHT-SIG-Bs reduces some overhead
  Per packet station selection possible with STA_PHY_IDs included in VHT-SIG-A
    Reduces management frame overhead in assigning GroupID
  Power saving by switching off receiver if STA_PHY_ID doesn’t match

## Slide 13: References
IEEE Std 802.11n-2009
09/0992r10, TGac Spec framework
10/0073r1, GroupID Concept for Downlink MU-MIMO Transmission

## Slide 14: Straw Poll on Partition Index – NSTS
Do you support allocating 4 bits for Partition index – NSTS in VHT-SIG-A of Multi-user frames and editing the spec. framework document 802.11-09/992 accordingly?
  Yes:
  No:
  Abs:
  It ____ to move to task group motion

## Slide 15: Straw Poll on Partition Index – NSS
Do you support allocating 4 bits for Partition index – NSS to indicate STBC encoding in VHT-SIG-A of Multi-user frames and editing the spec. framework document 802.11-09/992 accordingly?
  Yes:
  No:
  Abs:
  It ____ to move to task group motion

## Slide 16: Straw Poll on Multi-user packet indicator bit in VHT-SIG-A
Do you support allocating 1 bit in VHT-SIG-A to indicate whether the packet is of Multi-user type and editing the spec. framework document 802.11-09/992 accordingly?
  Yes:
  No:
  Abs:
  It ____ to move to task group motion