## Slide 1: DL MU-MIMO performance with QoS traffic and OBSS

## Slide 2: Introduction
TGac is adopting Multi-User-MIMO as a key technology
MU-MIMO is a spectral efficient technique which allows for higher aggregate throughput with use of limited bandwidth
In this presentation, we will show that for the same BW and in the presence of OBSS, MU-MIMO enables more high rate QoS flows compared to SU.
  MU-MIMO thereby enables dense home entertainment video distribution scenarios.

## Slide 3: Simulation Scenario
Scenario is based on the home entertainment FR-EM scenario 4, with OBSSs as described in 10/0451r14, with focus on video streams distribution only.
  One 11ac BSS, interfering with 2 OBSS (a 11ac BSS and a 11n BSS)
    11ac BSS-A: 8 antennas AP, 2 antennas STAs
    OBSS 11ac BSS-B: 8 antennas AP, 2 antennas STAs
    OBSS 11n BSS-C: 4 antennas AP, 2 antennas STAs
  Consider only high rate video streams (Blu-ray and HD) as shown in the next slide.
  Note that path losses are such that no devices are hidden from each other.
Assume 40 MHz bandwidth.
We will show that with MU-MIMO, BSS-A can support 4 QoS flows, guaranteeing the latency requirement, in the presence of OBSS
  However, BSS-A with SU protocol cannot support these flows.

## Slide 4: BSSs and traffic specifications
Flow No. | STAs (Source/Sink) | Source Location (meters) | Sink Location (meters) | Channel Model | Application (Forward Traffice / Backward Traffic) | Application Load (Mbps) (Forward / Backward) | Rate Distribution (Forward / Backward) | MSDU Size (B) (Forward / Backward) | Max. Delay (ms) (Forward / Backward) | Max. PLR (Forward / Backward)
1 | AP / STA1 | (0,0) | (0,5) | C | Blu-rayTM/ control channel | 50.00 / 0.06 | Constant, UDP / Constant UDP | 1500 / 64 | 20 / 100 | 10^-7 / 10^-2
2note | STA7 / STA2 | (7,-7) | (-10,-10) | C | HD MPEG2 / control channel | 20.00 / 0.06 | Constant UDP / Constant UDP | 1500 / 64 | 20 / 100 | 3x10^-7 / 10^-2
3 note | AP / STA3 | (0,0) | (5,0) | C | Blu-rayTM/ control channel | 50.00 / 0.06 | Constant, UDP / Constant UDP | 1500 / 64 | 20 / 100 | 10^-7 / 10^-2
4 note | STA9/STA 4 | (0,-10) | (-7,7) | C | Blu-rayTM/ control channel | 50.00 / 0.06 | Constant, UDP / Constant UDP | 1500 / 64 | 20 / 100 | 10^-7 / 10^-2
6 | AP / STA10 | (0,0) | (10,10) | C | HD MPEG2 / video console + Internet entertainment | 20.00 / 1.00 | Constant UDP / Constant UDP | 1500 / 512 | 20 / 50 | 3x10^-7 / 10^-4
Flow No. | STAs (Source/Sink) | Source Location (meters) | Sink Location (meters) | Channel Model | Application (Forward Traffice / Backward Traffic) | Application Load (Mbps) (Forward / Backward) | Rate Distribution (Forward / Backward) | MSDU Size (B) (Forward / Backward) | Max. Delay (ms) (Forward / Backward) | Max. PLR (Forward / Backward)
14 | AP B / STA15 | (xb,yb) | (xb,5+yb) | C | Blu-rayTM/ control channel | 50.00 / 0.06 | Constant, UDP / Constant UDP | 1500 / 64 | 20 / 100 | 10^-7 / 10^-2
Flow No. | STAs (Source/Sink) | Source Location (meters) | Sink Location (meters) | Channel Model | Application (Forward Traffice / Backward Traffic) | Application Load (Mbps) (Forward / Backward) | Rate Distribution (Forward / Backward) | MSDU Size (B) (Forward / Backward) | Max. Delay (ms) (Forward / Backward) | Max. PLR (Forward / Backward)
16 | AP C / STA18 | (xc,yc) | (xc,5+yc) | C | HD-MPEG2 / VoD control channel | 20/0.06 | Constant UDP / Constant UDP | 1500/64 | 20/100 | 3x10^-7 / 10^-2
BSS A
(802.11ac)
BSS B
(802.11ac)
BSS C
(802.11n)
Based on FR-EM Home Entertainment Scenarios with OBSS in 10/0451r14
Only Blu-ray and HD video flows are considered and shown in this slide
Note: BSS-A loaded up to the maximum load supported with DL-MU-MIMO; Video Flow #4 excluded because not supported

## Slide 5: Simulation Setup: DL-MU-MIMO MAC Protocol
Data (STA1)
Data (STA3)
BA
Data (STA2)
BA
BA
BAR
SIFS
RTS
CTS
SIFS
SIFS
SIFS
AP sends RTS to one of the STAs
STA replies with CTS
AP sends a MU-MIMO transmission to multiple STAs
STAs reply with BA
Additional details
  RTS, CTS and BA sent with 11a preamble
  DL-MU-MIMO data sent with 11ac preamble; A-MPDU aggregation is used
Used DL-MU-MIMO protocol as shown in 10/0324r1, slide 8

## Slide 6: Simulation Setup: CSI Feedback Protocol (for DL-MU-MIMO)
AP sends an MU-Announcement frame followed by an NDP sounding packet.
  MU-announcement requests CSI Feedback from multiple STAs
  MU-announcement reserves the NAV for uplink CSI feedback (FB) packets
STAs send CSI feedback uplink separated by SIFS, according to the instructions from MU-Announcement frame
MU-Ann.
NDP
CSI FB
CSI FB
CSI FB
STA1
AP
STA2
STA3
NAV

## Slide 7: Simulation Configuration
Simulation Software: NS2
PHY Rates computed based on post processing SINR
  AP TxPower = 24dBm; STA TxPower = 18dBm; TxEVM = -35dBc, Noise Figure = 10dB
  TGac Channel Model D NLOS.
  PHY Rates used are for 1% PER
  For SU case maximum PHY rate is supported on each link
  For MU the average aggregate PHY rate for 6SS is ~790Mbps
Aggregation
  A-MPDU aggregation for all traffic.
All traffic carried on Video Access category (AC-VI)
Scheduler at the AP
  802.11n: AP chooses each DL stream in a round robin manner.
  802.11ac: STAs are served based on queue length
CSI feedback requested every 10ms

## Slide 8: Throughput & Latency (40 MHz)
Data Throughput (Mbps)
99%ile Latency (msec)
For BSS-A
  Single User (SU) mode fails to provide enough throughput to sustain the 4 video flows.
    Higher bandwidth would be required to support the 4 video flows (80MHz)
  DL MU-MIMO allows to sustain the 4 video flows, guaranteeing low latency, in 40MHz
    Note: Further simulations showed that an additional downlink Blu-ray flow could be supported in the MU-MIMO case (flow not shown in this study as not available in FR-EM scenario)
Throughput
not met
(<50Mbps)
Mbps
Milliseconds
Unbounded delay
Throughput and delay for flows in BSS-A
Delay > 50ms

## Slide 9: Conclusions
DL MU-MIMO enables a dense home entertainment scenario, in the presence of OBSSs, in 40 MHz.
  A total of at least 4 QoS flows can be supported in BSS-A by using MU-MIMO
  Throughput and latency requirements for these QoS flows are guaranteed
  SU mode alone is not sufficient to support the offered traffic
    80MHz would be needed to support 4 QoS flows with SU transmissions
DL MU-MIMO allows to support larger amount of traffic in a given bandwidth
  Beneficial for increasing frequency reuse in an OBSS scenario.

## Slide 10: Appendix

## Slide 11
Throughput & Latency (40 MHz) Including results for BSS-B and BSS-C