## Slide 1: Replies to Q&A following 10/0788r2
Date: 2010-07-14
Authors:

## Slide 2: Abstract
This presentation provides answers to the Q&A session in the PM1 TGaa meeting on Tuesday during the July 2010 San Diego IEEE plenary

## Slide 3: Answers to Q&A (1)
Should the “question” for data frame reception be done in a separate frame?
  Yes. In making the mechanism consistent with the existing standard(s), the BAR in Block ACK essentially is a similar “question”, so the proposal should modify the MRG BAR and not modify the data frame header.
Should the “question” be asked before or after data?
  Afterwards, as it is done in 11n Block ACK and 11aa MRG
Specification of leader selection mechanism in 11aa?
  We agree to the commenter that an “out of scope of 11aa” note is required
Scalability of existing MRG-BA with the number of group members
  Although it is true that not all group members need to be addressed in the MRG BAR, once only a subset is addressed:
    this subset needs to be determined (leader-selection for several leaders)
    for the non-addressed group members, no feedback (not even implicit) is obtained

## Slide 4: Answers to Q&A (2)
Problem that the leader may roam or otherwise “leave”
  Since leader selection is out of scope, it is not a pre-requisite in the standard that the “weakest” receiver in a group has to be the leader.
  “weakest within the group” does not imply that this station has a very bad reception and will thus roam / de-associate
  When the leader leaves unexpectedly, this results in no more positive ACKs being received. Thus this makes the transmission less efficient, but not less reliable, which is considered the less significant problem
Frequency of update of the leader role
  Since the selection algorithm shall not be specified, also the frequency shall not be specified. But: The minimum granularity for probing group members for signal strength is the block size. After each block, it shall be possible to switch between MRG BA and aggregate BA
Does this assume that the leader always uses the smallest AID?
  No. The bitmap offset may start anywhere. The bitmap itself can be made a circular map or not be used at all, since only 1 station needs to be addressed

## Slide 5: Answers to Q&A (3)
Timing requirements to cancel ACK by NACK
  Requirements are less strict than for MRG BA, where NO overlap is tolerable. In this scheme, though, overlap does not matter, as measurements and simulations show
Overlay-FEC: Are protocols available?
  Yes. RTP-FEC defines an extension header / payload type to RTP, where RTP packets either carry (systematic) data or parity
Requirement for Deep Packet Inspection doing Overlay-FEC and thus increased AP complexity
  True. But it is up to the manufacturer of an AP to support this feature, since it is optional and, if implemented, can be used on demand (per-block decision) without additional protocol mechanisms

## Slide 6: Straw poll #1
Is Tgaa interested in seeing normative text for aggregate feedback cancellation incorporated as an optional feature of MRG Block ACK?
Yes:
No:
Abstain:

## Slide 7: Straw poll #2
Is Tgaa interested in seeing normative text for Overlay-FEC capability, where an AP distinguishes between (systematic) data and parity packets, in MRG Block ACK without aggregation?
Yes:
No:
Abstain:

## Slide 8: Straw poll #3
Is Tgaa interested in seeing normative text for Overlay-FEC capability , where an AP distinguishes between (systematic) data and parity packets, in MRG Block ACK with aggregation?
Yes:
No:
Abstain:

## Slide 9: References
doc.: IEEE 802.11-10/0788r2
doc.: IEEE 802.11-10/0768r2
doc.: IEEE 802.11-09/1150r2
doc.: IEEE 802.11-09/0290r1