## Slide 1: Potential performance improvements with fast initial link set-up
Date: 2010-08-04
Authors:

## Slide 2: Abstract
This presentations supports the PAR & 5C under creation by the FIA SG. It emphasizes the technical need and feasibility for a new 802.11 WG on Fast Initial Link Set-Up.
This presentation summarizes the potential performance improvements of fast initial link set-up.
The presentation only shows the final results and references corresponding presentations given more detail.

## Slide 3: Link Setup Phases
Phase | AP Discovery |  | Network Discovery | TSF Sync. (1 additional scan) | Auth. & Assoc. | Higher Layer (DHCP / IP)
 | Active | passive |  |  |  | 
Today | 102 ms | 1100 to 2300 ms | Leave as is | EAP-GPSK @ OFDM6: 6ms + 71ms processing time |  | 
Possible achievement | 2 ms | 50 ms | Leave as is | Yahalom (piggy back Upper Layer Setup) @ OFDM6: 4ms + 13ms processing time (reduced number of messages) |  | 
Gain | 98 % |  | 0 % | 78 % |  | 
Rel. document | 10/0922r1 |  | 802.11u | pending submission |  | 

## Slide 4: Link Setup Phases
[begin placing presentation body text here]
Phase | AP Discovery |  | Network Discovery | TSF Sync. (1 additional scan) | Auth. & Assoc. | Higher Layer (DHCP / IP)
 | Active | passive |  |  |  | 
Today | 102 ms | 1100 to 2300 ms | Leave as is | 17 ms |  | 
Possible achievement | 2 ms | 50 ms | Leave as is | 2 ms |  | 
Gain | 98 % |  | 0 % |  |  | 
Rel. document | 10/0922r1 |  | 802.11u | 10/0922r1 & pending submission |  | 

## Slide 5: References
10/922r1: Achievable gains in AP Discovery