IEEE P802.11
Wireless LANs

| CID 487 - Clarifications on Packet Formats |
| --- |
| Date: 2010-08-31 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Christopher Hansen | Broadcom Corporation | 190 Mathilda Place, Sunnyvale, CA 94086 USA | +1-408-543-3378 | chansen@broadcom.com |

Editor’s instructions:  replace Sections 21.3.6 and 21.3.6.1 with the following text:

### A Common Preamble

The preamble is the part of the PPDU that is used for packet detection, AGC, frequency offset estimation, synchronization, indication of modulation (SC or OFDM) and channel estimation. The format of the preamble is common to both OFDM packets and SC packets.

The preamble is composed of two parts (Figure XX): the Short Training field and the Channel Estimation field.

Figure XX – The SC preamble

#### The Short Training field

The Short Training field is composed of 16 repetitions of sequences Ga128(n) of length 128 defined in 21.9, followed by a single repetition of –Ga128(n).

The waveform for the Short Training field is:

# Where mod is the modulus operation.

Editor’s Instructions.  Replace Section 21.6.3.2.3.3 with the following text.

21.6.3.2.3.3 π/2-16 QAM Modulation

In π/2-16QAM modulation, the input bit stream is grouped into sets of 4 bits and mapped according to the following equation:

where k is the output symbol index, k =0, 1, …. Each output symbol is then rotated according to the following equation: . The constellation bit encoding is depicted on Figure 133.

Figure xxx - 16-QAM constellation bit encoding”

Increase all subsequent numbering of figures by 1.

Editor’s instructions:  replace Sections 21.4.4.1.1, 21.5.4.1.1, and 21.6.4.1.1 with the following text:

##### 21.4.4.1.1 Transmit EVM

The transmit EVM accuracy test shall be performed by instrumentation capable of converting the transmitted signal into a stream of complex samples, with sufficient accuracy in terms of I/Q arm amplitude and phase balance, dc offsets, phase noise, etc.  The instrumentation shall perform carrier lock, symbol timing recovery and amplitude adjustment while making the measurements. The instrumentation shall incorporate a rake receiver to minimize error resulting from multipath. For the CP PHY EVM, the signal is first de-spread using .  The EVM will then be calculated on the resulting symbols according to the formula below:

Where  is the number of symbols to be measured and Ns should be greater than 511, is the average power of the constellation, is the complex coordinates of the ith measured symbol, and  is the complex coordinates of the ideal constellation point for the ith measured symbol.

The test equipment should use a root-raised cosine filter with roll-off factor of 0.25 for the pulse shaping filter when conducting EVM measurement.

The transmit pulse shaping used is left to the implementer.

The EVM shall not exceed a data-rate dependent value according to Table 58.

Table 58 – EVM requirement for control PHY

| MCS Index | Description | EVM Value [dB] |
| --- | --- | --- |
| 0 | CP Modulation | -22 |

##### 21.5.4.1.1 Transmit EVM

The transmit EVM accuracy test shall be performed by instrumentation capable of converting the transmitted signal into a stream of complex samples, with sufficient accuracy in terms of I/Q arm amplitude and phase balance, dc offsets, phase noise, etc.

The sampled signal shall be processed in a manner similar to an actual receiver, according to the following steps, or an equivalent procedure:

a) 	Start of frame shall be detected.

b) 	Transition from short sequences to channel estimation sequences shall be detected, and fine timing (with one sample resolution) shall be established.

c) 	frequency offsets shall be estimated and corrected.

d)	The frame shall be de-rotated according to estimated frequency offset.

e) 	The complex channel response coefficients shall be estimated for each of the subcarriers using information contained in the preamble (STF and/or CEF)

f)	For each of the data OFDM symbols: transform the symbol into subcarrier received values, estimate the phase from the pilot subcarriers, derotate the subcarrier values according to estimated phase, and divide each subcarrier value with a complex estimated channel response coefficient.

g)	For each data-carrying subcarrier, find the closest constellation point and compute the Euclidean distance from it.

h)	Compute the RMS average of all errors in a packet. It is given by:

- Number of frames

i-frame index

k-carrier index

j-Symbol index

number of symbols

Total number of subcarriers.

I0,Q0- the ideal constellation point, for I and Q respectively.

Average power of the ideal constellation (, ) computed over the ith frame

The measurements shall occur only on the OFDM symbols, the measurement shall be performed on at least 10 frames with 16 symbols at least in each of them. Random data shall be used.

The EVM RMS error shall not exceed an MCS dependent value as found in the table below:

| MCS Index | Modulation | Coding Rate | EVM Value [dB] |
| --- | --- | --- | --- |
| 13 | SQPSK | ½ | -7 |
| 14 | SQPSK | 5/8 | -9 |
| 15 | QPSK | ½ | -10 |
| 16 | QPSK | 5/8 | -11 |
| 17 | QPSK | ¾ | -13 |
| 18 | 16QAM | ½ | -15 |
| 19 | 16QAM | 5/8 | -17 |
| 20 | 16QAM | ¾ | -19 |
| 21 | 16QAM | 13/16 | -20 |
| 22 | 64QAM | 5/8 | -24 |
| 23 | 64QAM | ¾ | -24 |
| 24 | 64QAM | 13/16 | -25 |

##### 21.6.4.1.1 Transmit EVM

The transmit EVM accuracy test shall be performed by instrumentation capable of converting the transmitted signal into a stream of complex samples, with sufficient accuracy in terms of I/Q arm amplitude and phase balance, dc offsets, phase noise, etc.   The instrumentation shall perform carrier lock, symbol timing recovery and amplitude adjustment and equalization while making the measurements.  The equalizer shall be trained using information in the SC Preamble (STF and/or CEF).   For the SC PHY EVM, measuring Ns samples at the sample rate, the measured symbols should not contain the first and the last hundred symbols of a given packet (ramp up/down) the EVM will be calculated according to the formula below:

Where Ns is the number of samples to be measured Ns should be bigger than 8000.

where is the average power of the constellation, is the complex coordinates of the i’th

measured symbols , and  is the complex coordinates of the ideal constellation point for the i’th measured symbols .

The test equipment should use a root-raised cosine filter with roll-off factor of 0.25 for the pulse shaping filter when conducting EVM measurement.

The transmit pulse shaping used is left to the implementer.

The relative constellation error (EVM) shall not exceed a MCS dependent value according to the Table below:

| MCS Indexes | Modulation | Coding Rate | EVM Value [dB] |
| --- | --- | --- | --- |
| 1 | π/2-BPSK | ½ with repetition | -6 |
| 2 | π/2-BPSK | 1/2 | -9 |
| 3 | π/2-BPSK | 5/8 | -10 |
| 4 | π/2-BPSK | 3/4 | -11 |
| 5 | π/2-BPSK | 13/16 | -12 |
| 6 | π/2-QPSK | 1/2 | -14 |
| 7 | π/2-QPSK | 5/8 | -15 |
| 8 | π/2-QPSK | 3/4 | -16 |
| 9 | π/2-QPSK | 13/16 | -17 |
| 10 | π/2-16QAM | 1/2 | -20 |
| 11 | π/2-16QAM | 5/8 | -21 |
| 12 | π/2-16QAM | 3/4 | -22 |

Editor’s instructions:  replace the text in 21.8.2.2.3 and 21.8.2.2.5 with the following text:

##### Beam Refinement AGC field

The beam refinement AGC fields are composed of 4N repetitions of the sequence [Ga64 Ga64 Ga64 Ga64 Ga64 ] when the packet is transmitted using the OFDM or SC PHY and [Gb64 Gb64 Gb64 Gb64 Gb64 ] when the packet is transmitted using the Control PHY. The sequences Ga64 and Gb64 are defined in 21.9. The sequences are transmitted using rotated π/2-BPSK modulation.

In a BRP-TX packet, the transmitter may change the TX AWV configuration at the beginning of each AGC field. Any transmit signal transients that occur due to this TX AWV configuration change shall completely settle by the end of the first Ga64 or Gb64 sub-sequence.

In a BRP-RX packet, the transmitter shall use the same TX AWV as in the preamble and data fields of the packet.

##### Beam Refinement TRN-T field

The TRN-T field enables transmitter AWV training. The TRN-T field has the form:

| CE | T1 | T2 | T3 | T4 | CE | T5 | T6 | T7 | T8 | … |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Each subfield CE matches the Channel Estimation field that is transmitted in the packet preamble. The 4N fields T1 through T4N each consist of the sequence [Ga128 -Gb128 Ga128 Gb128 Ga128]. The sequences Ga128 and Gb128 are defined in Table 67 and Table 68, respectively, in subclause 21.9. The sequences are transmitted using rotated π/2-BPSK modulation. When transmitting the CE subfield, the transmitter shall use the same AWV as in the preamble and data fields of the packet. Any transmit signal transients that occur due to TX AWV configuration changes between subfields shall completely settle by the end of the first 64 samples of the subfield.

Editor’s instructions:  replace Table 74 in section 21.10.4 with the following text:

Table 74 – mmWave PHY Characteristics

| PHY Parameter | Value |
| --- | --- |
| aRIFSTime | 1usec |
| aSIFSTime | 3usec |
| aDataPreambleLength | 1745ns |
| aControlPHYPreambleLength | 3564ns |
| aSBIFSTime | 1usec |
| aAirPropagationTime | << 1usec |
| aMmWaveDetectionThres | -48 dBm |
| aBRPIFS | 40 usec |
| aSlotTime | 3usec |

# Text boxes

Abstract

Some additional text in supporting CID 487.