## Slide 1: Wide Band OBSS Friendly PSMP
Date: 2010, September 13
Authors:

## Slide 2: Abstract
PSMP is an optional low power scheduling mechanism for 11n
The proposal extends the PSMP in 11n to the wide band 11ac channel
The proposal introduces several OBSS friendly and capacity enhancement features.

## Slide 3: PSMP Background
Power Save Multi-Poll (PSMP) was introduced in 802.11n
  Provide a low power scheduling mechanism
  Use a duplicate non-HT (OFDM) waveform for 40MHz channel to set up protection period against legacy devices
  Provide (downlink and uplink) scheduling information in the PSMP frame
PSMP
PSMP-DTT
STA1
PSMP-DTT
STA2
PSMP-DTT
STA3
PSMP-UTT
STA1
PSMP-Downlink
PSMP-Uplink
AP
STA1
STA2
STA3
PSMP-UTT
STA2
PSMP-UTT
STA3

## Slide 4: PSMP Pros and Cons
Pros
  Allows maximum power saving of clients, especially in enterprise and hotspot environments
  Hotspot is growing more and more important as a use case, as operators seek to offload mobile phone data traffic to WiFi
  A good differentiator for AP vendors since the basic features have become commodities
  Client complexity is low; a basic implementation can simply extend the fixed SIFS response to programmable UTT
Cons
  AP complexity is significant, but not daunting, comparable to scheduling of TSpec and also can be considered as an extension of QoS capabilities
This proposal can takes advantage of PSMP support in 11n devices when available, but does not depend on it

## Slide 5: Motivation and Potential Issues for Wide Band PSMP
Wide band extension of PSMP in 11ac is desirable
  Allow high bandwidth and low power PSMP operation
  Natural transition for 11n PSMP implementation
  Support of low power operation becomes more important as more the mobile devices, such as smart phones, incorporate WiFi
Issues associated with wide band PSMP
  OBSS issues become more severe with wide band channel
  Not full BSS bandwidth will be used since 11ac BSS most likely will comprise 802.11n and 11ac STAs
It is desirable to use bandwidth more prudently in wide band PSMP, i.e., to make it more OBSS friendly

## Slide 6: Wide band PSMP Waveforms
Proposed wide band TGac extension of PSMP waveform is to replicate the “40MHz 11n PSMP waveform” in each 40MHz subchannel
Frequency
40MHz duplicate non-HT (OFDM) Waveform
80MHz PSMP Waveform
Frequency
160MHz PSMP Waveform
40MHz duplicate non-HT (OFDM) Waveform

## Slide 7: Proposed 11ac OBSS PSMP Features
Feature 1: Allow different sub-channels to have different (protection) lengths
  Release the unused duration to OBSS
Feature 2: Allow selected (instead of all) subchannel(s) to be used
  AP and STA transmit only using selected subchannel(s) based on traffic requirements and STA capability, not occupy the entire BSS bandwidth

## Slide 8: Higher OBSS Usage
8
Secondary
Subchannel
Primary
Subchannel
PSMP Frame
80 MHz Bursts
40 MHz Bursts
Duration for the Primary Subchannel
Duration for the Secondary Subchannel
Release Unused Duration
Tertiary
Subchannel
Quantenary
Subchannel
Release Unused Subchannels
BSS Channel Width
Feature 1 and 2 allow release of unused subchannels and unused duration for OBSS use

## Slide 9: Capacity Enhancement PSMP Feature
Feature 3: During PSMP, allows FDMref1 (Frequency Division Multiplexing) use of sub-channels
  While transmission to 11n device in the primary subchannel, also allows simultaneous transmission to 11ac STAs in the non-primary channels
  Allows simultaneous transmisson of multiple 11ac STAs signals in different subchannels
9
Secondary
Subchannel
Primary
Subchannel
PSMP Frame
40/80/120 MHz Bursts to 11ac
40 MHz Bursts to 11n and 11ac
Quarternary
Subchannel
Tertiary
Subchannel

## Slide 10: What Available for Signaling
NAV setting: Duration ID -> set up protection against legacy STAs
“PSMP Sequence Duration” subfield (10 bits) in the PSMP Parameter Set field -> allows indication of different durations for different subchannels
“Reserved” subfield (6 bits) in PSMP STA Info field -> allow subchannel selection on a per STA basis
Replicate the waveform only in selected subchannel(s)

## Slide 11: Summary
A wide band PSMP scheme which extends the 11n PSMP to 11ac is presented
A wide band PSMP waveform constructed from replicating the 40MHz PSMP waveform in each of the subchannel is introduced
Two OBSS friendly features promoting higher OBSS usage in the unused PSMP subchannel(s) and unused PSMP subchannel duration(s) are discussed
One capacity enhancing feature using FDM or OFDMA is discussed
Possible signaling methods are presented

## Slide 12: References
[1] 11-10-0317-01-00ac, Brian Hart, Cisco “DL-OFDMA for Mixed Clients”

## Slide 13: Strawpoll #1
Are you interested in extending 11n PSMP to wide band (>40MHz) 11ac channel as an optional feature in 11ac ?
  Yes:
  No:
  Abstain:

## Slide 14: Strawpoll #2
Are you interested in enhancing higher OBSS usage during PSMP using the proposed features (1 and 2) ?
  Yes:
  No:
  Abstain: