## Slide 1: PSMP-Based MU-MIMO Communications
Date: 2010, September 14
Authors:

## Slide 2: Abstract
A scheme to enable MU-MIMO in 11n devices is presented
Downlink stream padding and uplink scheduling in the MU-MIMO transmission can be replaced with PSMP scheduling
The proposed scheme does not require changes in current specification and 11n STAs and 11ac AP can “easily” include this feature

## Slide 3: Issues and Motivation
Co-existence with legacy 11n devices
  An 11ac BSS most likely will comprise 802.11n and 11ac STAs
  Performance of BSS is downgraded during transmission to 11n STAs
MU-MIMO (11ac) has advantages over SU-MIMO
  System capacity is determined by the complexity of AP
  High degree of spatial multiplexing (thus, high capacity) can be achieved with low cost clients
  Less immune to propagation limitations, works in LOS environment
Desirable to enable MU-MIMO transmission to 11n STAs

## Slide 4: Limitations with 11n STAs
Limitations of 11n STAs
  Scheduling:
    Downlink: not able to do padding (synchronize multiple spatial streams)
    Uplink: not able to perform scheduled or polled responses
  Only capable of receiving SU-MIMO transmission
Scheduling limitations in 11n can be overcome by the use of PSMP
Precoding at AP makes the MU-MIMO signal look like SU-MIMO signal to each receiving STA

## Slide 5: MU-MIMO to Legacy 11n Stations
Downlink MU-MIMO using pre-coding:
  AP transmits to STA11 while nulls to STA12 and transmits to STA12 while nulls to STA11
  AP transmits to STA21 while nulls to STA22 and transmits to STA22 while nulls to STA21
Scheduled uplink transmission from all STAs, no need to synchronize between STA’s
PSMP
PSMP-DTT
(STA11)
PSMP-DTT
(STA12)
PSMP-DTT
(STA21)
PSMP-DTT
(STA22)
PSMP-UTT
(STA11)
Downlink PSMP-Based MU-MIMO
Scheduled Uplink
AP
STA11
STA12
STA21
STA22
Channel Sounding to stations
PSMP-UTT
(STA12)
PSMP-UTT
(STA21)
PSMP-UTT
(STA22)

## Slide 6: Transmit Beam-Forming (Precoding)
Transmit beam-forming (precoding) is an optional feature for the SU-MIMO
Transmit beam-forming (precoding) is crucial to reduce the system complexity in a MU-MIMO system
In a MU-MIMO transmission, transmit beam-forming (precoding) allows
  minimizing or eliminating mutual interference among STA’s
  STA only deals with spatial stream(s) intended for itself
  STA antennas and processing are proportional to the number spatial streams intended for itself, not to the total number of spatial streams transmitted by AP
  Note w/o precoding at AP, the STA needs to have equal or more antennas than the number of the spatial streams transmitted by AP

## Slide 7: Other Desirable Features
No specification changes required
No change in 11n STAs required
11ac AP can incorporate the PSMP-based MU-MIMO capability “easily”
PSMP also supports low power operation mode

## Slide 8: Summary
A PSMP-based MU-MIMO communications to 11n STA’s is introduced
The proposed scheme resolves scheduling issues using PSMP
This approach enhances the system performance for 11ac BSS with mixed 11n and 11ac devices
It is expected that 11ac AP can incorporate such capability easily and no specification changes are required

## Slide 9: References
Reference 1: “Zero-Forcing Methods for Downlink Spatial Multiplexing in Multi-User MIMO Channels”, by Quentin H. Spencer, A. Lee Swindlehurst, Martin Haardt, May 2003
Reference 2:11-10-1054-00-00ac, “Wide band OBSS Friendly PSMP”, MediaTek

## Slide 10: PSMP Pros and Cons
Pros
  Allows maximum power saving of clients, especially in enterprise and hotspot environments
  Hotspot is growing more and more important as a use case, as operators seek to offload mobile phone data traffic to WiFi
  A good differentiator for AP vendors since the basic features have become commodities
  Client complexity is much less; a basic implementation can simply extend the fixed SIFS response to programmable UTT
Cons
  AP complexity is significant, but not daunting, comparable to scheduling of TSpec and also can be considered as an extension of QoS capabilities