## Slide 1: Phase Rotations for 80 MHz
Date: 2010-09-13
Authors:

## Slide 2: Abstract
In 10/0802r0, we proposed for 80 MHz, a VHT-LTF sequence and the phase rotations to be used in each 20 MHz sub-band
  The proposal minimizes the peak-to-average power ratio during VHT-LTFs
    Assuming pilot tracking during VHT-LTFs as suggested in [3]
Other contribution on this topic
  10/0791r1 discussed potential issues when using a phase rotation in the legacy section which is not [1 j] as seen by 11n 40 MHz devices
In subsequent motions in TGac, the following were adopted
  80 MHz VHT-LTF base sequence as specified in 10/0802r0
  [1 -1 -1 -1] as 80 MHz phase rotations for VHT section (starting VHT-STF)
This document attempts to converge on the phase rotation values, for the legacy section of the PPDU (upto VHT-SIG-A)
  Further discussions with authors of 10/0791r1 have led to a consensus on rotations in legacy section

## Slide 3: Re-using 80 MHz VHT phase rotations for legacy
  Rotation of [1 -1 -1 -1] (adopted for VHT section) gives 3~4 dB lower PAPR than without rotation ([1 1 1 1]) in the legacy portion
Keeping the phase rotations same across legacy and VHT portions of the PPDU simplifies transmitter design
No known 11n devices with compatibility issues
  Better to estimate channel including the phase rotation directly, and then combine using [1 1]
Phase Rotations per 20 MHz band | PAPR (2x oversampled) |  | 
 | L-STF | L-LTF | L-SIG
[c1 c2 c3 c4] = [1 1 1 1] | 8.1dB | 9.2dB | 12dB
[c1 c2 c3 c4] = [1 -1 -1 -1] | 4.3dB | 5.4dB | 9.4dB

## Slide 4: Strawpoll 1
Do you agree to re-use the phase rotations adopted for the VHT section of the 80 MHz PPDU for the 80 MHz legacy preamble, and VHT-SIG-A by adding the following text to the spec framework document ?
“In all elements of an 80 MHz VHT PPDU , i.e., the L-STF, L-LTF, L-SIG, VHT-SIG-A, VHT-LTFs, VHT-SIG-B and the Data, the following function of k shall be used to multiply subcarrier k, prior to transmission”
  Y
  N
  A

## Slide 5: References
[1] 10/0802r0, “VHT-LTF sequence for 80 MHz”
[2] 09/0992r11, “Proposed Specification Framework for Tgac”
[3] 10/0771r0, “Phase Tracking during VHT-LTF”
[4] 10/0795r0, “PAPR reduction of Legacy portion of VHT PLCP Preamble”
[5] 10/791r1, “Phase Rotation for the 80 MHz 802.11ac Mixed Mode Packet”