## Slide 1: Interleavers for 160MHz Transmission
Date: 2010-09-12
Authors:

## Slide 2: Specification Framework for Tgac [1]
Contiguous and non-contiguous 160 MHz channel width transmission and reception capability is optional [3].
Frequency interleaver defined for 80MHz transmission [2]
  For BCC encoding, NCOL = 26 for 80 MHz. NROT = 58 for 4 or fewer streams;
  The cyclic shifts applied on the different streams are given by [0 2 1 3]* NROT, identical to 11n.

## Slide 3: Facts on 160MHz Transmission
Interferences
  160MHz transmission increases the probability of experiencing interference from other OBSS for one or a few 20MHz sub-bands
    Different sub-bands may have different interferences
    In some cases, interference could only exist in one 80MHz band
Frequency Selectivity
  160MHz channel has more frequency selectivity than 80MHz
Interleavers for 160MHz transmission
  Improve robustness when interferences exist
  Harvest frequency selectivity more efficiently

## Slide 4: Candidate Interleaving Methods for 160MHz Transmission
Define New Frequency Bit Interleaver for 160MHz
  Given by Nrow, Ncol, and Nrot
  Not hardware friendly since 80MHz modules can not be re-used
Bit Parser after Stream Parser
  Simple
  What about performance?
Add a Tone Interleaver Between Two 80MHz Segments
  80MHz modules can still be re-used in 160MHz transmission
  Little changes on architecture
  Can be on top of any simple bit parser idea
  More flexible if other channel combining is required in the future

## Slide 5: Tone Interleaver Proposal
Requirements
  The index of DC tones, pilot tones and null tones must match the 11ac specification framework after interleaving
  The adjacent tones are mapped to far separated tones
  Interleaver crosses the whole OFDM symbol
Bit Reversal Tone Interleaver or Block Tone Interleaver
Description of Bit Reversal Tone Interleaver
  Convert the index k (k=0, 1, …, 511) into binary representation as
  The interleaved/de-interleaved index

## Slide 6: Transmit Architecture with Tone Interleaver
Introduces little modification
  Can be applied together with bit parser
Flexible
  If other sub-band combinations allowed in the future, fixed bit parser maybe not applicable

## Slide 7: Simulation Parameters
Bit Parser
  The stream parser output bits are allocated to two 80 MHz segments in an alternating fashion (IEEE 802.11-10-1063)
Tone Interleaver
  Bit-reversal interleaver
Simulation Scenario
  Using channel DNLOS with 10000 channel trials
  Applying bit interleaver as defined in [1] on each 80MHz segment
  Interferences from OBSS are only at one or two 20MHz sub-bands; with Interference-Over-Signal-Ratio in the particular sub-bands of -K dB.

## Slide 8: MCS 3
0.7 dB

## Slide 9: MCS 3 with Two 20MHz sub-channels have -12dB interference
2.8 dB

## Slide 10: MCS4

## Slide 11: MCS 4 with One 20MHz sub-channels has -16dB interference
2 dB

## Slide 12: MCS 6
1.6 dB

## Slide 13: MCS 6 with One 20MHz sub-channels has -24dB interference
3.2 dB

## Slide 14: Conclusions
Interleaver Across Two 80MHz Segments Can Significantly Improves Performance of 160MHz Transmission
  Harvest Frequency Selectivity
  Improve Robustness to Interference
Tone Interleaver Looks Desirable
  Little Change on Architecture and Implementation
  Improve Performance For Most MCS
  Decrease Error Floor When Sub-Band Interferences Exist

## Slide 15: Straw poll #1
Do you agree to further investigate interleaver and/or bit parser for 160MHz transmission?

## Slide 16: References
[1] Stacey, R. et al., Specification Framework for TGac, IEEE 802.11-09/0992r13, July 2010
[2] ac 80MHz Transmission Flow, 10/0548r2 11, May 2010
[3] Kim, Y. et al., 160 MHz Transmissions, 10/0774r0, July 2010