## Slide 1: Time-Domain CSI Compression Schemes for Explicit Beamforming in MU-MIMO
Sept. 2010
Slide 1
Slide 1
Date: 2010-9-14
Authors:

## Slide 2: Introduction
Sept. 2010
Downlink (DL) MU-MIMO will be adopted to improve the spectrum efficiency in TGac.
We have shown CSI report requirements for TGac in explicit feedback and in need of some CSI compression scheme to achieve higher MAC efficiency for MU-MIMO transmission [1].
In [2] and [3], time-domain CSI compression schemes were proposed to reduce the amount of CSI needed.
  [2] uses discrete cosine transform (DCT).
  [3] uses truncated inverse discrete Fourier transform (TiDFT).
In this submission, we present these CSI compression schemes and evaluate these performances.

## Slide 3: Concept of time-domain CSI feedback
Sept. 2010
Slide 3
Frequency-domain (FD) CSI-FB: CSI between a Tx antenna and a Rx antenna consists of Nsubc subcarrier components.
Time-domain (TD) CSI-FB: CSI consists of only Ng components since it is assumed that the actual channel impulse response is present only the GI duration.
Less CSI-FB needed with TD than with FD: factor is Ng/Nsubc.
freq.
Nsubc
time
Ng
Power
Power
Frequency-domain CSI
Time-domain CSI
TD/FD conversion

## Slide 4: CSI compression scheme using DCT [2]
Sept. 2010
Slide 4
Power
Freq.
Channel gain
Freq.
Freq.
Discontinuity
Inverse discrete Fourier transform (IDFT)
Discrete cosine transform (DCT)
Power
Time
DCT
IDFT
IDFT and DCT can create time-domain components.
In IDFT, the discontinuity at the band edges results in a spreading of energy in the impulse response since DFT assumes that the frequency response is periodic, which causes large CSI error.
In contrast, DCT can reduce the high-frequency components compared to DFT since it assumes mirror extension of the original data.
Continuity
Ng

## Slide 5: CSI compression scheme using TiDFT [3]
Sept. 2010
In IDFT, the discontinuity at the band edges results in a spreading of energy in the impulse response.
To overcome this problem, a truncated IDFT (TiDFT) matrix is applied: TiDFT matrix is the truncated SVD of pseudo-inverse matrix for IDFT.
TiDFT/FFT operation enables CSI compression since it can suppress CSI error due to discontinuity of the band edges.
(NsubcxNFFT)-DFT matrix
F
Pseudo-inverse matrix
Truncated SVD decomposition
TiDFT matrix

## Slide 6: Performance comparison of 3 CSI-FB schemes (1/2)
Sept. 2010
Slide 6
Nb=8bits
7bits
6bits
5bits
4bits
DCT
TiDFT
Conventional (FD)
Simulation parameters
Nb: Number of bits for each CSI coefficient
Channel model |  | Model E
Bandwidth |  | 40MHz
Number of FFT points N |  | 128
Number of subcarriers Nsubc |  | 114
Number of antennas at AP NT |  | 8
Number of antennas at STA NR |  | 1
DCT | Number of CSI-FB components for DCT LDCT | 32x2
 | Number of DCT points NDCT | 64
TiDFT | Number of CSI-FB components for TiDFT LTiDFT | 32
Note: CSI before compression is perfect CSI.
When CSI before compression includes the effect of noise, MSE performance of DCT and TiDFT will be 3dB and 6dB better than conventional FD respectively because of time domain smoothing.

## Slide 7: Performance comparison of 3 CSI-FB schemes (2/2)
Sept. 2010
Simulation parameters
Channel model |  | Model E
Bandwidth |  | 40MHz
Modulation |  | 64QAM
Coding rate |  | 5/6
Transmit beamforming |  | ZF
DCT | Number of CSI-FB components for DCT LDCT | 32x2
 | Number of DCT points NDCT | 64
TiDFT | Number of CSI-FB components for TiDFT LTiDFT | 32
DL MU-MIMO:
AP(8Tx) to 4 STAs(1Tx)
Note: “Ideal” means Perfect CSI.
The original CSI of three CSI-FB schemes is perfect CSI. The CSI error is due to quantization error and CSI compression operation. If original CSI includes the effect of noise, BER performance of time domain CSI-FB becomes much better than conventional scheme because of noise reduction by smoothing.

## Slide 8: Amount of FB information and calculation complexity
Sept. 2010
Slide 8
 | DCT | TiDFT
AP | 2NDCTlog2(NDCT) | NsubcxLTiDFT
STA | 2NDCTlog2(NDCT) | Nlog2N
FB information bits per STA
DCT | (3+2xNbxNTxNR)xLDCT
TiDFT | (3+2xNbxNTxNR)xLTiDFT
Conv. | (3+2xNbxNTxNR)xNsubc
Number of additional multiplications for TD conversion
Nb=6bits

## Slide 9: Effect of the number of CSI-FB coefficients
Sept. 2010
Slide 9
Channel model B (small delay spread)
Channel model E (large delay spread)
DCT
DCT
Nb=6bits
Nb=6bits
LDCT=32x2, 24x2, 16x2
LDCT=32x2
LDCT=24x2
LDCT=16x2

## Slide 10: Performance comparison of 3 CSI-FB schemes (2/2)
Sept. 2010
Channel model B
Nb = 6bits
Nb=6bits
When the delay spread is small, the amount of FB information can reduce by controlling the number of CSI-FB components L.
Note: When using optimization of TiDFT matrix, TiDFT can also reduce the number of FB information bits.

## Slide 11: Conclusion
Sept. 2010
Slide 11
We presented the performance evaluations for time-domain CSI-FB schemes to reduce the amount of FB information.
Time-domain approach can reduce FB information since the number of channel impulse response components fits within GI period.
  DCT reduces CSI-FB information by about half of the conventional one with some additional calculation.
  TiDFT is the most effective scheme of CSI compression although calculation complexity increases at STA.
The amount of FB information can be adjusted dynamically by controlling the number of CSI-FB components with the demand of CSI accuracy.
In addition, time-domain operation can improve the CSI estimation accuracy by reducing the noise on the estimated channel coefficients.

## Slide 12
Sept. 2010
K. Ishihara et al.,(NTT)
Slide 12
References
[1] K. Ishihara et al., CSI Report for Explicit Feedback Beamforming in Downlink MU-MIMO, IEEE 802.11-10/0332r0, Mar. 2010.
[2] K. Ishihara et al., CSI Feedback Scheme using DCT for Explicit Beamforming, IEEE 802.11-10/0806r1, July 2010.
[3] L. Cariou and M. Diallo, Time Domain CSI report for explicit feedback, IEEE 802.11-10/0586r1, May 2010.